## Slide 1
Diagnostics, Repair, & Calibration
This material is based on work supported by the National Science Foundation Grant DUE #2054997; any opinions, findings, conclusions, or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation
DUE #2054997

## Slide 2
ADAS Networks
This material is based on work supported by the National Science Foundation Grant DUE #2054997; any opinions, findings, conclusions, or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation
DUE #2054997

## Slide 3
Network Systems
Network Systems Offer Many Advantages Over “Hard Wiring” Components Together
Network systems substantially lower the amount of wiring in a vehicle, sometimes eliminating a harness of 50 wires and replacing it with 3 wires.

## Slide 4
With networking, the speed signal would first go to one module, the Engine module and then be sent out over either a 1 wire network or a 2-wire network to be shared with every module.
This eliminates the need for several different wiring harnesses.
Network Systems

## Slide 5
TCOE – What it is NOT
An NSF Center
A large agency (only 4 full-time staff)
The only Center of Excellence in the State
Academic programing or enrollments
Chris

## Slide 6
Network Systems
Single Wire Network
CAN BUS 2-Wire Network
Networks Can Be Either a Single Wire or 2-WIre Networks

## Slide 7
Overview of ISA-TOPE Grant
What we heard from employers and why we started this project.
Multiple listening sessions
What we heard
  Graduates need to be well trained in electrical theory and electrical diagnosis
  Incoming students are interested in new technology
  Emerging technologies can be a “hook” for students to consider a transportation pathway
  Autonomous technology is an emerging technology in diesel truck/equipment technician and driver/operator programs
  Autonomous technology can be a method in teaching electrical theory and diagnostic techniques
  New technology is expensive
  Colleges can’t afford additional expenses – some are struggling to keep the doors open
Carl

## Slide 8
CAN BUS
Controller Area Network (CAN) Protocol first Invented by Bosch in 1986
First Used in Automobiles in 1992
Now used by Cars, Trucks, Drones, Heavy Equipment, Boats, Motorcycles, and many other applications.
Allows many modules to be connected via the “Twisted Wires”.
Some Vehicles can have more than 70 modules connected together talking to each other on 1 network.
Allows for super fast communications between modules
2- Wire High Speed Networks Used In Vehicles are Called CAN BUS Networks.

## Slide 9
Overview of ISA-TOPE Grant
What the grant does and how the project works
What we are doing
    Buying autonomous technology in the heavy truck and construction arena to be shared with colleges around the state
    Curating OEM approved professional development related to autonomous technology specific to items purchased
    Creating OER for use in the classroom when teaching about autonomous technologies
  Leveraging our existing “Can I Borrow That?” program (https://www.minntran.org/can-i-borrow-that/)
  Communicate about the program through existing channels (Sector Meetings, Newsletter, ASE, AED, etc.) along with new resources (NCAT, CAAT, ATE Connect, etc.)
Chris

## Slide 10
Overview of How CAN BUS Works
https://www.youtube.com/watch?v=FqLDpHsxvf8

## Slide 11
Chris

## Slide 12
Binary Language
Modules communicate with each other using Binary Language
Binary language is very simple: It is full of 1’s and 0’s
A “1” means that the “Bit” of information has power turned on
A “0” means that the “Bit” of information has the power turned off
A group of 1’s and 0’s creates a Byte of information
A 500kb/second means that 500,000 of these “bits” is moving through the network
The very first Binary Language was Morse Code with on and off signals that would be sent via telegraph.

## Slide 13
Challenges Faced
What roadblocks were faced and how they were navigated.
Asked to start grant earlier than anticipated
Pandemic
Severe Supply Chain Issues
Distractions (changing commitments of staff)
Detractors (not everyone is going to be on board with the project – even consortiums have these challenges)
Internal Hurdles (Business Office)
Chris

## Slide 14
Lessons Learned
What could be done differently by others wishing to duplicate the project.
    Expect things to take longer than expected
    Seek mentorship
    Be a mentor to others
    Be patient
    Do what you can when you can
    Stay focused
    Continue to communicate your plans
    Listen to feedback
    Adapt
    Ask for help
    Utilize existing resources – and find new ones
Shannon/Forrest

## Slide 15
Binary Language
As one can see, the on and off of the binary language is how a module on a network communicates with other modules.
Most CAN BUS networks use a 5 volt reference with a 2.5 volt bias
CAN BUS uses a High and a Low. One always mirrors the other to produce a “fail safe” signal if one were to fail

## Slide 16
CAN BUS Wiring
CAN BUS wiring is “twisted and shielded to reduce the possibility of interference.
RFI (radio Frequency Interference) can cause noise if the wiring is not twisted and shielded.
Shielding Protects the Twisted Wires against Outside Radio Frequency Waves (Called RFI). Shielding needs to be grounded on both ends.
If the ground is damaged on the shielding, it will pick up RFI like a vehicle's antenna, so it is important that grounds on shield wiring are intact.

## Slide 17
Q&A Session
A chance for attendees to ask specific questions about the project or how it may apply to something they are doing in their project or possible future projects.
In the last 2 years, what has been your experiences with obtaining high tech, expensive, and employer requested equipment for your program?
Do you have any employer partnerships that already help you get access to high tech, expensive, equipment? Has that changed in the last few years with the recent supply chain issues? Is it going to always be there the same as it is now?
How would you be able to create a consortium or collaboration in your state/region to acquire high tech, expensive, employer-requested equipment? What are the roadblocks? Who are the people to connect with?
Chris

## Slide 18
CAN BUS Network
Trucks use the J1939 connector.
This is the standard CAN BUS protocol for the heavy truck and heavy equipment industry.
The diagnostic pins for network communication are all located in the same place for all makes and models.
Trucks and heavy equipment may have several other networks in addition to the J1939 network.
Pins C and D are used for the J1939 network. This is standardized.

## Slide 19
Carl Borleis
Director of Program Excellence, TCOE
PI, ISA-TOPE
651-423-8577
carl.borleis@dctc.edu
Chris Hadfield, Ed.M.
Executive Director, TCOE
Co-PI, National Center for Autonomous Technologies (NCAT)
Co-PI, ISA-TOPE
651-423-8311
Chris.hadfield@dctc.edu
Get
Forrest Brownlee
Diesel Technology Instructor, Minnesota North - Hibbing
MTTIA Board of Directors
SME, ISA-TOPE
218-293-6862
forrest.brownlee@minnesotanorth.edu
ISA-TOPE.ORG
Shannon Mohn
Automotive Instructor, M-State
MTTIA Training Coordinator
Co-PI, ISA-TOPE
218-299-6563
Shannon.mohn@minnesota.edu
in
touch.

## Slide 20
Transfers data at 250kb/s on older models and at 500kb/s on newer models.
Packets of data travel over the network and can be read by all modules.
Modules are connected to the network via 2 wires in the network. Each module has its own power and ground but exchange information on the network.
On each end of the network are 2–120-ohm resisters. These resisters are referred to as “Terminating Resisters”
Networks with a 500kb/s transfer rate or higher are called "High Speed" Networks.
J1939 Network

## Slide 21
Terminating Resisters
On each side of the CAN Bus Network, connecting the high and low circuits are 2, 120 ohm terminating resisters. These resisters absorb any residual voltage allowing for a "clean" signal. These resisters can be located independently in the circuit, or in a module. The sum of these 2 resisters should give you 60 ohms of resistance. Any other reading you get will indicate a problem in the circuit. It is important to know where these resisters are to service the system. Service information should give you these locations.

## Slide 22
Terminating Resisters

## Slide 23
Data Packets
CAN BUS uses both a High voltage line and a low Voltage Line.
The High Voltage line toggles between a low of 2.5 volts and a high of 3.5 volts.
The Low voltage line toggles between 1.5 volts and a high of 2.5 volts.
The high side should ALWAYS be an exact opposite mirror image of the low side.
Both the high and low sides of the CAN BUS network should have a voltage right around 2.5 volts measured with a multi-meter with no traffic on the line.

## Slide 24
Data Packets
Because every module sees every message that is traveling on the BUS line, the first part of the message “identifies” which module(s) the message is intended for.
That is the 29 bit identifier
Every message contains this identifier and if it does not match what the module is looking for, it will disregard the message.
Breaking Down the Data Packet

## Slide 25
Data Packets
The second part of the message is the 64 bit data field.
This tells the modules what is the important data ie. “Engine Speed”, “Transmission Temperature”, ect…….
Breaking Down the Data Packet

## Slide 26
Data Packets
The Next Part Repeats and Rechecks the Information
The Last Part of the Message Tells the Modules That the Message is Ending.
Breaking Down the Data Packet

## Slide 27
Network Testing
Testing the Network is Actually Quite Easily Done
A Number of Quick Diagnostic Tests Will Help Quickly Determine if the Problem is Network Related or Just Related to that Module.
Every Module Needs Power, Ground, and Network Connections to Talk on the CAN Bus Network.
Relax!

## Slide 28
Network Testing
The First Step is to do a Network Test Using the Scan Tool
When Hooking Up the Factory Freightliner Scan Tool, This is the First Thing that Will Happen.
The Lower Left Will Highlight All of the Modules that the Scan Tool "Pinged" and Which Ones Responded Back. If the Modules Light Up in Green, the Module Responded and is Sending Data.
If the Module is NOT Lit Up in Green, Then Proceed to the Next Step and See If the Network is Functioning.

## Slide 29
Network Testing
Note the Network Test on the Lower Left of the Screen and How the Modules Light Up in Green Showing the J1939 High Speed Network.

## Slide 30
Network Testing​
Once You Have Performed a Network Test and Tested the Integrity of the Network, All That is Left is to Hook Up a Scope. Set Scope to 50 us/div on the 5 Volt Scale and Use Both Channels A and B.
This is a Great Tool if You Have 1 Module Taking Down the Network.
You Can Unplug Each Module and See Which Module is Bad.

## Slide 31
Network Testing​
If the Network "Comes Back to Life" After a Module is Disconnected, That is the Module That is Shorted.
You Can Also Use This Same Method if the Terminating Resistance is Above or Below Specifications. You Will Just Need to Have Information on Which Modules Contain the Resisters.

## Slide 32
Network Testing​
If the Network "Comes Back to Life" After a Module is Disconnected, That is the Module That is Shorted.
You Can Also Use This Same Method if the Terminating Resistance is Above or Below Specifications. You Will Just Need to Have Information on Which Modules Contain the Resisters.

## Slide 33
References Used:​
(https://www.csselectronics.com/products/terminal-resistor-can-bus) accessed 06/01/2023
(https://www.pngegg.com/en/search?q=shielded+Twisted+Pair) accessed 06/01/2023
(https://static.nhtsa.gov/odi/tsbs/2018/MC-10161073-9999.pdf) accessed 06/01/2023

## Slide 34
References Used:​
Slide #3​ - (https://rennlist.com/forums/944-turbo-and-turbo-s-forum/309056-how-to-read-wiring-diagrams-no-start-post-42-a-3.html) accessed 06/01/2023
Slide #6 - (https://www.mdpi.com/1424-8220/22/18/6901) accessed 06/01/2023
Slide #6 - (https://www.robotsforroboticists.com/can-bus/) accessed 06/01/2023
Slide #8 - (https://www.youtube.com/watch?v=FqLDpHsxvf8) accessed 06/01/2023
Slide #