## Slide 1
Cat WAVS
2D trimble
This material is based on work supported by the National Science Foundation Grant DUE #2054997; any opinions, findings, conclusions, or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation
DUE #2054997

## Slide 2
Agenda
Introductions
Overview of WAVS
Overview of 2D system
Carl

## Slide 3
WAVS
Work
Area
Vision
Systems
Carl

## Slide 4
The system consists of a dedicated
20.3 cm(8.00 inch)display and up to four cameras. The WAVS enhances an operators awareness of the site surroundings, work tool activities, and changes in work area conditions increasing safety and productivity. The customer can select precisely the WAVS options the customer needs, based on equipment size, work site environment, and application.

## Slide 5
2 Day/night mode
3 Brightness Adjustment
4 Reverence lines Menu
5 Manual camera toggle
6 Menu

## Slide 6
Day/Night Mode (2)- Provides the capability to toggle between a bright screen and a dim screen, depending on ambient light conditions.
Brightness Adjustment
(3)- Allows for the adjustment of the screen brightness. Reference Lines Menu
(4)- Allows the ability to set horizontal and vertical reference lines on the screen. The reference lines provide a fixed distance reference line from the machine. Manual Camera Toggle
(5) - Provides the capability to toggle manually between cameras, if the machine is installed. The numbers displayed below the camera on the manual camera toggle icon button, is the number of cameras currently detected on the machine. The number displayed is subject to change depending on the detected cameras.
Menu (6)-This icon provides access to two options: Display option and Service option.

## Slide 7
2d Trimble system
Laser System
Laser Receivers provide the elevation
Laser receivers require a laser to be mounted somewhere, most commonly on a tripod.
(For Dual Laser) When both of the receivers are benched on the laser plane they form a constant slope.

## Slide 9: 2D and Laser Systems​
The cross slope is either determined by an angle sensor or by adding a second laser receiver to the blade​
  When both of the receivers are locked on to the laser plane they form a constant slope between them allowing the blade to cut the desired slope. ​
Laser receivers require a laser to mounted somewhere on a tripod for stability. This is the simplest form of infrastructure and provides the most precise vertical control. ​
​

## Slide 10: Insert cat info need do tone down control information saved on drive

## Slide 12
Carl Borleis
Director of Program Excellence, TCOE
PI, ISA-TOPE
651-423-8577
carl.borleis@dctc.edu
Chris Hadfield, Ed.M.
Executive Director, TCOE
Co-PI, National Center for Autonomous Technologies (NCAT)
Co-PI, ISA-TOPE
651-423-8311
Chris.hadfield@dctc.edu
Get
Forrest Brownlee
Diesel Technology Instructor, Minnesota North - Hibbing
MTTIA Board of Directors
SME, ISA-TOPE
218-293-6862
forrest.brownlee@minnesotanorth.edu
ISA-TOPE.ORG
Shannon Mohn
Automotive Instructor, M-State
MTTIA Training Coordinator
Co-PI, ISA-TOPE
218-299-6563
Shannon.mohn@minnesota.edu
in
touch.