## Slide 1
Components to Understand
This material is based on work supported by the National Science Foundation Grant DUE #2054997; any opinions, findings, conclusions, or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation
DUE #2054997

## Slide 2
Covered topics in this section
1. Left joystick controls.
2. Right Joystick controls
3. Auxiliary controls
4. 2D system

## Slide 3: Left joystick
Functions
Forward travel
Backwards travel
Right turn
Left turn
Horn
Two speed control
Creep control
Aux 5-7

## Slide 8: Right joystick
Functions
Lower
Dump
Raise
Tilt back
Float
Aux 1-4

## Slide 11: Auxiliary Controls

## Slide 12
(E) Work Tool Electrical Connector (J) 1/2 inch Hydraulic Supply (L) 3/8 inch Case Drain (K) 1/2 inch Hydraulic Return

## Slide 14
Typical electrical connection on the loading arm (A) Left-Hand Trigger Control “AUX 7” (C) C- Control (D) C+ Control (E) C2 Control (F) C1 Control (J) Auxiliary Electrical Control “AUX 8” (P) +12V with KEY ON

## Slide 15
Auxiliary Hydraulic Control (A1) - This control provides hydraulic oil flow to the auxiliary connections on the loader arm. Engage the control to provide hydraulic oil flow to the female connectors (A1) and (a1)

## Slide 16
Auxiliary Hydraulic Control (A2) - This control provides hydraulic oil flow to the auxiliary connections on the loader arm. Engage the control to provide hydraulic oil flow to the male connectors (A2) and (a2).

## Slide 17
Auxiliary Electrical Control 3 (C−) - This control provides electrical power to activate additional work tool functions using a three-position diverter valve that is on some work tools. Press the switch and hold the switch to send power to the pin (C) this action will activate the required Work Tool function. Release the switch to deactivate the control. If auxiliary hydraulic controls (A1/A2), and continuous flow is inactive, and a work tool featuring auto reverse functionality (such as cold planers) is connected, pressing the switch will send power to pin (C) and provide hydraulic flow to the female connectors (A1) and (a1).

## Slide 18
Auxiliary Electrical Control 4 (C+) - This control provides electrical power to activate additional work tool functions using a three-position diverter valve that is on some work tools. Press the switch and hold the switch to send power to the pin (D). This action will activate the required Work Tool function. Release the switch to deactivate the control. If auxiliary hydraulic controls (A1/A2), and continuous flow is inactive and a work tool featuring auto reverse functionality (such as cold planers) is connected, pressing the switch will send power to pin (D) and provide hydraulic flow to the female connectors (A1) and (a1).

## Slide 19
Auxiliary Electrical Control 5 (C2) - This control provides electrical power to activate additional work tool functions using a three-position diverter valve that is on some work tools. Press the switch and hold the switch to send power to the pin (E) this will activate the required Work Tool function. Release the switch to deactivate the control.

## Slide 20
Auxiliary Electrical Control (C1) - This control provides electrical power to activate additional work tool functions using a three-position diverter valve that is on some work tools. Press the switch and hold the switch to send power to pin (F). This action will activate the required Work Tool function. Release the switch to deactivate the control.

## Slide 21
Left-Hand Trigger - Pull the trigger and hold the trigger on the left-hand joystick to provide electrical power to pin (A). Release the trigger to deactivate the control.

## Slide 23: 2D (Reference Elevation)     Sensor Based (Cross Slope/Depth and Slope)     Laser (Single or Dual)

## Slide 24: Types of 2D systems
Cross Slope
Use of sensors to determine slope
Mostly found on graders but also found on small dozers and compact machines
Types of sensors are Angle Sensors/IMU’s (AS400, GS520) and Rotation Sensors (RS400)
Laser Systems
Laser Receivers provide the elevation
Laser receivers require a laser to be mounted somewhere, most commonly on a tripod.
(For Dual Laser) When both of the receivers are benched on the laser plane they form a constant slope.

## Slide 25: 2D and Laser Systems
2D refers to elevation and slope
  Laser Receivers provide the elevation on HEX, TTT, MG and Compact Loaders that are set up and configured to use them.

## Slide 26: 2D Lazer system
The cross slope is either determined by an angle sensor or by adding a second laser receiver to the blade
  When both of the receivers are locked on to the laser plane they form a constant slope between them allowing the blade to cut the desired slope.
  Laser receivers require a laser to mounted somewhere on a tripod for stability. This is the simplest form of infrastructure and provides the most precise vertical control.

## Slide 27
Carl Borleis
Director of Program Excellence, TCOE
PI, ISA-TOPE
651-423-8577
carl.borleis@dctc.edu
Chris Hadfield, Ed.M.
Executive Director, TCOE
Co-PI, National Center for Autonomous Technologies (NCAT)
Co-PI, ISA-TOPE
651-423-8311
Chris.hadfield@dctc.edu
Get
Forrest Brownlee
Diesel Technology Instructor, Minnesota North - Hibbing
MTTIA Board of Directors
SME, ISA-TOPE
218-293-6862
Forrest.brownlee@minnesotanorth.edu
ISA-TOPE.ORG
Shannon Mohn
Automotive Instructor, M-State
MTTIA Training Coordinator
Co-PI, ISA-TOPE
218-299-6563
Shannon.mohn@minnesota.edu
in
touch.