## Slide 1: DIGITAL SCALE
Taylor Model 7519

## Slide 2: Components
Control Board
Back of LCD Display
Load Cell under foot
Battery Holder

## Slide 3: Control Board
Electrolytic Capacitors
Mode Switch
Control Logic
Surface Mount Components
Strain Gauge Connections

## Slide 4: LCD Display
7-Segment Numeral
e d c
f a b
g (segment is off)

## Slide 5: Load Cell
Foot Covering Load Cell
Load Cell Uncovered

## Slide 6: Load Cell
Metal Frame
Strain Gauge (under epoxy)

## Slide 7: SEN-10245 50kg Load Cell Specifications
Capacity kg 40-50 Comprehensive Error mv/v 0.05 Output Sensitivity mv/v 1.0±0.1 Nonlinearity %FS 0.03 Repeatability %FS 0.03 Hysteresis %FS 0.03 Creep (3min)%FS 0.03 Zero Drift (1min)%FS 0.03 Temp. Effect on Zero %FS/10℃ 1 Temp. Effect on | Output %FS/10℃ 0.05 Zero Output mV/V ±0.1 Input Resistance Ω 1000±20 Output Resistance Ω 1000±20 Insulation Resistance MΩ ≥5000 Excitation Voltage V ≤10 Operation Temp. Range ℃ 0--+50 Overload Capacity %FS 150

## Slide 8: Strain Gauge
Sample Strain Gauges
Flexible Resistive Material
Resistance of Material Changes when Stressed