## Slide 1
The webinar will begin at 1 PM Eastern time
ASU’s Compact X-ray Laser Project
Capturing Movies of Molecules Using Ultrafast X-rays

## Slide 2: This Webinar Is Hosted By
ATE Central acts as an information Hub for the National Science Foundation ATE Grantee Community
atecentral.net/webinars

## Slide 3: This Webinar Is Brought To You By
Nanotechnology Collaborative Infrastructure Southwest (NCI-Southwest) at Arizona State University
And
The NACK Network at Penn State University

## Slide 4
Mike
Lesiecki
William Graves
Associate Professor, Arizona State University
Trevor Thornton Professor, Director NCI-SW
Introductions

## Slide 5
Wilhelm Röntgen awarded the first Nobel prize in physics in 1901 for the discovery of x-rays

## Slide 6
Lawrence and William Bragg awarded the 1915 Nobel prize in physics for the discovery of crystal structure by x-ray diffraction

## Slide 7
Spatial Scales
Temporal Scales
X-rays probe a vast range of spatial and temporal scales

## Slide 8
X-ray tube from 1917
X-ray tube today
Flux of 5 X 109 photons/sec
Brilliance* of 109
Factor of ~100 better than 100 years ago
X-ray flux of 107 photons/sec from source of few mm2 and large opening angle
From Roentgen’s tube to today’s best laboratory-scale sources
*Brilliance is in units
photons/(sec mm2 mrad2 0.1%)
Tubes are primitive low energy (0.1 MeV) electron accelerators

## Slide 9
Particle accelerators in the 20th century
Advanced Photon Source near Chicago
About 1 mile in circumference and $1 billion in cost

## Slide 10
ASU Compact X-ray Light Source (CXLS)
21st century tech: 20 ft long
Linac Coherent Light Source (LCLS): 2 miles long!
ASU X-ray Light Source

## Slide 11
Magnetic undulators in big machines
X-ray radiation
Laser field
Electron beam
Laser replaces undulator
Laser wavelength is 10,000X shorter than undulator period
Electron energy is 100X lower for same x-rays
Facility size and cost is 100X lower ($1B -> $10M)
How to make a compact x-ray source?
Using state-of-the-art laser and accelerator technology we can shrink the size and cost 100X.

## Slide 12
The Biodesign Institute at ASU

## Slide 13
Movies of Molecules in Motion
Courtesy of physics.org

## Slide 14
Photosystem 1
(key to photosynthesis)
Lysozyme
enzyme
Complex molecular structures from x-ray diffraction
X-ray diffraction studies can solve very complex molecular structures

## Slide 15
Kirk Clark
Novartis Institutes for Biomedical Research
Structural Biology important to drug discovery programs
Insight into protein function
Facilitate expanding structural biology to integral membrane proteins.
Drug Discovery

## Slide 16
Courtesy of F. Pfeiffer, TU-Munich
Phase Contrast Medical Imaging
The very bright and monochromatic x-ray beam allows a new type of much more powerful medical imaging at lower dose to the patient.
Soft tissue structures such as this liver cancer become visible
ASU is working with the Mayo Clinic and Harvard to develop this method

## Slide 17
Phase Contrast X-ray
MRI Image
Cross-section of a person’s wrist

## Slide 18
Microscopy of Carbonate Reservoirs
Courtesy of Theis Solling, Maersk Oil

## Slide 19
-Philippe Walter - director
Objectives: Research, expertise and support for curators and conservators
Cultural Studies - Louvre
Notes: 19

## Slide 20
X-rays show us the invisible

## Slide 21
Coherent x-rays require coherent electron bunching
Random electron spacing
Undulator radiation with GeV electrons or
Inverse Compton Scattering with MeV electrons
Coherent spacing
XFEL radiation (GeV electrons) or
Coherent ICS, compact CXFEL (MeV electrons)
lx
bc
lx

## Slide 22
Low magnification image showing 50 micron square grid pattern with 400 nm period. Membrane is 200 nm thick
(Norcada supplied)
TEM Diffraction Through Patterned Membrane
Diffraction pattern of grid with beam block
Pinhole inserted allowing single Bragg spot through
Resulting electron density nanopattern at image plane

## Slide 23
FEL bunching factor
Experimental data: Nanopatterned electron beam generated by diffraction
Nanopatterned Electron beams for Compact XFEL
Harmonics

## Slide 24
CXFEL Estimated Performance
ASU CXFEL
The ASU CXFEL uniquely controls the x-ray phase and amplitude
Multiple-color, tunable time delays
CXFEL can seed large XFELs to increase their brilliance X100

## Slide 25
Thank you!