## Slide 1: Motion SensinG Light Teardown

## Slide 2: Wiring
Power to circuit board
Ground
Positive
Neutral
We opened the back end of the fixture to expose the AC wiring.

## Slide 3: Close up view of wiring

## Slide 4: Adding manual toggle switch
On/Off switch
Positive
Neutral
Ground
For our experimentation purposes we broke out the wiring in order to measure voltage and current.

## Slide 5: Positive, neutral and ground wiring for lights
Power to circuit board
Added wiring from power supply on back of circuit board to manual toggle switch
120V, 60Hz, 4.2A UL listing
Neutral to lights
Positive to lights
This is the sensor circuit board.

## Slide 6: FRONT of Circuit board
Photo resistor
Controller
Infrared motion sensor
Relay
Capacitors
Wiring added to power supply for on/off toggle
Timer circuitry
Infrared light impinges the sensor through a diffuser lens. Changes are interpreted as motion.

## Slide 7: Measuring voltage and current on cfl
Manual toggle in off position
Manual toggle on position
14W - .23A (listed on bulb)
116.5 volts
232 mA current
With our breakout box we can measure differences between incandescent, CFL and LED bulb performance.