## Slide 1: Plane Geometry and Solid Figures (Part 1)
- This material is based on work supported by the National Science Foundation under Grant No. DUE-1406857. Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author(s) and do not necessarily reflect the views of the National Science Foundation.
- This work is licensed under the Creative Commons Attribution 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by/4.0/.
- For answer keys and additional resources about this activity, go to www.nwtc.edu/mathnsf and submit the form for more information.

## Slide 2
Objectives
Angle Definitions
Polygons
Calculating Perimeter and Area for Quadrilaterals
Pythagorean Theorem
Area of a Triangle
  Height Known
  Isosceles Triangle
  Equilateral Triangle
Regular Hexagons
Area of Irregular Polygons
Circles – Circumference and Area
Irregular Shapes with Circles
Length of Stock

## Slide 3: Angle Definitions
Angle – how we measure the amount of the opening between the two lines
  The basic unit we attach to an angle is degrees (°)
  We also use minutes (´) and seconds (´´) to break down degrees more accurately in Trigonometry
  Vertex – where two lines meet and form an angle
Basic Angles
  A full circle is ______ °.
  A straight line is _____ °.
  A perfect vertical line and horizontal line makes a ____ ° angle.
Types of Angles
  Acute – the angle is between 0° and 90°
  Right – the angle is exactly 90°
  Obtuse – the angle is between 90° and 180°
Angles of a triangle – add up to _____°

## Slide 4: Angle Definitions
Example: Find the missing angle:
Example: A bolt hole circle has eight circles. How far apart are the holes, in degrees?
35°
35°

## Slide 5: Angle Relationships
Vertical angles – the opposite angles of two intersecting lines
  The two vertical angles formed are always equal
Example: Find angles m, n, and p
25˚
p
n
m

## Slide 6: Angle Relationships
Parallel Lines – two lines that never cross
Transversal – a line that crosses two parallel lines
  The corresponding angles formed are equal
Example: Fill in all missing angles
55˚

## Slide 7: Try Yourself
Find the missing angles
1)
2) The vertical and horizontal lines are perpendicular
40°
10°
B
25°
C

## Slide 8: Polygons
Polygon – a shape with at least three straight sides
The different things that we calculate for two-dimensional polygons are
  Perimeter
  Area
  What does it mean to calculate each of these? Give examples of when you would do each.
See the formula sheet to look at the different shapes we will calculate Perimeter, Area, Surface Area, and Volume for.

## Slide 9: Rectangles
Example: Find the perimeter and area
8.5 in
94 in

## Slide 10: Rectangles
The rectangle above is a 10 gauge, low carbon commercial steel sheet. Go to http://www.ryerson.com/en/Products/Stock-List to determine that the weight per square foot in lbs is 5.625 lbs/sq ft and then determine the weight of the sheet.

## Slide 11: Try Yourself
Example: Find the perimeter (in ft and in) and area (in square feet).
4ft,2in
3 in

## Slide 12: Try Yourself
Example: You want to pave your driveway that is currently gravel. One company tells you that they charge $45/square yard. Your driveway is sixty feet long and fifteen feet wide. What would the cost be?

## Slide 13: Trapezoid
Example: Find the perimeter and area
3 ft
2.75 ft
3 ft
4.25 ft
2.5 ft

## Slide 14: Try Yourself - Parallelogram
See Formula Sheet
Example: Find the perimeter and area
25”
12”
30”

## Slide 15: Pythagorean Theorem
Used to find the third side of a right triangle if we know two of the sides.
Notice that c must be the hypotenuse.
Pythagorean Theorem: a2 + b2 = c2
Example: Find the missing side
12
4”

## Slide 16: Pythagorean Theorem
Example: Find the missing dimension to the nearest 16th of an inch
8
4

## Slide 17: Try Yourself
Example: Find the missing side
16
5

## Slide 18: Try Yourself
The following cross brace needs to be made. Find the total length of bar needed to make this piece.
14.875”

## Slide 19: Area of a Triangle – Height Known
Example: Find the perimeter and area
7 in
13 in
9 in
11 in

## Slide 20: Area of a Triangle – Isosceles Triangle
Isosceles Triangle – two sides are equal
Example: Find the perimeter and area
6 ft
6 ft
2 ft

## Slide 21: Area of a Triangle – Equilateral Triangle
Equilateral Triangle – all three sides are equal
Example: Find the perimeter and area

## Slide 22: Try Yourself
Find the total length of weld needed to go around the sheet of metal. Also calculate the area
65 mm
65 mm
20 mm

## Slide 23: Try Yourself
The supports under a bridge are shown below. If the sheets weigh 14.8 lb/sq ft, how much does each piece weigh?
5’ 3”
1’ 6”

## Slide 24: Regular Hexagons
Regular Hexagon – a polygon with six equal sides
  a is the length of a side
  d is the distance from opposite corners
  f is the shortest distance across opposite sides
a
f
d

## Slide 25: Regular Hexagons
Example: Find the side of the hexagon and find the area
5 in

## Slide 26: Try Yourself
Example: You are asked to make a road sign in the shape of a regular hexagon. They should have a maximum width of 2 ft 3 in. Find the length of each side and find the area of the sign.

## Slide 27: Irregular Polygons
Find the area of the sheet of metal.
25 mm
12 mm
20 mm
12 mm

## Slide 28: Irregular Polygons
Find the area of the shaded part:
Compare the two different strategies used to calculate the area of these shapes.
4”
4”
1.5”

## Slide 29: Application Problem
The following figure needs to be cut from an originally rectangular sheet of metal that is by Determine the original area and the area once the triangular parts have been cut and removed.

## Slide 30
4.5625
5.8125
3.75
4.75
3.25
6.3915
9.921
6.5

## Slide 31: Try Yourself
Determine the perimeter and area of the following sheet of metal in order to determine costs of materials related to the job.

## Slide 32: Try Yourself
Find the perimeter and area of the figure below.
2.875
16.625
3.9375
2
4.8750
6.0000
2.125
3.5000
6.0000

## Slide 33: Circles
Find the π button on your calculator. What is π?
Examples: Convert to the decimal form to the nearest thousandth:
  π =
  2π =
  0.57π =
Circles: r is the radius, d is the diameter
  Area: A = πr2
  Circumference (Perimeter): C = πd = 2πr

## Slide 34: Circles
  Example: Find the area and circumference for a circle with a diameter of 5 in.
  Example: Find the area of the shaded part of the circle:
3.5”
6.75”

## Slide 35: Try Yourself
Find the area and circumference of the circle:

## Slide 36: Irregular Shapes with Circles
Find the area and perimeter of the figure with the semicircles removed from a rectangular sheet of metal.
R3.75
R5.00
9.00
R1.50
R2.00
18.00

## Slide 37: Try Yourself
Find the area of the shaded figure: (∅ is diameter)
6.4375
∅5.00
R0.75
14.00
∅3.50

## Slide 38: Length of Stock
Measure from the middle of the piece. This gives the mean(average) diameter or mean radius.
Example: Find the original length of stock needed to have bend a ½” diameter round stock to have an inner diameter of 6” and bent 180°.

## Slide 39: Try Yourself
Find the length of stock in the figure below, including the vertical and horizontal parts at the ends:
2.00
R4.00
2.00
.125