## Slide 1: 4th Axis Lecture 4
Tailstocks and lead angles

## Slide 2: Tailstocks with a 4th Axis Set-up
A tailstock can be used for support long projects using a 4th axis
must be set-up on the same centerline as the 4th axis rotary
should be set-up so the quill has the minimal amount of stroke needed for the job
  The longer the quill is extended, the less rigidity the set-up will have
Photo Source: Watson, Devin. 4th Axis Tailstock. 2015. Photograph. Central Maine Community College, Maine.

## Slide 3: Tailstock Set-up
Tailstocks should be bolted down through the two cut-outs on the base
If they can’t be bolted down, strap clamps are acceptable to use
Photo Source: Watson, Devin. 4th Axis Tailstock Set-up. 2015. Photograph. Central Maine Community College, Maine.

## Slide 4: Tailstock Alignment Methods
  Test part - made to fit in the bore of the rotary
  Test indicator - used to check the misalignment in the x axis
  The tailstock can then be adjusted to make the test bar parallel to the rotary centerline
    This method does not mean the tailstock is parallel to the centerline, only the tip of the tailstock is
Photo Source: Watson, Devin. 4th Axis Tailstock. 2015. Photograph. Central Maine Community College, Maine.

## Slide 5: Tailstock Alignment Methods
  Ensure the tailstock is parallel to the x axis and on centerline of the rotary
    Most reliable method
  Can be done with a test indicator traversing the quill to ensure parallelism with the X axis
  Test indicator can be used to check to see if the quill is also on the rotary centerline
    Requires more skill and time to set-up, but provides more repeatability
Photo Source: Watson, Devin. 4th Axis Tailstock. 2015. Photograph. Central Maine Community College, Maine.

## Slide 6: Cutting Forces on a 4th Axis
Cutting forces and pressure should always be:
  Considered and transferred into the strongest part of the set-up
  The cutting forces from tools should be directed towards the rotary
No tools should be programmed to cut towards the tailstock due to the lack of rigidity
Photo Source: Watson, Devin. 4th Axis Cutting Forces. 2015. Photograph. Central Maine Community College, Maine.

## Slide 7: Cutting Forces on a 4th Axis
Toolpaths should be programmed towards the spindle to rough or semi-finish
  Transfers more of the forces towards the rotary, which is the strongest part of set-up
Cutter Direction
Photo Source: Watson, Devin. Cutter Direction. 2015. Photograph. Central Maine Community College, Maine.

## Slide 8: Cutting Forces on a 4th Axis
When cutting towards the tailstock or across the part, consider speeds, feeds, and DOC
If the force is large enough, it will cause the rotary to rotate out the desired position
  This can happen even when the rotary clamp is on
Cutter Direction
Photo Source: Watson, Devin. Cutter Direction. 2015. Photograph. Central Maine Community College, Maine.

## Slide 9: Lead and Lag Angles
The tool is programmed normal to the surface (90° from the surface) it is machining
Ball endmills theoretically have 0 SFM at the center
  Causes the tool to push through the material rather than cut
Cut / Rotary Direction

## Slide 10: Lead and Lag Angles
When lead or lag is applied to the tool, the program moves away from cutting normal to the surface
Allows the tool to cut on a larger diameter of the ball
  This larger diameter has a higher SFM, creating a better finish and less cutting pressure
Cut / Rotary Direction

## Slide 11: Lead and Lag Angles
These angles can be applied to any cutting tool used with full rotary motion on the 4th axis
Lead angles tilt the tool into the cut
  Creates a more axial cutting pressure
Lag angle tilt the tool away from the cut
  Creates a more radial cutting pressure
Lag Angle
Lead Angle

## Slide 12: Lead and Lag Angles
Lead and Lag Angles can be activated in MasterCam by adding the desired angle in under the Tool Axis Control tab
Photo Source: Watson, Devin. 4th Axis Lead Angles. 2015. Photograph. Central Maine Community College, Maine.