## Slide 1: 4th Axis Lecture 1
- 4th axis Overview

## Slide 2: Axis Nomenclature
The basic 3 axis mill:
X,Y,Z
  X and Y control table movement
  Z controls tool depth
X AXIS
Y AXIS
Z AXIS

## Slide 3: Adding a 4th Rotational Axis
X,Y, & Z all have a rotational axis
  A - Rotates about X
  B - Rotates about Y
  C - Rotates about Z
This is what gives the machine its fourth rotational axis
X AXIS
Y AXIS
Z AXIS
A
B
C

## Slide 4: 4th Axis CNC Mills
The 4th axis is usually an add on for most machines
  Allows machinists to take an existing three axis machine and add a 4th axis rotary on the table when it is needed
  Machine must have the 4th axis servo drives in order for this to work
Photo Source: Manocchio, Greg. 4th Axis. 2015. Photograph. Central Maine Community College, Maine.

## Slide 5: 4th Axis CNC Mills
The majority of CNC vertical mills have more travel in the X axis
Most 4th axes rotaries are mounted parallel with the X axis of the machine
Use the A Axis of rotation
The A axis movement is expressed in degrees:
  360° = full rotation of the 4th axis
Photo Source: Manocchio, Greg. 4th Axis. 2015. Photograph. Central Maine Community College, Maine.

## Slide 6: Loosing Space
With rotational work, the work envelope in the machines gets smaller as we add the 4th axis
  The VM-2 pictured on the right has 30” of X axis travel
  When the rotary is added, travel size decreases
Loss of X Axis Travel
Photo Source: Manocchio, Greg. 4th Axis Travel. 2015. Photograph. Central Maine Community College, Maine.

## Slide 7: Gaining Space
VF-2 has a sub plate added to the table to allow for the rotary to be placed outside of x axis travel
  Little to no loss of X axis travel
  No chance of the 4th axis getting hit by a cutting tool
Photo Source: Manocchio, Greg. 4th Axis Space. 2015. Photograph. Central Maine Community College, Maine.

## Slide 8: New Codes for the Haas 4th Axis
New Letter Address:
  A - used as the rotational degree increment to position the rotary
    Must use a decimal, A90., if you want to position the rotary to 90°
New M Codes for the Rotary to work:
  M10 - Rotary Brake On
    Better rigidity when not doing simultaneous 4 axis milling work
  M11 - Rotary Brake Off
    Brake must be unclamped before the rotary will position

## Slide 9: Two Types of Positioning
Indexing:
  The part is rotated to a specific degree then the machining takes place
Rotational:
  Sometimes referred to as simultaneous 4th axis
  The rotary moves with any combination of the three positional axis to make a cut
Indexing Cut
Rotational Cut
Photo Source: Manocchio, Greg. 4th Axis Positioning. 2015. Photograph. Central Maine Community College, Maine.

## Slide 10: Indexing
Indexing:
  The rotary is used as an indexing device
  The part is rotated to a specific degree then the machining takes place
  Not all parts machined on a 4th axis are complex parts
  Using a 4th axis is a good way to reduce the number of set-ups needed to make a part

## Slide 11: Example of a 4th Axis Indexing Job:
Soft jaws are normally a three set-up job
Allows for 6 soft jaws to be made in one set-up
The rotary indexes to 0°, 90°, and 180° to work on three sides of the soft jaws
Side 1 at 0°
Side 2 at 90°
Side 3 at 180°
Photo Source: Manocchio, Greg. 4th Axis indexing. 2015. Photograph. Central Maine Community College, Maine.

## Slide 12: Rotational
Rotational:
  The rotary moves with any combination of the three positional axis to make a cut
  The most common axis move together are X and A.
  Z is brought to a specific depth and Y is kept on part center line
Photo Source: Manocchio, Greg. 4th Axis Rotation. 2015. Photograph. Central Maine Community College, Maine.

## Slide 13: Types of Rotaries
Indexing
  Can only rotate in manufacture specific increments, usually 1° or 5°,
  Cannot rotate while the other three axis are moving
  Sequence:
    Position XYZ, unclamp indexing table, rotate, clamp, cut
  Cheaper purchasing price
Rotary
  Can move to unlimited positions
  Can rotate while other machine axis are moving
  Rotary brake must remain unclamped for simultaneous cutting motions
    This makes the rotary less rigid
  Can also be used as an indexing rotary