## Slide 1: 4th Axis Lecture 2
4th Axis Set-up and Offsets

## Slide 2: How is a 4th Axis Set-up?
How to set-up a rotary on a Haas CNC mill:
Photo Source: Manocchio, Greg. 4th Axis Fixture. 2015. Photograph. Central Maine Community College, Maine.

## Slide 3: Chuck Install Video
How to set up an 8” three jaw chuck:
Photo Source: Manocchio, Greg. 4th Axis Chuck. 2015. Photograph. Central Maine Community College, Maine.

## Slide 4: Setting Offsets on a 4th Axis
Usually, machinists set offsets on a 3 axis VMC
The PRZ is usually a corner
The addition of a 4th axis changes how we do offsets
There is no longer a stationary corner to set a PRZ
XY- 0,0
Z0.

## Slide 5: Setting Offsets on a 4th Axis
Parts machined on a 4th axis will be rotating
The easiest way to program this is from the part centerline
The parts will rotate about the A axis
Centerline of Part
Photo Source: Manocchio, Greg. 4th Axis Centerline. 2015. Photograph. Central Maine Community College, Maine.

## Slide 6: Setting Offsets on a 4th Axis
Both Y and Z are normally set to the center of the part
Because the two sides vary in width, it would be confusing if the Z offset came from the top of the part
By setting Z at the center of the part as we rotate around to cut the rectangle, a Z positive value can be used
+Y Axis
+Z Axis
Photo Source: Manocchio, Greg. 4th Axis Centerline. 2015. Photograph. Central Maine Community College, Maine.

## Slide 7: Setting Offsets on a 4th Axis
The X axis offset can be set from the face of the part
  The x moves in the program would be a positive value in absolute
The X axis offset could be set from the back face of the part
  This would make the x moves in the program a negative value in absolute
+X Axis
+Z Axis
Photo Source: Manocchio, Greg. 4th Axis Offsets. 2015. Photograph. Central Maine Community College, Maine.

## Slide 8: Setting Offsets on a 4th Axis
Offsets can be set manually with an edge finder for both the X and Y axis
  Once the Y axis center is found the Z axis offset can be touched off the top of the part,
  The radius of the part can be subtracted
Another option is to make a height block the distance from the table to rotary centerline
  Note the height block pictured to the right
Photo Source: Manocchio, Greg. 4th Axis Touch Off. 2015. Photograph. Central Maine Community College, Maine.

## Slide 9: Setting Offsets on a 4th Axis
Offsets can also be set with a Probe if your machine has this feature:
Photo Source: Manocchio, Greg. 4th Axis Probe Offsets. 2015. Photograph. Central Maine Community College, Maine.

## Slide 10: Dry Running a 4 Axis Set-up
After setting your offsets, loading you program, and loading your part, do a Dry Run of your set-up
  Allows you to check to see if the tool heights and work offset were properly set
  It also allows you to check for tool and tool holder clearances