## Slide 1: PMT 284- Multi Axis CNC Milling
-4th Axis- Lecture 3
Programming

## Slide 2: Lets look at a 4th axis program
This lesson will cover 3 basic 4 axis programming functions:
  Indexing Cuts
  Rotational Cuts
  Drilling
We will be referring to the 4th axis Project 1 as a programming example
You may want to print off your O03701 Project 1 programing exercise to follow along as we go through the lesson

## Slide 3: Indexing Cuts- Milling the Rectangle
Notice the size difference in the height and width of the rectangle
+Y
+Z
For this part we will be programming from the centerline of the part

## Slide 4: Indexing Cuts- 4th Axis Moves
To the right is the program you will be running.
The rectangle on the part will be cut first these are indexing cuts.
This means we will be applying the 4th axis brake for the highest rigidity while cutting.
Before any A axis move you will see an M11(A axis Unclamp). This is needed so the rotary can move to position.
Unclamp
Clamp
Rotate

## Slide 5: Indexing Cuts- Feed Moves
At A0. the 1.500 dimension will be cut first.
Because the part is programed from part centerline this will make our Z height the apart is cut at +.750
Move cutter to position with clearance from the part
Feed to Z depth
Cut across the part
Rapid retract to Z clearance plane

## Slide 6: Indexing Cuts- Feed Moves
After the first flat is cut the A axis will need to be positioned at 180° to cut the second flat
For this to happen the A axis will need to be unclamped, rotated, clamped, then the feed moves can happen
Rotate to 2nd cut to make 1.500 dimension
Feed to Z depth
Cut across the part
Rapid retract to Z clearance plane

## Slide 7: Indexing Cuts- Milling the Rectangle
This completes the 1.500” dimension of the rectangle

## Slide 8: Indexing Cuts- 1.750 Dimension
After the 1.500” side of the rectangle is completed the 1.750” side must be milled.
This will happen at 90° and 270° to complete the rectangle
The program to the right is a continuation of the first tool
The programmed moves will all look the same except for the A axis positions and Z depths for the tool
Note the change in A axis position and Z depth
Note the change in A axis position and Z depth

## Slide 9: Indexing Cuts- Milling the Rectangle
This completes both sides of the rectangle

## Slide 10: Rotational Cutting- Milling the Helixes
Now the program will mill the Helixes
Tool Depth

## Slide 11: Cutting the Helixes
Because the tool need to move in both X and A at the same time to cut the A axis needs to be left unclamped
This makes the set-up less rigid, the trade off is the added capability for simultaneous 4 axis machining
Once the 4th axis is unclamped it will stay unclamped
A axis unclamps and stays unclamped

## Slide 12: Cutting the Helixes- Z depth
The helixes will be cut with a ¼” ball endmill
The helix depth is .1875”
The part is a 2.000” diameter
Because the part is programmed from centerline this make the top of the part 1.000”
  2.000”/2= 1.000”
To get the calculated z depth subtract the helix depth from the top of the part
  1.000”-.1875”=.8125”
Helix Depth
Helix Depth

## Slide 13: Rotational Cutting- Milling the Helixes
Start of Helix is X.750”
End of Helix is X2.750”
This means the helix rotates 360° every 2.000”

## Slide 14: Cutting the Helixes- Start and End Positions
To cut the helix the Y axis will stay on the centerline of the part or Y0.
As noted on the print the start of the helix is at X.750”
In the program the cutter will approach the part with X out of the cut
The cutter will then move to the start of the helix
Cutter rapids to approach position
Cutter feeds to start of helix
Cutter feeds to calculated helix depth

## Slide 15: Rotational Cutting- Milling the Helixes
The helixes start on the 1.500” sides of the rectangle
Because we programmed the 1.500” cuts at A0.° and A180.° the helixes will have to start here as well
The part will need to rotate 360° over 2.000” to make a helix
Because the helix starts at X.750 this means the helix will end at X2.750”
There are two Helixes that start on the 1.500” side of the rectangle

## Slide 16: Rotational Cutting- Milling the Helixes
The endmill can not stop at X2.750”, it should go beyond the stop point
The program has then endmill stopping at X3.000”
This brings the endmill out of the cut
If X end point is adjusted the A axis rotation must be compensated as well
  If not the helix will not be correct

## Slide 17: Rotational Cutting- Milling the Helixes
To calculation for the rotational compensation is as follows:
360° rotation in 2.000” of travel
  180° per 1.000”
  Added .250” of X travel
  180° x .250= 45°
360°+45°=405°
End of helix
Start of Helix

## Slide 18: Rotational Cutting- Milling the Helixes
The second helix must start at 180.°
Because the program is in absolute the 405.° rotated be the A axis must be added to the 180.°
    405.°+180.°=585.°
585.° will be the end point of the second cut
End of 2nd helix
A axis start of 2nd Helix

## Slide 19: Rotational Cutting- A Axis Feed Rates
On a Haas Mill A axis rotational moves are programmed in IPM.
Some machine builders program the A axis with Degrees per minute
In order for the A axis feedrates to come out to the 8 IPM in the program the control does an angular feedrate compensation
  You must enter the Diameter of the part you are cutting in setting 34 of the machine for this angular compensation to be correctly calculated
Note that the A axis is programmed in IPM

## Slide 20: Drilling with a 4th Axis
There are two holes that need to be drilled

## Slide 21: Drilling with a 4th Axis
There are two .250” holes that will need to be drilled to complete the part
These holes are on the face of 1.750” sides of the rectangle
This program is using a carbide drill that does not need a spot drill to start it on location
  If you are not using a similar drill you may need to add a spot drill cycle to the program

## Slide 22: Drilling with a 4th Axis
The drill must first be moved to the start position
  On the print the position it at X.375” and Y-.250
  This position will be the same for both holes
Because the holes are on the face of the 1.7500” sides of the square the holes will need to be drilled at 90° and 270°
  This is were the1.750” flats were milled on the part

## Slide 23: Drilling with a 4th Axis
Because the part is programed in the +Z axis our canned cycle may look a little different then it would on a traditional 3 axis program
The program uses a feed plane and retract plane of Z1.1”
    This is the radius of the part plus .1”
The Z depth to drill to is also a positive number
  This is because the depth does not go beyond the centerline of the part
Feed Plane
Retract Plane
+Z Drill Plane

## Slide 24: Drilling with a 4th Axis
Once a drilling canned cycle it activated the control needs the next drill position
Normally the program would contain the XY move to the next position
In this case the XY position stays the same
What changes is the A axis position
  An A axis move can be used as a position move when a canned cycle is active
Position used to drill second hole