## Slide 1: 5th Axis Lecture 1
-Overview

## Slide 2: Let’s Review Axis Nomenclature
By adding a rotational axis we can utilize a 4 axis mill
  X/Y control table movement
  Z controls tool depth
  A controls rotation about the X axis
X AXIS
Y AXIS
Z AXIS
A

## Slide 3: Adding Two Rotational Axis
X,Y, & Z all have a rotational axis
  A - Rotates about X
  B - Rotates about Y
  C - Rotates about Z
If two rotational axis are added to a machine it becomes a 5th axis mill
X AXIS
Y AXIS
Z AXIS
A
B
C

## Slide 4: 5 Axis CNC Mills
The most common rotational axis combination is A and B
This means that the rotational axis are about the X and Y axis
A AXIS
B AXIS
Photo Source: Manocchio, Greg. 5 axis rotational axis. 2015. Photograph. Central Maine Community College, Maine.

## Slide 5: Types of 5 axis CNC Mills
5th axis machining is a “chicken and the egg” scenario
Machines are specific to a type of part that will be made
Not all parts can be made on each type of 5 axis mill
Photo Source: Manocchio, Greg. 5 axis drilling. 2015. Photograph. Central Maine Community College, Maine.

## Slide 6: Types of 5 axis CNC Mills
There are three main types of 5th axis mills:
  Table/Head rotation
  Head/Head rotation
  Table/Table rotation
The Haas UMC 750 is a 5 axis CNC mill with dedicated A and B rotational axis built in the table, this would be a table/table machine
Photo Source: CNC Report. UMC 750. N.D. Web. 3 February 2015. <www.cncreport.com/haas-umc-750>

## Slide 7: Table/Head Machines
Table/Head Machines
Machines utilize a rotational axis in the table
  Could possibly be a rotating table
Machines utilize a rotational axis that allows the head to rotate side to side
A type of table/head machine could be a 4th axis rotary (A axis) and a tilting head (B axis)

## Slide 8: Head/Head Machines
Head/Head Machines
Machines have a rotating head
Head will tilt
Both rotational axis are built into the head of the machine
The table is a normal CNC mill table
Machines work very well for large work that may be hard to tilt or rotate
Front view of the spindle
Side view of the spindle

## Slide 9: Table/Table Machines
Table/Table Machines
Machines have both rotational axis built into the table
Table can both rotate and tilt
Machines work well for smaller parts
Photo Source: CNC Report. UMC 750. N.D. Web. 3 February 2015. <www.cncreport.com/haas-umc-750>

## Slide 10: Bolt on Trunnion Style Machine
An affordable table/table machine is a bolt on trunnion style machine
  Utilize a 3rd axis mill
  Trunnion can be placed on the table
  Once the servos are enabled, the mill has five axis capabilities
Manocchio, Greg. 5 axis trunnion. 2015. Photograph. Central Maine Community College, Maine.

## Slide 11: Two Main Types of Positioning
  Axis Positioning- often called 3+2 machining
    Consist of two parts that are not complicated
    They are put on a five axis mill to reduce the number of set-ups
  Simultaneous- both rotational axis and any of X,Y, or Z axis are moving at the same time while cutting

## Slide 12: Pivot Point on 5th Axis Machines
All 5th axis machines have a pivot point
On rotating head machines, this distance is calculated one of two ways:
  From the center of rotation to the tip of the tool
  From the center of rotation to the gage line of the spindle
Pivot Distance

## Slide 13: Pivot Point on 5th Axis Machines
This distance must be entered in the CAM system before posting the NC code
If not, the machine will not properly cut the part
Pivot Distance

## Slide 14: Pivot Point on 5th Axis Machines
Machines with both axis of rotation in the table have a diffeent pivot point
The picture to right shows where the pivot point would be located on a trunnion style 5th axis
This distance must be built into the CAM program for the 5th axis moves to be posted correctly in the NC code
A Axis Rotation
B Axis Platter
Pivot distance is the difference between the center of A axis of rotation and the top of the B axis platter

## Slide 15: Work Offsets
Difficult to keep track of the part when it is being manipulated with 2 rotational axes
Easier to set the part to centerline of rotation of the trunnion
  XY - offsets are center of platter hole
  Z - offsets are set to the pivot point of the trunnion
All fixtures used are made to hold the part to the centerline of the trunnion
  If a fixture sits above the pivot point on the trunnion, the value must be added in to the CAM program to achieve the correct cut
The fixture locates the XY centerline of the part at the trunnions center of rotation
Photo Source: Manocchio, Greg. 5 axis fixture. 2015. Photograph. Central Maine Community College, Maine.

## Slide 16: Work Offsets
Some machines, like the Haas UMC 750, utilize a universal work offset
  A part can be placed anywhere on the table
  The CAM program is still made from the centerline of rotation
The distance from the center of rotation to the part is recorded in the machine offsets
  The machine will make the calculations to machine the part where it sits on the table
Part
Top view of the machine table

## Slide 17: New M Codes
The A and B axis both can be clamped and unclamped
  M10 - A axis clamp
  M11 - A axis unclamp
  M12 - B axis clamp
  M13 - B axis unclamp
Remember, before a rotational axis can position, it needs to be unclamped
Unclamp A and B axis
Clamp A and B axis