## Slide 1: 5th Axis Lecture 2
-Set-up & Offsets

## Slide 2: Set-up Tolerances
Using two axes of rotation creates a compounding tolerance issue when rotation occurs
  The set-up must have little to no deviation
A rule of thumb:
  A 3rd Axis set-up can have 20% of part tolerance used in the set-up
    A ±.005 tolerance and .010 deviation, the set-up (possibly a vise) could have .002 of run out
  A 4th Axis set-up can have 10-15% of part tolerance used in the set-up
    A.010 deviation on a part could only have .001-.0015 deviation in the set-up
Photo Source: Manocchio, Greg. TR160 Trunnion. 2015. Photograph. Central Maine Community College, Maine.

## Slide 3: Set-up Tolerances
  A 5th axis part can have 5-10% of part tolerance in the set-up
  If a part has a .005 tolerance, this leaves .0005 to .001 tolerance for the entire set-up
  This tolerance includes:
    Setting the trunnion parallel to the X axis
    Leveling the A axis
    Finding X and Y centerline
    Finding the Pivot Point
    Setting Z height offsets
    Setting the B axis offset
Photo Source: Manocchio, Greg. TR160 Trunnion. 2015. Photograph. Central Maine Community College, Maine.

## Slide 4: Installing the Trunnion
The trunnion must be installed on the machine before a part can be made
The trunnion must:
  Be placed in the machine
  Be connected to servo wiring and air
  Have servos enabled on the control
  Level the A axis
  Be indicated parallel to the x axis
Photo Source: Manocchio, Greg. TR160 Trunnion. 2015. Photograph. Central Maine Community College, Maine.

## Slide 5: Leveling the A axis
The A axis must be leveled before any offsets can be recorded
If the A axis is not level, any offsets recorded will be off
  Could cause the parts produced on the set-up to be made out of tolerance
Photo Source: Manocchio, Greg. Leveling A Axis. 2015. Photograph. Central Maine Community College, Maine.

## Slide 6: Finding Center for X & Y
Haas trunnion machines do not use a universal work offset
It is easier to locate the part to the center of rotation.
Why?
  Fixtures are designed to hold the part on centerline
  Programs are easier to make
  Machinist have an easier time setting up the machine
Photo Source: Manocchio, Greg. Locating XY. 2015. Photograph. Central Maine Community College, Maine.

## Slide 7: Setting the Z Axis height
Z heights need to be set to the center of the A axis of rotation
    This is were the CAM program has Z 0.0 located
Can be done by:
  Leveling the A axis
  Finding the Z offset from the top of the platter
  Adding the pivot distance distance to the Z offset distance
The Z axis height offset can be set by finding the Z machine distance to the top of the B axis platter and adding the pivot distance

## Slide 8: Setting Offsets on a 5 Axis Mill
The following offsets can be found manually with an edge finder and indicator or with a probe:
  Finding the XY Center
  Z axis height offsets
  Pivot Distance
Photo Source: Manocchio, Greg. Locating XY. 2015. Photograph. Central Maine Community College, Maine.

## Slide 9: Finding the Pivot Distance
To find the pivot distance on a trunnion:
  Level the A axis of rotation
  Find XY axis center of the platter
    Record these values in the work offset
Find XY center of the platter
Record the XY machine position
Photo Source: Manocchio, Greg. XY Center. 2015. Photograph. Central Maine Community College, Maine.
Photo Source: Manocchio, Greg. Machine Position. 2015. Photograph. Central Maine Community College, Maine.

## Slide 10: Finding the Pivot Distance
To find the pivot distance on a trunnion:
  Rotate A 90°
  Edge find the Platter
  Write down the Y machine position after the edge finding is complete
Record the Y axis position after the edge finding is complete
Edge find the platter with the Aaxis @ 90°
Photo Source: Manocchio, Greg. Edge finding Y. 2015. Photograph. Central Maine Community College, Maine.
Photo Source: Manocchio, Greg. Pivot Point. 2015. Photograph. Central Maine Community College, Maine.

## Slide 11: Finding the Pivot Distance
To find the pivot distance on a trunnion:
  Subtract the Y axis machine position when the platter was @ 90° from the Y centerline machine position
    In this case 10.0057-9.7577= .2479
    .2479 would be the pivot point, or the distance the A axis of rotation happens above the platter
A Axis Rotation
B Axis Platter
Pivot distance is the difference between the center of A axis of rotation and the top of the B axis platter
.2479 is the
pivot distance

## Slide 12: Setting Offsets on a 5th Axis Mill
The following offsets can be found manually with an edge finder and indicator or with a probe:
  Finding the XY Center
  Z axis height offsets
  Pivot Distance
Photo Source: Manocchio, Greg. Probing XY. 2015. Photograph. Central Maine Community College, Maine.

## Slide 13: Installing a Fixture on a 5th Axis Mill
Most 5 axis part will be held in a fixture
Fixtures are usually part specific
Fixtures must be oriented to the B axis in same way they were programmed
The height of the fixture must be added into the CAM program to get the correct toolpath
Photo Source: Manocchio, Greg. 5 Axis Fixture. 2015. Photograph. Central Maine Community College, Maine.

## Slide 14: Dry Running a 5th Axis Set-up
After setting your offsets, loading you program, and loading your part, Dry Run your set-up
Check to see if the tool heights and work offset were properly set
Check for too and tool holder clearances
  May be better to remove the part to check all tool clearance, then lift Z up
Photo Source: Manocchio, Greg. 5 Axis Dry Running. 2015. Photograph. Central Maine Community College, Maine.