## Slide 1: 5th Axis Lecture 4
-5th Axis- Considerations

## Slide 2: Lead/Lag Angles
Lead/Lag angles can be applied to 5th axis toolpaths
Allows the tool to be cut on a larger diameter of the ball
  The larger diameter has a higher SFM
  Creates a better finish and less cutting pressure
Cut / Rotary Direction

## Slide 3: Lead/Lag Angles
Angles can be applied to any cutting tool used with full rotary motion on the 4th or 5th axis
Lead angles tilt the tool into the cut
  create more axial cutting pressure
Lag angle tilt the tool away from the cut
  create more radial cutting pressure
Lag Angle
Lead Angle
Cut Direction
Cut Direction

## Slide 4: Lead/Lag Angles
Lead and Lag angles can be activated in MasterCam by adding the desired angle under the Tool Axis Control tab
Photo Source: Watson, Devin. Lead Parameters. 2015. Photograph. Central Maine Community College, Maine.

## Slide 5: Tilt Angles
5th axis programs can have tilt angles applied to the endmill
Can be used to angle the tool to the side
Can change the cutting pressure or entry angle of the end mill
Tilt Angle
Cut
Direction

## Slide 6: Tilt Angles
Tilt is used to avoid undercutting a part
Used frequently on parts like impellers, pictured on to the right
The combination of a tapered endmill and tilt allow the blades of the part to be machined without undercutting any of the features on the part
Photo Source: Watson, Devin. Tilt Parameters. 2015. Photograph. Central Maine Community College, Maine.

## Slide 7: Tilt Angles
Tilt can also be applied to pockets and parts with undercuts
Helps to fully machine cavities that may not be done with normal toolpaths
Photo Source: Watson, Devin. Tilt Angles. 2015. Photograph. Central Maine Community College, Maine.

## Slide 8: Cutting Pressure
Three major considerations when programming 5th axis parts:
  Fixture being used
  Rigidity
  Stability of the part
Photo Source: Watson, Devin. Blade Machining. 2015. Photograph. Central Maine Community College, Maine.

## Slide 9: Cutting Pressure - Fixture
Consideration must be made for the fixture:
  How much holding pressure is it applying to the part?
    DOC and feedrates may need to be adjusted during these cuts if there is not enough holding pressure
  How far up is the fixture from the trunnion?
    The higher the fixture to less rigidity there is
  Is the tool going to clear the fixture while machining?
    Does the fixture have enough clearance built in for tool retracts
Photo Source: Watson, Devin. Blade Machining. 2015. Photograph. Central Maine Community College, Maine.

## Slide 10: Cutting Pressure - Rigidity
Rigidity Considerations:
  How rigid is the trunnion that is being used?
  How well is the part being held?
  What is the material?
Will affect the parameters of the toolpaths that are used
Photo Source: Watson, Devin. Blade Machining. 2015. Photograph. Central Maine Community College, Maine.

## Slide 11: Cutting Pressure - Stability
Stability Considerations:
  How many operations will the part need?
    Rough
    Semi-finish
    Finish
  What is the max DOC and feeds for both roughing and finishing?
  Will the part move or vibrate while machining?
Photo Source: Watson, Devin. Blade Machining. 2015. Photograph. Central Maine Community College, Maine.

## Slide 12: Cutting Pressure
The toolpaths should be programmed so that the pressure created from the tool is applied towards the hard stops in the fixture
If not possible, then the parameters of the toolpath may need to be adjusted
Forces should be transfer towards physical stops like these whenever possible
Photo Source: Watson, Devin. Cutting Pressure. 2015. Photograph. Central Maine Community College, Maine.