## Slide 1: PMT 284- Multi Axis CNC Milling
-5 Axis- Lecture 5
- 5 Axis Overview

## Slide 2: Let’s review axis nomenclature
We just covered that by adding a rotational axis we can utilize a 4 axis mill
  X/Y control table movement
  Z controls tool depth
  A controls rotation about the X axis
X AXIS
Y AXIS
Z AXIS
A

## Slide 3: Adding Two Rotational Axis
X,Y, & Z all have a rotational axis
  A- Rotates about X
  B-Rotates about Y
  C-Rotates about Z
If two rotational axis are added to a machine it becomes a 5 axis mill
X AXIS
Y AXIS
Z AXIS
A
B
C

## Slide 4: 5 Axis CNC Mills
The most common rotational axis combination is A and B
This means that the rotational axis are about the X and Y axis
A AXIS
B AXIS

## Slide 5: Types of 5 axis CNC Mills
5 axis machining is a chicken and the egg scenario
5 axis machines specific to a type of part that will be made
Not all parts can be made on each type of 5 axis mill

## Slide 6: Types of 5 axis CNC Mills
There are three main types of 5 axis mills:
  Table/Table rotation
  Table/Head rotation
  Head/Head rotation
The Haas UMC 750 is a 5 axis CNC mill with dedicated A and B rotational axis built in the table, this would be a table/table machine

## Slide 7: Types of 5 axis CNC Mills
Table/Head Machines
These machines utilize a rotational axis in the table.
  This could possibly be a rotating table
These machines utilize a rotational axis that allow the head to rotate side to side
A type of table/head machine could be a 4th axis rotary (A axis) and a tilting head (B axis)

## Slide 8: Types of 5 axis CNC Mills
Head/Head Machines
These machines have a rotating head
The head will also tilt
Both rotational axis are built into the head of the machine
The table to a normal CNC mill table
These machines work very well for large work that may be hard to tilt or rotate
Front view of the spindle
Side view of the spindle

## Slide 9: Types of 5 axis CNC Mills
Table/Table Machines
These machines have both rotational axis built into the table. The table can both rotate and tilt
These machines work well for smaller parts.

## Slide 10: Types of 5 axis CNC Mills
Table/Table Machines
An affordable table/table machine is a bolt on trunnion style machine
These machines utilize a 3 axis mill
When needed the trunnion can be placed on the table
Once the servos are enabled the mill now had five axis capabilities

## Slide 11: Types of Positioning
Much like 4 axis machining there are two main types of cutting with 5 axis machining
  Axis Positioning- this is often called 3+2 machining
    These are parts that are not complicated but are put on a five axis mill to reduce the number of set-ups
  Simultaneous- both rotational axis and any of X,Y, or Z axis are moving at the same time while cutting

## Slide 12: Pivot Point on 5 axis machines
All 5 axis machines have a pivot point
On rotating head machines this distance is calculated one of two ways:
  From the center of rotation to the tip of the tool
  From the center of rotation to the gage line of the spindle
Pivot Distance

## Slide 13: Pivot Point on 5 axis machines
This distance must be entered in the CAM system before posting the NC code
If this is not done the machine will not properly cut the part
Pivot Distance

## Slide 14: Pivot Point on 5 axis machines
Table/Table Machines
Machines with both axis of rotation in the table have a pivot point that is different
The picture to right shows where the pivot point would be located on a trunnion style 5 axis
This distance must be built into the CAM program for the 5 axis moves to be posted correctly in the NC code
A Axis Rotation
B Axis Platter
Pivot distance is the difference between the center of A axis of rotation and the top of the B axis platter

## Slide 15: Work Offsets
It is harder to keep track of the part when it is being manipulated with 2 rotational axis
As described in the 4th axis lecture it is easier to set the part to centerline of rotation of the trunnion
  XY- offsets are center of platter hole
  Z- offsets are set to the pivot point of the trunnion
All fixtures used are made to hold the part to the centerline of the trunnion as well
  If a fixture sits above the pivot point on the trunnion this value must be added in to the CAM program to achieve the correct
The fixture locates the XY centerline of the part at the trunnions center of rotation

## Slide 16: Work Offsets
Some machines, like the Haas UMC 750, utilize a universal work offset
This means that a part can be placed anywhere on the table
  The CAM program is still made from the centerline of rotation
The distance from the center of rotation to the part is recorded in the machine offsets
  The machine will make the calculations to machine the part where it sits on the table
Part
Top view of the machine table