## Slide 1: Live Tooling Lathes
Lecture 1- Overview

## Slide 2: CNC Slant Bed Lathes
Most CNC slant bed lathes consist of two axis
  X- controls diameter
  Z- controls depth
These machines can perform simple turning, drilling, threading, boring, etc.
All work must be done on the centerline of the spindle
Haas Automation Inc. "Y-Axis." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 255. Print.

## Slide 3: CNC Lathes with Live Tooling?
Live tooling is the ability to add milling operations to a lathe
    Done by adding driven tools that can be bolted on the turret of the CNC lathe
Tools will not be as powerful as a CNC mill
Tools will enable turning and milling in one set-up
Haas Automation Inc. “Axial and Radial Live Tooling." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 242. Print.

## Slide 4: Types of Live Tooling
Radial tools
  Hold the cutting tool parallel to the face of the turret
  Designed to work on the diameter of the part performing operations
    milling
    drilling
    tapping
Haas Automation Inc. “Axial and Radial Live Tooling." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 242. Print.

## Slide 5: Types of Live Tooling
Axial tools
  Hold the cutting tool perpendicular to the face of the turret
  Designed to work on the face of the part performing operations
    milling
    drilling
    tapping
Haas Automation Inc. “Axial and Radial Live Tooling." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 242. Print.

## Slide 6: Types of Live Tooling
Options:
  Typical live tooling holders have a 1:1 gear ratio
  The following holders can be purchased:
    High Torque- 1.5: 1 ratio
      Reduced RPM, increased torque
    High Speed - 1:3 ratio
      Increased RPM, Decreased Torque
    Compact Size
    Adjustable Angle
Photo Source: Hiwtc. “VDI Live Tool Holder.” N.d. Web. 28 January 2015. <http://www.hiwtc.com/products/vdi-live-tool-holder-din-5480-din-5482-14617-36464.htm>

## Slide 7: Live Tooling Capacities
Live tooling on a Haas lathe is designed for medium duty milling
  Machinists don’t have the rigidity of a true milling spindle
    3000 RPM limit
    5 HP motor
  Allows the machinist to cut a milling operation out of the process
Productivity Inc. “Live Tooling Torque Chart." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 7. Print.

## Slide 8: C Axis
Fine control of the spindle is needed to position the part for accurate cutting
  The C axis of rotation is added to the machine on the spindle to control the positioning when cutting
    C rotation is used because we are rotating about the z axis
X AXIS
Y AXIS
Z AXIS
A
B
C

## Slide 9: C Axis
The lathe spindle becomes a rotary to be utilized by the live tooling
  This is a true rotary which can preform simultaneous cutting
C axis enables positioning for live tooling
  machine can still only cut on the spindle centerline
Haas Automation Inc. “Y axis Motion." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 255. Print.

## Slide 10: Y axis
With live tooling and a C axis rotation, machinists can make cuts on the centerline of the part
What if we what to make cuts off the centerline of the part?
  The Y axis can be added to the lathe to move the turret perpendicular to the x axis
    The Haas lathes have the ability to travel +/-2” from spindle centerline
Haas Automation Inc. “Y axis Motion." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 255. Print.

## Slide 11: Y axis
The Y axis allows the machine to cut off centerline
This allows features like the following to be machined:
  Flats
  Bolt circles on the diameter
  Holes of centerline
Haas Automation Inc. “Y axis Motion." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 255. Print.

## Slide 12: Y axis
Another look at Y axis usage:
Haas Automation Inc. “Y axis Milling." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 258. Print.