## Slide 1: Live Tooling Lathes
Lecture 7 – Dual Spindle lathes

## Slide 2: Dual Spindle Lathes
Dual spindles add a secondary spindle where a tail stock would normally be
  Can advance forward to clamp on a part that is in the main spindle
Once the sub spindle retracts, the turret can then work on the part in the sub spindle
  Allows for the completion of both sides of the part in one machine
Haas Automation Inc. “Y axis Motion." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 255. Print.

## Slide 3: Dual Spindle Lathes
Dual spindle lathes can be ordered in a variety of configurations:
  With or w/out C axis
  With or w/out Y axis
  With or w/out live tooling
  One, Two, or even Three turrets
The configuration depends on the type of work that will be done on the machine
Haas Automation Inc. “Y axis Motion." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 255. Print.

## Slide 4: Multi-Tasking Machines
Live tooling lathes are commonly referred to as Multi-Tasking machines, but this is wrong
Here are the major differences:
  Live tooling lathes have secondary milling capabilities
    The milling is not as powerful as it would be on a mill
  Multi-tasking machines have both turning and milling capabilities that are equal to having either machine
    There is no performance lag with having either capability on the machines
Photo Source: Production Machining. Mill Turn. N.D. Web. 5 February 2015. www.productionmachining.com/articles/turn-mill-classics