## Slide 1: Live Tooling Lathes
Lecture 5- milling Toolpaths

## Slide 2: Milling with Live Tooling
Milling toolpaths can be programmed on a Live tooling lathe in different ways
Use the 278-3 project as a guide as we review different milling toolpaths on the live tooling lathe

## Slide 3: Axial or Face Milling
Let’s review the slot on the front face of this part
This can be cut two ways:
  With X & C programming
  With G112 Cartesian to Polar programming

## Slide 4: Milling the Face Slot
We have set the entrance of the groove to 90° and the exit at 270°
A ¼” Endmill is used to mill the slot in one pass at the desired depth
G98 is used because of the milling operation
Entry point
Exit point

## Slide 5: Milling the Face Slot
It is important to note that the feedrate is set to IPM
The C axis will also be rotating while cutting
  This is a rotational move, not a linear move
The Haas control will convert linear feeds to rotation feeds automatically
For the control to do this properly, setting 102 must be set to the diameter that is going to cut
  If this diameter is wrong, the feed conversion will not be precise
Programmed feedrate

## Slide 6: Milling the Face Slot
Set the entrance of the groove to 90° and the exit at 270°
A ¼” Endmill is used to mill the slot in one pass at the desired depth
G98 is used because of the milling operation
Start of slot
End of slot
Move to Depth
Start cutting slot
Exit part

## Slide 9: Programming the slot with G112
G41 can also be used with G112
  The comp. value would be set in radius column on the tool wear page when using G112
  The radius column on the tool geometry page is used for the nose radius of the turning inserts
Central Maine Community College. Haas Tool Offsets [Photograph]

## Slide 10: Programming the Slot with G112
G41 or G42 can be used with the function
  G40 must be used before G113 cancels the operation

## Slide 11: Programming the Slot with G112
Note: the XY moves (see program on right)
The machine will not move in the Y axis
All XY moves will be converted to XC moves in the machine

## Slide 12: Radial Milling the Large Flat
The large flat will be cut with a 1.5” shoulder mill
The shell mill is qualified from the front face of the part
  This makes calculating the Z depth easier
Z 0.0

## Slide 13: Radial Milling the Large Flat
The Flat had a dimension of 1.700
What Diameter is the flat on?
  This dimeter is where the X axis will need to be positioned to cut the flat

## Slide 14: Radial Milling the Large Flat
Diameter of part is 2.0
Radius of part is 1.0
  1.70 - 1.00 = .700
  700 x 2 = 1.400
The flat is located on a diameter of 1.400

## Slide 15: Radial Milling the Large Flat
Radial milling for this flat can be broken into simple steps:
  Engage tool & pickup offsets
  Rotate to Position
  Move to depth
  Cut across part
  Retract in X
  Rapid across the part
  Repeat steps until desired depth is reached

## Slide 16: Drilling the Radial holes
Drilling on the OD of the part can be done with the G240 series of canned cycles
  These are designed to work with radial tool holders
Y and Z will position the tool and X will control depth on these tool paths

## Slide 17: OD - Radial Drilling
Cross drilling takes more thought and calculation for a successful toolpath
The depth is controlled by X for these paths
  X is read by the machine as a diameter
  For this to work, more math will need to be done
Where did this depth come from?

## Slide 18: Calculating Drill Depth
The print states the holes are .38 deep, but this is from the flat
This value will need to double (.760) since we are drilling to a diameter because we are on a lathe
To get the final drill depth, subtract the final drill depth from the starting diameter
  1.400 - .760 = .640 Diameter