## Slide 1: Live Tooling Lathes
Lecture 6- Drilling Toolpaths

## Slide 2: Face and Axial Drilling
This lecture will look at the different toolpaths and how they work on a live tooling lathe
Use the 328-2 project as a guide as we review different toolpaths on the live tooling lathe

## Slide 3: Drilling the 1.063 Thru Hole
The first drilling toolpath we will review is the drilling of the 1.063 diameter hole
  Done with a Sandvik 880 insert drill
The 880 drill can drill, retract, then bore a hole
  This is the process we will demonstrate to produce this hole

## Slide 4: Drilling the 1.063 Thru Hole
The drill will drill to depth at the centerline of the part
The drill will retract then step up in X
  Note: the X value to the right is not correct
  After the drill has finished, take a measurement and check surface finish
  Next, adjust diameter and feedrates to achieve desired result
The drill will then feed to depth boring the hole
  The peripheral insert must be in X positive for this to work
Drill to Depth
Bore to Depth
Offset in X

## Slide 5: Face and Axial Drilling
Drilling the three holes on the face of the part can be done with the regular G80 series drilling canned cycles
  The part will be programmed without a peck because of the depth

## Slide 6: Face and Axial Drilling
G81 is programmed the same way it would be on a mill or a lathe
  Note: a C value can be used as a position move during a canned cycle
The depth is controlled by Z
  The plane needs to be set with G18

## Slide 7: Face and Axial Drilling
If G82 is used, a P value needs to be entered for a dwell after the depth is reached
If G83 is used, a Q value needs to be entered to specify the peck amount

## Slide 8: OD and Radial Drilling
Drilling on the OD of the part can be done with the G240 series of canned cycles
  Designed to work with radial tool holders
Y and Z will position the tool
X will control depth on these tool paths

## Slide 9: OD and Radial Drilling
Cross drilling takes more thought and calculation for a successful toolpath
  The depth is controlled by X for these paths
    X is read by the machine as a diameter
    for this to work more math will need to be done
Where did this depth come from?

## Slide 10: Calculating Drill Depth
The flat is at a dimension of 1.700 from the opposite side
This means the flat is .300 deep
  This depth need to be doubled (.600) to find the diameter on the lathe where the holes start
1.700 - .600 depth = 1.100
  Diameter for the starting drill depth

## Slide 11: Calculating Drill Depth
The print states the holes are .38 deep
  This is from the flat
This value will need to double (.740)
  Drilling to a diameter because we are on a lathe
To get the final drill depth, subtract the final drill depth from the starting diameter
  1.400 - .740 = .660 Diameter

## Slide 12: OD and Radial Drilling
G19 is used because Y and Z are the positioning axis
This makes X the retract axis for the canned cycle
If G18 was used, the automatic retract would happen in Z and result in a broken drill

## Slide 13: G242 and G243
If G242 is used, a P value would need to be added for a dwell time to happen
If G243 is used, a Q value would need to be added to specify the peck amount that is desired