## Slide 1: Live Tooling Lathes
Lecture 2- Live Tooling Set-ups

## Slide 2: Live Tooling Lathes
This lecture will review the following:
  Installing Axial Tools
  Offsets for Axial Tools
  Installing Radial Tools
  Offsets for Radial Tools
  C axis engagement and offsets
  Y axis offsets

## Slide 3: Axial Tools
The driven tools on the Haas lathes are mounted in the VDI tool holders
VDI holders are a quick change tool holder built into the turret
Photo Source: Exsys Tool. N.d. Web. 29 January 2015.<http://www.exsystool.com/images/catalog/archive/haas-tooling-catalog.pdf>

## Slide 4: Axial Tools
Axial tools are offset similar to turning tools
  The Z offset can be set by touching off the face of the part
  The X offset can be set by touching the endmill off the outside of the part, then adding the diameter of the tool and part to the offset

## Slide 5: Radial Tools
Like axial tools, radial tools are set-up in the turret
These live tooling holders have many types of holders that can be used:
  ER collets
  Endmill holders
  Shellmill holders
  Tap holders
Photo Source: Exsys Tool. N.d. Web. 29 January 2015.<http://www.exsystool.com/images/catalog/archive/haas-tooling-catalog.pdf>

## Slide 6: Radial Tools
Radials tools are offset opposite the axial tools:
  To set Z offset: touch the diameter of the cutting tool off the face of the part
  To set X offset: set end of the endmill off the outer diameter of the part, then subtract the diameter from the offset
  The coolant line of the tool should also be set while doing the tool offsets
Coolant should be adjusted here when setting the tool up
Photo Source: Exsys Tool. N.d. Web. 29 January 2015.<http://www.exsystool.com/images/catalog/archive/haas-tooling-catalog.pdf>

## Slide 7: Starting the Live Tooling
C180
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C270.
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
M135
M155
M09
G0 G28 H0.
G53 X0. Y0.
G18
G99
M01
M133- Live Tool Forward
  P sets the speed
    M133 P500- would turn the tool on at 500 RPM
M134- Live Tool Reverse
M135- Live Tool Stop
G98
M154
G0 G54 C0. Y1.0 X1.0 Z.1
M14
G97 M133 P1500
M08
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C90.
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15

## Slide 8: Engaging the C axis
The spindle is normally used as a high RPM rotating feature on a lathe
With a live tooling lathe, the spindle has the capability to be engaged as a fine increment rotary
Haas Automation Inc. “Y axis Motion." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 255. Print.

## Slide 9: Engaging the C axis
New Codes:
M154- C axis engage
M155- C axis disengage
M14- Clamp Spindle
    Used for clamping the C axis while making cuts with live tooling
M15- Unclamp spindle
  H sends the C axis home incrementally
%
O01234
G19
G98
M154
G0 G54 C0. Y1.0 X1.0 Z.1
M14
G97 M133 P1500
M08
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C90.
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C180
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C270.
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
M135
M155
M09
G0 G28 H0.
G53 X0. Y0. W0.
G18
G99
M01

## Slide 10: Engaging the Y Axis
The Y axis:
Is used to bring the turret off centerline from the spindle
Is used mainly in programmed moves to cut the part
Can be offset like any other axis on the machine
  If a Y axis offset is needed when setting a boring bar, it may mean the turret is not properly aligned
Haas Automation Inc. “Y axis Motion." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 255. Print.