## Slide 1: Live Tooling Lathes
Lecture 4- pLANES

## Slide 2: Plane Selection
Different planes can be used to make different canned cycles and milling tool paths work correctly on a live tooling lathe
Drill or Mill- refers to face work or axial work on a live tooling lathe
Cross Mill or Cross Drill- refers to work on the OD or radial work on a live tooling lathe
Haas Automation Inc. “Axial and Radial Live Tooling." Lathe Operator's Manual. N.p.: Haas Automation Inc., 2014. 242. Print.
Productivity Inc. “Plane Selection." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 10. Print.

## Slide 3: Plane Selection
G17, G18, G19
  What are these codes?
    G17-XY plane
    G18-XZ plane
    G19-YZ plane
Productivity Inc. “Plane Selection." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 10. Print.

## Slide 4: Plane Selection
What do these planes mean?
  Plane selection (G17, G18, G19) determines the main plane of work.
  Think of these planes as axis selection:
    G17 - the Z axis positions and the main cutting axis would be X and Y
    G18 - the Y axis positions and the main cutting axis would be X and Z
    G19 - the X axis positions and the main cutting axis’ would be Y and Z.
Productivity Inc. “Plane Selection." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 10. Print.

## Slide 5: G17- Axial Milling
G17 is used when XY milling is taken place
G17 is also used with G112
  G112 can convert XY moves to XC moves
  This means a milling toolpath could be converted to XC moves
G112 could be used with the slot

## Slide 6: G18 - The Default
G18 is the default for slant bed lathes
All of the typical OD and ID turning will happen in the XZ plane
    These are the main axes of the machine
XC milling also happens with G18 active
The turning, drilling and boring for the 278-3 part would all happen with the G18 plane
G18 could also be used for the XC milling for the slot on the front face

## Slide 7: G19 - Radial and Cross Drilling
G19 is used with all radial and cross drilling toolpaths
G19 would also be used with any facing or milling happening on the OD the of part
G19 would be used on for milling the Flat on the OD of the 278-3 part
G19 would also be used when drilling the four holes on the flat of the part

## Slide 8: G17 Plane Selection Guide
Cycle | Description | Feedrate
XY AXIS MILLING | MANUAL FACE PROGARMMING | G98
G112 | CARTIESAN TO POLAR | G98

## Slide 9: G18 Plane Selection Guide
Cycle | Description | Feedrate
G81 | SIMPLE DRILLING | G98
G82 | SIMPLE DRILLW/ DWELL | G98
G83 | DRILL W/ PECK | G98
G95 | RIGID TAP | G99
G186 | RIGID TAP LEFT HAND | G99
X-C MILLING | FACE MILLING | G98

## Slide 10: G19 Plane Selection Guide
Cycle | Description | Feedrate
G241 | CROSS DRILL | G98
G242 | CROSS DRILLW/ DWELL | G98
G243 | CROSS DRILL W/ PECK | G98
G195 | RIGID TAP | G99
G196 | RIGID TAP LEFT HAND | G99

## Slide 11: Axial Drilling
Let’s look at programing axial canned drilling cycles
  We know we will need to use the G18 plane
  We will need to use the X, Z and C axis for these holes
  An axial live tool will be needed
Productivity Inc. “Axial machining." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 13. Print.

## Slide 12: Axial Drilling
Example Program using G81:
Plane Selection
Canned Cycle
Productivity Inc. “Axial machining." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 13. Print.

## Slide 13: Axial Drilling
C Axis Positioning:
During canned cycles, the C axis can be used for positioning just like the XY axis can be used:
Productivity Inc. “Axial machining." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 13. Print.

## Slide 14: Axial Drilling
Example Program using G83:
Plane Selection
Canned Cycle
Productivity Inc. “Axial machining." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 13. Print.

## Slide 15: Radial Drilling
Radial Drilling using G241, G242, G243:
Let’s look at drilling holes on the diameter of the part:
  Use the G19 plane
  A Radial live tooling holder will be needed
  Remember that the machine still reads diameter
    Depths and retracts still need to be programed to diameters and not radii
Productivity Inc. “G241 Radial Drilling Canned Cycle." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 30. Print.

## Slide 16: Radial Drilling
Radial Drilling using G241:
Productivity Inc. “G241 Radial Drilling Canned Cycle." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 30. Print.

## Slide 17: Radial Drilling
Radial Drilling using G241:
Productivity Inc. “G241 Radial Drilling Canned Cycle." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 30. Print.

## Slide 18: Radial Drilling
Radial Drilling using G242:
Productivity Inc. “G242 Radial Spot Drilling Canned Cycle." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 31. Print.

## Slide 19: Radial Drilling
Radial Drilling using G242:
Productivity Inc. “G242 Radial Spot Drilling Canned Cycle." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 31. Print.

## Slide 20: Radial Drilling
Radial Drilling using G243:
Productivity Inc. “G243 Radial Peck Drilling Canned Cycle." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 33. Print.

## Slide 21: Radial Drilling
Radial Drilling using G243
Productivity Inc. “G243 Radial Peck Drilling Canned Cycle." Live Tool For has Lathes. N.p.: Productivity Inc., 2012. 33. Print.