## Slide 1: Live Tooling Lathes
Lecture 3- Programming Changes

## Slide 2: Let’s look at a Live Tooling Program
The Live Tooling program is used with the 278-1 program to review the new codes associated with Live Tooling lathes
The 1” square will be cut with a Radial tool
The ¾” square will be cut with an Axial tool
2

## Slide 3: Let’s look at a Live Tooling Program
Here is the program for the 1” square cut with the Radial Tool:
%
O01234
(MILL 1.00 SQUARE WITH RADIAL TOOLHOLDER)
T1010 (RADIAL TOOL W/ ½ E.M.)
G19
G98
M154
G0 G54 C0. Y-1.0 X1.0 Z.1
M14
G97 P1500 M133
M08
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C90.
M14
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C180
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C270.
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
M135
M155
M09
G0 G28 H0.
G53 U0. V0. W0.
G18 G99
M01
3

## Slide 4: Starting the Live Tooling
M133- Live Tool Forward
  P sets the speed
    M133 P500- would turn the tool on at 500 RPM
M134- Live Tool Reverse
M135- Live Tool Stop
%
O01234
(MILL 1.00 SQUARE WITH RADIAL TOOLHOLDER)
T1010 (RADIAL TOOL W/ ½ E.M.)
G19
G98
M154
G0 G54 C0. Y-1.0 X1.0 Z.1
M14
G97 P1500 M133
M08
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C90.
M14
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C180
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C270.
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
M135
M155
M09
G0 G28 H0.
G53 U0. V0. W0.
G18 G99
M01
4

## Slide 5: C Axis Engagement
New Codes:
M154- C axis engage
  The C axis must be engaged to locate and position the spindle
M155- C axis disengage
  The C axis must be disengaged before using the spindle at high RPM
%
O01234
(MILL 1.00 SQUARE WITH RADIAL TOOLHOLDER)
T1010 (RADIAL TOOL W/ ½ E.M.)
G19
G98
M154
G0 G54 C0. Y-1.0 X1.0 Z.1
M14
G97 P1500 M133
M08
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C90.
M14
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C180
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C270.
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
M135
M155
M09
G0 G28 H0.
G53 U0. V0. W0.
G18 G99
M01
5

## Slide 6: Spindle Lock
New Codes:
M14- Clamp Spindle
    Used for clamping the C axis while making cuts with live tooling
M15- Unclamp spindle
  The C axis must be unclamped before positioning or it will not move
H sends the C axis home
%
O01234
(MILL 1.00 SQUARE WITH RADIAL TOOLHOLDER)
T1010 (RADIAL TOOL W/ ½ E.M.)
G19
G98
M154
G0 G54 C0. Y-1.0 X1.0 Z.1
M14
G97 P1500 M133
M08
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C90.
M14
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C180
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C270.
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
M135
M155
M09
G0 G28 H0.
G53 Y0.
G53 X0 Z0.
G18 G99
M01
6

## Slide 7: Can We Use a Sub-Program?
Does any code repeat?
The following code repeats:
  M14
  G1 Y1.0 F15.
  G0 X1.5
  Y-1.0
  X1.0 M15
We can use a subprogram to reduce the length of the program
%
O01234
(MILL 1.00 SQUARE WITH RADIAL TOOLHOLDER)
T1010 (RADIAL TOOL W/ ½ E.M.)
G19
G98
M154
G0 G54 C0. Y-1.0 X1.0 Z.1
M14
G97 P1500 M133
M08
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C90.
M14
G1 Y-1.0 F15.
G0 X1.5
Y1.0
X1.0 M15
C180
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
C270.
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
M135
M155
M09
G0 G28 H0.
G53 Y0.
G53 X0. Z0.
G18 G99
M01
7

## Slide 8: The Formatted Program
Sub-program codes:
  M98- Sub-program call
  P- Sub-program call
  M99- Sub-program end
The M98 P1235 Call up the Sub-program
Once the Sub-program is done running, the M99 returns to the main program
%
O01234
(MILL 1.00 SQUARE WITH RADIAL TOOLHOLDER)
T1010 (RADIAL TOOL W/ ½ E.M.)
G19
G98
M154
G0 G54 C0. Y-1.0 X1.0 Z.1
G97 P1500 M133
M98 P1235
C90.
M98 P1235
C180.
M98 P1235
C270.
M98 P1235
M135
M155
M09
G0 G28 H0.
G53 Y0.
G53 X0. Y0.
G18 G99
M01
%
O01235
M14
G1 Y1.0 F15.
G0 X1.5
Y-1.0
X1.0 M15
M99
8

## Slide 9: Programming the ¾” Square with an Axial Tool
This will be done with the axial cutting tool
This operation will utilize the same format with a main program and sub program for cutting
%
O01236
(MILL .750 SQUARE WITH RADIAL TOOLHOLDER)
G0 G40 G80
T1010 (AXIAL TOOL W/ ½ E.M.)
G17
G98
M154
G97 P2000 M133
G0 G54 C0. Y1.0 X1.25 Z1.
Z.1
M98 P1237
C90.
M98 P1237
C180.
M98 P1237
C270.
M98 P1237
M135
M155
G53 Y0.
G53 X0. Z0.
G18
G99
M01
%
O01237
M14
G01 Z-.125 F15.
Y-1.
G00 Z.1
Y1.
M15
M99
%
9