## Slide 1: PMT 280- 3-D CNC Milling
Lecture 2- What is three dimensional machining

## Slide 2: What is 3-D Machining?
A simple definition is: 3-D machining is the machining of non-flat surfaces.
  These surfaces generally need to be finished with a spherical or ball endmill to achieve the finish that is needed

## Slide 3: Types of Parts utilizing 3-D Machining
Medical
  Replacement Joints
Aerospace
  Have you ever seen a flat part on a plane
Molds and Dies
  All molds and dies need to be machined to the surface they are creating
Power Generation
  Airfoils
This list is just a small example of parts need
Industries utilizing 3-D machining

## Slide 4: New Concepts
High Speed Machining (HSM)
Ball Endmills for finishing
High Feeds and Speeds with low radial engagement
Dampened tools
  Adding carbide in the shank of an insert able cutter to reduce vibration at higher RPM and Feed Rates
We will be covering all of these topics more in depth in later lectures in this class

## Slide 5: Basic types of Cutters
Basic types of endmills used:
  Flat Endmill
    Often used to rough parts
  Bull Endmill
    Can be used to rough parts or in some cases finish parts
  Ball Endmill
    Utilized with a small step over to finish complex surfaces
Cutters under ½” diameter are normally solid carbide. Cutters over ½” diameter should be insertable to save time and money.

## Slide 6: Common Operations with 3-D Machining
Rough Machining:
  Large amounts of material are removed as quickly as possible
  Often with an insert able cutter
  Material is left on the finished part so another operation can bring the part to finish

## Slide 7: Common Operations with 3-D Machining
Semi Finishing:
  After the part is roughed a tool may be used before the finishing tool to bring the part closer to finished shape
  This can reduce the large material deviations left from the roughing tool that the finish tool may not be able to handle
  Less material is left on the part then with the roughing step before the part is finished

## Slide 8: Common Operations with 3-D Machining
Finishing:
  After the rough and/or semi finish stage the part can now be finished
  This is normally done with a ball tool(solid carbide or insertable).
  Very small radial step over to achieve the desired finish and tolerance needed
  Happens at very high RPM and Feedrates due to the small amount of material being removed

## Slide 9: New Codes
G17, G18, G19
  What are these codes?
    G17-XY plane
    G18-XZ plane
    G18-YZ plane
What do these planes mean?
  Plane selection (G17, G18, G19) determine the main plane of work.
  Think of these planes as axis selection.
    With G17 the Z axis positions and the main cutting axis’ would be X and Y.
    With G18 the Y axis positions and the main cutting axis’ would be X and Z.
    With G19 the X axis positions and the main cutting axis’ would be Y and Z.

## Slide 10: Plane Selection Continued
Cutter Compensation can also be applied based on plane selection.
Cutter comp. is applied to two axis of movement when activated in the program. This would apply as follows:
  G17- XY
  G18- XZ
  G19- YZ
Plane selection also effects G2 and G3 moves.
  Using Center Point Method of arc programming arcs would be programmed the following way:
    G17- G2 X Y I J
    G18- G2 X Z I K G19- G2 Y Z J K

## Slide 11: Plane Selection Continued
Plane selection can also affect automatic cycles such as canned drilling cycles:
  G17- Z is the drilling axis
  G18- Y is the drilling axis
  G19- X is the drilling axis
An example of needing cutter compensation or a drilling cycle in a plane other then G17 would be with the use of a right angle head in a CNC Mill.

## Slide 12: Thru Spindle Coolant (TSC)
For this class we will be utilizing the thru spindle coolant option when it is available
TSC’s main advantage is providing coolant directly at the cutting source.
  This requires the tool, holder, and machine to all be capable of handling TSC.
On a Haas Mill TSC is activated by:
M88- TSC on
M89- TSCC off

## Slide 13: Calculating Surface Finish of 3-D part
Surface finish, by definition, is the allowable deviation from a perfectly flat surface that is made by some manufacturing process.
This is normally calculated in Ra or roughness average
  The following can affect surface finish:
    Choice to tool
    Speed and feed
    Machine conditions
    Programming
This lecture will focus on the programming of finish tools, more importantly step over.

## Slide 14: Cusp Height/ Scallop Height
Cusp or Scallop height is common when ball endmills are used.
The ball nose is needed when finishing a non-flat surface.
Because the tool is a ball we program the tool to profile the surface
  Profiling a surface is taking a small radial step over as the tool travel around the surface finishing the part
The red in the above picture is the scallop left behind when a ball endmill steps over

## Slide 15: Cusp Height/ Scallop Height
The stepover in the tool path causes the scallop left from the ball endmill.
There is a trade off:
  A larger stepover takes less machining time but creates a worse surface finish
  A smaller stepover takes more machining time but creates a better surface finish
    Everybody loves sanding and polishing parts!

## Slide 16: Step Over Percentage
A step over percentage of 1/3 of the diameter of the finish tool would look like the picture below
A ½” ball endmill with this percentage step over would be .1666”
This type of step over would be take the least amount of time to machine
This type of step over would be good on a material that is easy to sand like wood

## Slide 17: Step Over Percentage
A step over percentage of 1/5 of the diameter of the finish tool would look like the picture below
A ½” ball endmill with this percentage step over would be .100”
This type of step over would increase the machining time minimally to achieve a better surface finish

## Slide 18: Step Over Percentage
A step over percentage of 1/10th or 1/20th of the diameter of the finish tool would look like the picture below
A ½” ball endmill with this percentage step over would be .025-.050”
This type of step over would be take the longest time to machine but provide the greatest detail
This type of step over would be good on materials like tool steels or even aluminum where secondary finishing operations can take significant time

## Slide 19: Step Over Notes
It is important to consider the material being machined
Materials like MDF or wood may not be able to hold the detail of a small step over and they can be finished so easily that there is not need to take the extra machining time
It is important to use the largest possible tool, this will achieve the smallest scallop height with largest stepover possible
Also consider that with these small step overs for finishing the feeds will be very high due to the very light chip load
Cutting the step over in half does not always double machining time due the increased feed rates. (This will be covered more in the week 3 lecture)

## Slide 20: MasterCam Can Help
Many of our MasterCam surface finish toolpaths contain a cusp height calculator
It is located under the Max stepover button

## Slide 21: MasterCam Can Help
Once in the calculator you can enter the step over you would like to find the scallop height
You can also enter the scallop height you would like to find the maximum step over to achieve this
  Note: This is based on the tool you have selected in MasterCam

## Slide 22: How do you Calculate Ra
The surface finish is usually called out on the print or on a specific surface on the print
In the lab we have two methods for finding surface finish
  Surface Roughness Standards
    This is a manual method
  Profilometer
    This is a small portable device to measure finish
Once you have finished a project if you are unfamiliar with checking finish with one of these two methods please let me know and I will show you