## Slide 1: PMT 280- 3D CNC MILLING
Lecture 4- Radial Chip Thinning

## Slide 2: Two Types of Chip Thinning
Radial Chip Thinning
Ball Nose Chip Thinning

## Slide 3: Review of concepts
Axial Cuts:
  Think of as Depth Cuts
  Pressure transferred to the Z axis
    Drilling is a good axial pressure application
  Less vibration with this cutting method
Axial
Radial

## Slide 4: Review of concepts
Radial Cuts:
  Think of as Amount of Step Over
  Pressure transferred to the X or Y axis
    Side milling is a cut that creates radial pressure
  This pressure creates more cutter pressure as the width of cut increases
Axial
Radial

## Slide 5: Key Terms
Chip Per Tooth- IPT
  the calculated/ theoretical chip load the cutter should have
  We use this to calculate federate
    IPM= IPT x # of teeth X RPM
Chip Thickness
  This is the actual thickness of the chip after it is cut.
  This can vary due to the radial step over
IPT
Chip Thickness

## Slide 6: What is Radial Chip Thinning
Based on the previous slides we now know that it relates to the “Step Over” or Width of Cut (WOC)
Chip thinning takes effect when we are cutting with less then 50% of the cutters diameter
The smaller the radial engagement the larger the difference becomes between IPT and Chip Thickness
IPT
Chip Thickness

## Slide 7: Lets Take a Look at How it Works
Lets look at the following scenario:
  2” Diameter Cutter
  1500 RPM
  5 Flute
  .010 IPT
We know the formula for federate is:
  IPM= IPT x # of teeth X RPM
  IPM=.010 x 5 x1500
  IPM= 75
.010 IPT
Chip Thickness
2” Diameter Cutter

## Slide 8: Lets Take a Look at How it Works
75 IPM sounds good but have we figured radial chip thinning into the factor yet?
  Notice on the right the radial engagement is only .400
  Look and the Chip Thickness relative to the IPT.
  It is not what we calculated
.010 IPT
Chip Thickness
2” Diameter Cutter
.400 Radial Engagement

## Slide 9: The Radial Chip Thinning Factor
To find the radial chip thinning factor we need a chart like the one on the left.
To do this:
  Find the line corresponding to the cutter diameter
  Find the line corresponding to the radial depth of cut
  Follow the two lines until the intersect. The closest diagonal line is your chip thinning factor
  You can see our chip thinning factor in .8

## Slide 10: How to Apply the Chip Thinning Factor (CTF)
Appling the factor is vary simple:
  Take the calculated feed and divide it by the Chip Thinning Factor
  75/.8 = 93.75 IPM
  94 IPM is our new feed rate to maintain .010 IPT and the point of contact
.010 IPT
Chip Thickness
2” Diameter Cutter
.400 Radial Engagement

## Slide 11: When the factor really works
The CTF becomes more beneficial when the radial engagement is less then 25% of the cutter Diameter
  Lets say the Radial engagement on this cutter is only .050
  This would give us a CTF of .35 on the chart
    75/.35= 214.3 IPM
    Notice the Increase!
.010 IPT
Chip Thickness
2” Diameter Cutter
.050 Radial Engagement

## Slide 12: Why is RCTF so Important?
Increased Feed Rate
  We have just calculated this, you can see the potential savings
Increased Tool Life
  Maintianing proper chip load prevents rubbing
Insert Entry Angle
  When radial engagement is less then ½ the cutter diameter the insert enters the cut with a positive rake

## Slide 13: Insert Entry Angles
Three insert entry angles
  Positive
  Neutral
  Negative
Not the picture on the right
  The cutter’s radial engagement is greater then 50% of the tool Diameter
  This means the insert enters with a negative rake angle
Negative Entry Attributes:
  Strongest Entry
  Created the most vibration/shock
  Face of inserts hits before edge
  Creates a shearing effect rather then cutting

## Slide 14: Insert Entry Angles
Three insert entry angles
  Positive
  Neutral
  Negative
Not the picture on the right
  The cutter’s radial engagement is at the centerline of the tool
  This means the insert enters with a neutral rake angle
Neutral Entry Attributes:
  Creates less vibration/shock
  Face and edge of insert contact the part at the same time
  Shearing force is less then negative entry

## Slide 15: Insert Entry Angles
Three insert entry angles
  Positive
  Neutral
  Negative
Not the picture on the right
  The cutter’s radial engagement is at less then 50% of the tool
  This means the insert enters with a positive rake angle
    This the entry angle we want to always try and maintain
Positive Entry Attributes:
  Creates very little vibration/shock
  Edge of insert contacts part before the face
  Chips are cut rather then sheared from the part
  Less pressure means faster speeds, feeds, better tool life, less horsepower consumption

## Slide 16: To Review
Radial Chip Thinning:
Only works when engagement is less then 50% of cutter diameter
Decrease Cycle Time
Increase tool life
Have more consitiancy
Types of Chip Thinning
Radial Chip Thinning
Ball Nose Chip Thinning
Insert Entry Angles
Positive
Negative
Neutral