## Slide 1: PMT 280- 3-D CNC MILLING
ball nose chip thinning

## Slide 2: Two Types of Chip Thinning
Radial Chip Thinning
As the name states it only effects radial cuts
We have learned that Radial Chip Thinning takes effect when the cutter has less then 50% radial engagement with the work piece
This makes the chip thickness thinner then the calculated IPT
Ball Nose Chip Thinning
Is applied to Ball Nose cutters
Only effects the tool in relation to an axial cut when the tool is not at full depth of cut
This calculation can effect both speed and feed

## Slide 3: Review of concepts
Axial Cuts:
  Think of as Depth Cuts
  Pressure transferred to the Z axis
    Drilling is a good axial pressure application
  Less vibration with this cutting method
Axial
Radial

## Slide 4: The Ball Nose Trifecta
  Ball nose feed and speed adjustments can be confusing
  Ball Nose calculations consist of the following factors:
    Radial Chip Thinning Factor
      We have just learned about this calculation last week
    Axial Chip Thinning Factor
      As the axial depth decreases the calculated RPM should change because the diameter is now smaller
      As the axial depth decreases the calculated Depth of Cut also decreases, this will effect the feed

## Slide 5: Speed Adjustments
  When we calculate speed it is based on the diameter of the tool.
    RPM =(CS*3.82)/Diameter
    For this tool:
      CS- 800
      RPM= 3056
  With Ball Endmills we need to base it from the Effective Diameter (ED) of the tool
  Note the picture on the right. The diameter of the tool is 1” but the axial depth of cut is .125. This makes the ED smaller.
1” Dia
??? Dia
Cutting Tool Parameters:
-1” Dia, 2 Flute Ball EM
-CS-800
-IPT-.010
-Radial DOC-.020
-Axial DOC- .125

## Slide 6: Cordial Measurement
  To calculate the ED we will have to use a cordial calculation
    R= radius of cutter
    D= distance from chord to center of the cutter. To find this subtract the DOC from the radius of the tool
      R=.500
      D=.375
    When we put these values in the equation it gives us a ED of .663
1” Dia
??? Dia
Axial Depth of Cut is .125
R
D

## Slide 7: Speed Adjustments
  The ED RPM would be as follows
    RPM =(CS*3.82)/Diameter
    For this tool:
      CS- 800
      RPM= 4069
  You can see the change in RPM that is needed to maintain the proper cutting speed for the cutter
1” Dia
.663 Dia
Axial Depth of Cut is .125

## Slide 8: Axial Chip Thinning Factor (ACTF)
  Much like we learned about Radial Chip Thinning Axial Chip Thinning takes effect when the cutting tool is not engaged in the full axial cut
  The smaller the axial cut with a ball endmill the smaller the chip becomes
  Much like Radial Chip Thinning there is a chart for ACTF
Axial Depth of Cut is .125
Programmed IPT
Actual Chip Thickness

## Slide 9: Initial Feed Rate
  Initial Feed Rate:
    IPM= IPT* # of Flutes*RPM
    IPM= .010*2*3056
      IPM =61.1
  Feed Rate with RPM based from ED:
    IPM= .010*2*4069
      IPM=81.4
Programmed IPT
Actual Chip Thickness
Cutting Tool Parameters:
-1” Dia, 2 Flute Ball EM
-CS-800
-IPT-.010
-Radial DOC-.020
-Axial DOC- .125

## Slide 10: ACTF Chart

## Slide 11: Feed Rate W/Axial Chip Thinning Factor (ACTF)
  From the chart on the previous slide we can see at .125 DOC on a 1” Diameter the ACTF is .66
  To find the new IPT:
    IPT/ACTF
    .010/.66
      New IPT=.015
    IPM= .015*2*4069
      IPM=122.1
Programmed IPT
Actual Chip Thickness
Cutting Tool Parameters:
-1” Dia, 2 Flute Ball EM
-CS-800
IPT-.010
-Radial DOC-.020
-Axial DOC- .125

## Slide 12: The Final part of the Trifecta: RCTF
  We have found both new feed and speed based on the ACTF
  The last part of the ball nose calculations come from the RCTF
    We did this in the last lesson but there will be a slight twist on it
    The Radial DOC is: .020
Cutting Tool Parameters:
-1” Dia, 2 Flute Ball EM
-CS-800
IPT-.010
-Radial DOC-.020
-Axial DOC- .125
.010 IPT
Chip Thickness
.020 Radial Engagement

## Slide 13: The Radial Chip Thinning Factor

## Slide 14: The Final part of the Trifecta: RCTF
  When we look up the 1” diameter and .020 RDOC on the chart on the previous slide we get a factor of approximately .3
  Ball nose radial chip thinning calculation in not as simple as a normal Radial Chip Thinning calculation
  You must multiply the ACTF and the RCTF to get the new Feed Correction Factor (FCF)
    ACTF*RCTF=FCF
    .66*.3=.198 FCF
Cutting Tool Parameters:
-1” Dia, 2 Flute Ball EM
-CS-800
IPT-.010
-Radial DOC-.020
-Axial DOC- .125
.010 IPT
Chip Thickness
.020 Radial Engagement

## Slide 15: The Final part of the Trifecta: RCTF
  ACTF*RCTF=FCF
  .66*.3=.198 FCF
  To find the final feed rate we need to first find the new chip load
  .010/.198=.0505
  Note the final IPT is 5 times the original. Lets calculate the final feed rate:
    IPM= .0505*2*4069
      IPM=410.9
  Notice the very large increase in the final feed rate!
Cutting Tool Parameters:
-1” Dia, 2 Flute Ball EM
-CS-800
IPT-.010
-Radial DOC-.020
-Axial DOC- .125
.010 IPT
Chip Thickness
.020 Radial Engagement

## Slide 16: To Review
Three factors in Ball Nose Calculations:
Axial Chip Thinning Factor:
  Cutter Speed
  Axial DOC
Radial Chip Thinning Factor:
Feed Correction Factor takes into account both ACTF and RCTF
Initial Tool Data:
RPM=3056
IPM=61
Tool Data After ACTF:
RPM=4069
IPM=81
Tool Data with FCF:
RPM=4069
IPM=410.9