## Slide 1: PMT 330- 3-D CNC Milling
semi-finishing & Finishing Strategies

## Slide 2: Finishing
As we have previously learned some High Speed Toolpaths have the ability to rough and finish the part in one toolpath
This can not be done on all parts or toolpaths
When a single operation can not rough and finish the part extra operations like finish or semi-finish toolpaths may need to be added

## Slide 3: Semi-Finishing
Semi-Finishing is done when there is to much material after the roughing operation
Using a Semi-Finish operation allows the finish tool:
  Faster feeds and speeds
  More consistent surface finish
  Better tool life
Reasons for Semi-Finish:
  Part distorts after roughing
  To much material left for the finish tool
  Faster to add a third operation
In cases like this the material is to inconsistent for a finishing operation

## Slide 4: Finishing
Most surface finish tools have a ball shape
This allows any point of the tool to cut on the curved surface of the part, providing the radius of the tool is smaller then the radius of the part
Most finish toolpaths take .010 to .050 off

## Slide 5: Finishing
If a surface has a flat it may work better to use a bull endmill
The radius of the tool can cut the surfaces
The flat on the tool can cut flat surfaces with a large stepover then a ball endmill
  This will save cycle time and increase surface finish

## Slide 6: Cut Strategies
One Way
Cutting one way, in most cases climb milling, provide a more constant surface finish and tool life
Increases cycle time because of the retract and rapid to position across the part with every cut
Zig Zag
This back and forth motion changes from climb to conventional milling
Creates a less consistent surface finish which may require more polishing coming off the machine
The change in direction can also cause premature insert wear
Most common path used due to the savings in cycle time

## Slide 7: Tool Path Containment
If a part such as 330-1 is being finished we have two options:
  Contain the toolpath within the surface
    This keeps a consistent chip load
  Allow the toolpath to run off the surface
    This allows the very edge of the part to be machined

## Slide 8: Types of tools used
Solid Carbide
Solid Carbide can be used as a finish tool
These tools offer many styles and sizes as well as increases stiffness in the shank
The endmill does need to be replaced when the tool is dullCC

## Slide 9: Types of tools used
Replaceable Tip
Solid Carbide tips can be used as a finish tool
The same shank can use a flat, bull, or ball endmill
When dull these tools only need the tip replaced
May need a carbide dampened holder to reduce vibration

## Slide 10: Types of tools used
Ball Nose Replaceable Tip
Carbide 2 flute inserts can be placed in the holder
These are an excellent choice for finishing tools
Come in steel shank or carbide dampened when needed