## Slide 1: PMT 330- 3-D CNC Milling
Roughing Strategies w/3-D milling

## Slide 2: Roughing?
There are a number of strategies we will cover that will help improve tool life, surface finish , and increase feedrates while roughing
Sounds like a real losing situation!

## Slide 3: Roll In Technique
This is mainly used with shell/face mills
  This method should be used with any cutter entering the side of the part
The idea is not to shock the inserts on entry of the cut
By rolling into the cut the load is gradually picked up by the cutter
Roll in Techniques

## Slide 4: Dynamic Face Mill ToolPath
This tool path rolls into the cut
Dynamic toolpaths maintain engagement in the cut until the cut is done
This maintains the same surface finish thru out the cut
Can possibility eliminate the need for a finish pass, even with heavier DOC
Dynamic Face Milling

## Slide 5: Entering A Pocket
Ramping
Ramping is a common method to enter a pocket
This avoids plunging the tool which creates tool pressure and poor chip evacuation
Helix and Linear Ramps are often used
Most parameters can be manually controlled with ramping
Note that parameters like radius size, clearances from walls, and plunge angles can all be controlled in the CAM system

## Slide 6: Entering A Pocket
Ramping
Most insertable cutters used are not center cutting
These tools can still ramp as long as the plunge angle is less then 3°
When helical ramping the radius must be large enough to inserts pass through the center of the cut
Note that the cutter above is not center cutting

## Slide 7: Milling a Slot
Linear Move
Traditionally done to mill a slot
May take 2-4 depth cuts
Needs finish passes to finish walls of slot
Unpredictable tool life
Peel Milling
Utilizes low radial engagement with large axial engagement
Can often rough and finish a slot in one pass
Very predictable tool life

## Slide 8: Milling a Slot
Peel Milling
Toolpath is programmed to arc into cut
Then cuts linearly across the slot
Arcs out of the cut
Can be programmed with a z micro lift to tool does not rub as it rapids across the part to enter the cut again

## Slide 9: Avoiding Radial Burial
Trochoidal Cuts
When entering corners full radial engagement happens
This causes stress on the endmill
  Reduces tool life
  Increase spindle load
  Increased chatter
Trochoidal cuts can be used to “loop” into a corner or radius
Entering a corner can double a tools radial engagement

## Slide 10: Round Vs Square Inserts
Square Inserts
Square insert cutting tools are a versatile tool
There are many insert choices for these cutters
These cutters can mill the wall of a very tall part
The draw back in roughing the surface of a part is the 90° shoulder leaves a large variation in the material on the part
  This may mean the is a need for a semi-finish pass before the finish tool can be used
Surface to be machined
Depending on where the DOC is set radially or axially there is still a large change is material left on the part because of the square shoulder

## Slide 11: Round Vs Square Inserts
Round Inserts
Stronger geometry
Creates more cutting force
Less insert choices
Can rough the part closer to the finish size due their round geometry
  This may eliminate the need for a semi-finish pass
Surface to be machined
Round inserts can rough a part closer to the finish dimension with less variation of the stock left on the part

## Slide 12: Entry Angle of Insert
As covered previously there are three entry angles
  Positive
  Neutral
  Negative
Cutter Position

## Slide 13: Insert Entry Angles
Three insert entry angles
  Positive
  Neutral
  Negative
Not the picture on the right
  The cutter’s radial engagement is at less then 50% of the tool
  This means the insert enters with a positive rake angle
    This the entry angle we want to always try and maintain
Positive Entry Attributes:
  Creates very little vibration/shock
  Edge of insert contacts part before the face
  Chips are cut rather then sheared from the part
  Less pressure means faster speeds, feeds, better tool life, less horsepower consumption