## Slide 1: PMT 330- 3-D CNC Milling
High Speed Machining

## Slide 2: What is High Speed Machining?
There is no real definition of High Speed Machining (HSM)
Every shop has a different definition of HSM
In this lecture we will explore some of those different definitions

## Slide 3: High Speed Machining Concepts
High RPM
The main concept of HSM is high material removal rates while maintaining good surface finish
HSM typically has a starting RPM of 10,000 and goes up to 40,000 RPM Spindles
This requires the use of balanced tool holders and tooling

## Slide 4: High Speed Machining
Small Radial Stepover
Reduced Radial step over is another common theme
Generally HSM utilizes 10-20% of tool diameter as the step over
This radial cut allows for larger axial cuts, utilizing more of the flute length
High Speed Machining Concepts

## Slide 5: High Speed Machining
Maintaining Engagement
The cutter should be engaged in the cut as long as possible
Entering and Exiting the cut are the hardest part of the cut for the tool
Engagement concept one:
  This is for materials like aluminum and mild steel
High Speed Machining Concepts

## Slide 6: High Speed Machining
Reducing Stress/Heat
When parts are extremely hard(55-60 RC) or produced a lot of heat
The idea is to move in and out of the cut very fast so heat and stress can not build up and have a negative effect on the tool
High Speed Machining Concepts
HSM Strategies

## Slide 7: High Speed Machining
Smaller Diameter Tools
Smaller tools are usually used with HSM, as a general rule 1” diameter of smaller
These tools replace the larger, slower, hogging style tooling
These tools are easier to balance
When material removal rates are calculated tools with higher RPM, higher feedrates and lighter depth of cut will out preform a slower larger diameter tool
High Speed Machining Concepts

## Slide 8: High Speed Machining
Combining Cuts
True HSM toolpaths combine both roughing and finishing cuts
This can be done because of the lighter DOC and increased SFM
HSM can happen at lower RPM’s but toolpaths may needed to be added
HSM can happen at lower RPM’s but toolpaths may needed to be added
  Example:
  A spindle with 30000 RPM many be able to combine Rough, Semi-finish, Finish tool paths all in one cut
  A Spindle with 15,000 RPM may need a Rough and Finish Pass
  A spindle with 8,000 RPM may need a Rough, Semi-Finish, and Finish tool path
    This does not mean that HSM techniques can’t be applied to these toolpaths as well
High Speed Machining Concepts

## Slide 9: High Speed Machining
Radial chip thinning is used to help with feed rate adjustments because of the smaller RDOC
Since HSM is used on many 3-D parts ball nose chip thinning is also commonly used with HSM
These concepts help us achieve the feedrates we are trying to achieve with HSM
High Speed Machining Concepts

## Slide 10: Programming Considerations
Tools don’t respond well to full radial engagement in a corner
This is made worse with high feeds and speeds in HSM
Toolpaths should be programmed to avoided full radial engagement
Entering a corner can double a tools radial engagement

## Slide 11: Ways to Avoid Corners
MasterCam uses dynamic toolpaths that help with high speed corner avoidance
These toolpath options that are commonly used are Trochoidal milling or peel milling
Note how the toolpath on the right has many sharp corners while the toolpath on the left uses looping paths to avoid burying the cutter in material
Trochodial Milling

## Slide 12: Machine Considerations
In order for this to all work the machine tool must be able to preform these tasks
The control must be able to read the code as fast the feedrate wants to travel
If the machine can not read and interpret the code fast enough a slow down or stutter will happen
The graphic on the left shows the cutter machining into a sharp corner. The 120-degree change in vector direction in one block of code causes the machine to slow down dramatically. If the cutter can interpolate a more gradual change in direction, it will result in a noticeable reduction in cycle time.

## Slide 13: Machine Considerations
HSM is often a control option that can be added on
This allows the machine to “look ahead” in the program and anticipate what is happening in the program
If a machine tool has a standard look ahead of 100 lines the HSM option may have a look ahead of 1000 lines
The graphic on the left shows the cutter machining into a sharp corner. The 120-degree change in vector direction in one block of code causes the machine to slow down dramatically. If the cutter can interpolate a more gradual change in direction, it will result in a noticeable reduction in cycle time.