## Slide 1: ICS Security Zoning
Made possible through support from the National Science Foundation (NSF) award number 1800929

## Slide 2: Objectives
Discuss the concept of network zoning using the Purdue Model.
Learn how to create network zones using segmentation.
Demonstrate how hackers can take advantage of improperly segmented networks and intercept secure communications.
Demonstrate how network segmentation restricts a hacker’s ability to intercept secure communications.

## Slide 3: Purdue Model
Purdue Enterprise Reference Architecture (PERA)
  Part of ICS99 – Industrial Automation and Control Systems Security
Separates systems into four zones and six levels

## Slide 4: Purdue Model
Enterprise Security Zone
Manufacturing Zone
Industrial Demilitarized Zone
Cell/Area Zone

## Slide 5: Purdue Model
Enterprise Security Zone
  Levels 4 and 5
  Contains traditional IT services (Email, Enterprise Resource Planning (ERP), File Sharing, etc)
Enterprise Security Zone

## Slide 6: Purdue Model
Industrial Demilitarized Zone
  Sits between levels 3 and 4
  This zone provides common services needed by both traditional IT and industrial systems (databases, web servers, etc)
  This zone contains security devices such as firewalls
Industrial Demilitarized Zone

## Slide 7: Purdue Model
Manufacturing Zone
  Contains level 3
  This zone houses systems such as historians, OPC servers and engineering workstations
Manufacturing Zone

## Slide 8: Purdue Model
Cell/area Zone
  Contains levels 0, 1 and 2
  This zone contains operator HMI devices, PLCs, sensors and electrical controls
Cell/Area Zone

## Slide 9: Network Segmentation
Network segmentation occurs when a computer network is split into multiple subnets or segments
Network segmentation can be done by physically separating a large network into smaller subnetworks
Single Network
Subnet
Subnet
Subnet

## Slide 10: Network Segmentation
Network segmentation can be done by logically separating a large network into smaller subnetworks using virtual LANs (VLANs)
Single Network
Subnet
Subnet
Subnet

## Slide 11: Network Segmentation
Devices that exist on the same network segment CAN see one another's traffic potentially allowing a hacker to access sensitive data
Data
Single Network Segment
Yeah!

## Slide 12: Network Segmentation
Devices that exist on different network segments CANNOT see one another's traffic blocking a hacker’s ability to access sensitive data
Network Segment B
Data
Network Segment A
??????

## Slide 13: For More Information
For further information go to https://www.nl.northweststate.edu/camo or contact:
  Tony Hills – thills@northweststate.edu – 419-267-1354
  Mike Kwiatkowski – mkwiatkowski@northweststate.edu – 419-267-1231
Made possible through support from the National Science Foundation (NSF) award number 1800929