## Slide 1: Introduction to Semiconductor Materials
A presentation of eSyst.org
Louis E. Frenzel
Notes: <number>

## Slide 2: Summary
A presentation of eSyst.org
Course use: DC circuits and/or AC circuits. Semiconductor devices or solid state courses. In-class presentation.
Objective: To provide an early introduction to semiconductor devices prior to a formal course to reinforce their importance and their total dominance of electronics hardware.
Content: Defines semiconductors and shows basic atomic structures. Summarizes types of semiconductor materials. Introduces PN junctions and diodes. Gives an overview of the concept of a transistor and how it is used in electronics. A brief introduction to integrated circuits.
Notes: <number>

## Slide 3: Prerequisites
A presentation of eSyst.org
To understand this presentation, you should have the following prior knowledge:
  Draw the structure of an atom, including electrons, protons, and neutrons.
  Define resistance and conductance.
  Label an electronic schematic, indicating current flow.
  Define Ohm’s and Kirchhoff’s laws.
  Describe the characteristics of DC and AC (sine wave) voltages.
Notes: <number>

## Slide 4: Student Learning Outcomes
A presentation of eSyst.org
Upon completion of viewing this presentation, you should be able to:
  Define conductor, insulator and semiconductor, and state the resistance or conductance of each.
  Name at least three semiconductor materials and state the most widely used.
  Name the basic structure of material and explain how it is formed with atoms.
  Define doping and name the two types of semiconductor material formed with doping.
  Name the current carriers in N and P-type material.
  Explain how current flows in semiconductor material.
Notes: <number>

## Slide 5: Electronic Materials
A presentation of eSyst.org
The goal of electronic materials is to generate and control the flow of an electrical current.
Electronic materials include:
  Conductors: have low resistance which allows electrical current flow
  Insulators: have high resistance which suppresses electrical current flow
  Semiconductors: can allow or suppress electrical current flow
Notes: <number>

## Slide 6: Conductors
A presentation of eSyst.org
Good conductors have low resistance so electrons flow through them with ease.
Best element conductors include:
  Copper, silver, gold, aluminum, & nickel
Alloys are also good conductors:
  Brass & steel
Good conductors can also be liquid:
  Salt water
Notes: <number>

## Slide 7: Conductor Atomic Structure
A presentation of eSyst.org
The atomic structure of good conductors usually includes only one electron in their outer shell.
  It is called a valence electron.
  It is easily striped from the atom, producing current flow.
Copper Atom
Notes: <number>

## Slide 8: Insulators
A presentation of eSyst.org
Insulators have a high resistance so current does not flow in them.
Good insulators include:
  Glass, ceramic, plastics, & wood
Most insulators are compounds of several elements.
The atoms are tightly bound to one another so electrons are difficult to strip away for current flow.
Notes: <number>

## Slide 9: Semiconductors
A presentation of eSyst.org
Semiconductors are materials that essentially can be conditioned to act as good conductors, or good insulators, or any thing in between.
Common elements such as carbon, silicon, and germanium are semiconductors.
Silicon is the best and most widely used semiconductor.
Notes: <number>

## Slide 10: Semiconductor Valence Orbit
A presentation of eSyst.org
The main characteristic of a semiconductor element is that it has four electrons in its outer or valence orbit.
Notes: <number>

## Slide 11: Crystal Lattice Structure
A presentation of eSyst.org
The unique capability of semiconductor atoms is their ability to link together to form a physical structure called a crystal lattice.
The atoms link together with one another sharing their outer electrons.
These links are called covalent bonds.
2D Crystal Lattice Structure
Notes: <number>

## Slide 12: 3D Crystal Lattice Structure
A presentation of eSyst.org
Notes: <number>

## Slide 13: Semiconductors can be Insulators
A presentation of eSyst.org
If the material is pure semiconductor material like silicon, the crystal lattice structure forms an excellent insulator since all the atoms are bound to one another and are not free for current flow.
Good insulating semiconductor material is referred to as intrinsic.
Since the outer valence electrons of each atom are tightly bound together with one another, the electrons are difficult to dislodge for current flow.
Silicon in this form is a great insulator.
Semiconductor material is often used as an insulator.
Notes: <number>

## Slide 14: Doping
A presentation of eSyst.org
To make the semiconductor conduct electricity, other atoms called impurities must be added.
“Impurities” are different elements.
This process is called doping.
Notes: <number>

## Slide 15: Semiconductors can be Conductors
A presentation of eSyst.org
An impurity, or element like arsenic, has 5 valence electrons.
Adding arsenic (doping) will allow four of the arsenic valence electrons to bond with the neighboring silicon atoms.
The one electron left over for each arsenic atom becomes available to conduct current flow.
Notes: <number>

## Slide 16: Resistance Effects of Doping
A presentation of eSyst.org
If you use lots of arsenic atoms for doping, there will be lots of extra electrons so the resistance of the material will be low and current will flow freely.
If you use only a few boron atoms, there will be fewer free electrons so the resistance will be high and less current will flow.
By controlling the doping amount, virtually any resistance can be achieved.
Notes: <number>

## Slide 17: Another Way to Dope
A presentation of eSyst.org
You can also dope a semiconductor material with an atom such as boron that has only 3 valence electrons.
The 3 electrons in the outer orbit do form covalent bonds with its neighboring semiconductor atoms as before. But one atom is missing from the bond.
This place where a fourth electron should be is referred to as a hole.
The hole assumes a positive charge so it can attract electrons from some other source.
Holes become a type of current carrier like the electron to support current flow.
Notes: <number>

## Slide 18: Types of Semiconductor Materials
A presentation of eSyst.org
The silicon doped with extra electrons is called an “N type” semiconductor.
  “N” is for negative, which is the charge of an electron.
Silicon doped with material missing electrons that produce locations called holes is called “P type” semiconductor.
  “P” is for positive, which is the charge of a hole.
Notes: <number>

## Slide 19: Current Flow in N-type Semiconductors
A presentation of eSyst.org
The DC voltage source has a positive terminal that attracts the free electrons in the semiconductor and pulls them away from their atoms leaving the atoms charged positively.
Electrons from the negative terminal of the supply enter the semiconductor material and are attracted by the positive charge of the atoms missing one of their electrons.
Current (electrons) flows from the positive terminal to the negative terminal.
Notes: <number>

## Slide 20: Current Flow in P-type Semiconductors
A presentation of eSyst.org
Electrons from the negative supply terminal are attracted to the positive holes and fill them.
The positive terminal of the supply pulls the electrons from the holes leaving the holes to attract more electrons.
Current (electrons) flows from the negative terminal to the positive terminal.
Inside the semiconductor current flow is actually by the movement of the holes from positive to negative.
Notes: <number>

## Slide 21: In Summary
A presentation of eSyst.org
In its pure state, semiconductor material is an excellent insulator.
The commonly used semiconductor material is silicon.
Semiconductor materials can be doped with other atoms to add or subtract electrons.
An N-type semiconductor material has extra electrons.
A P-type semiconductor material has a shortage of electrons with vacancies called holes.
The heavier the doping, the greater the conductivity or the lower the resistance.
By controlling the doping of silicon the semiconductor material can be made as conductive as desired.
Notes: <number>