## Slide 1: An Electronic System Power Supply Example
A presentation of eSyst.org
Louis E. Frenzel
Notes: <number>

## Slide 2: Summary
A presentation of eSyst.org
Course use: DC circuits and/or AC circuits. Semiconductor devices or solid state courses. In-class presentation.
Objective: To provide an example of a full system in early courses to show the relevance of the theory and circuits to real equipment.
Content: Every piece of electronic equipment has a power supply and that power supply is a key sub-system in every other product or system. Typical examples are given in block diagram form. All major components and circuits are identified and explained.
Notes: <number>

## Slide 3: Prerequisites
A presentation of eSyst.org
To understand this presentation, you should have the following prior knowledge:
  Draw the structure of an atom, including electrons, protons, and neutrons.
  Define resistance and conductance.
  Label an electronic schematic, indicating current flow.
  Define Ohm’s and Kirchhoff’s laws.
  Describe the characteristics of DC and AC (sine wave) voltages.
Notes: <number>

## Slide 4: Student Learning Outcomes
A presentation of eSyst.org
Upon completion of viewing this presentation, you should be able to:
  Define power supply.
  Name the main components in a common linear AC to DC power supply and explain the purpose and function of each.
  Define rectifier and name two common types.
  Name the component that transforms pulsating DC into constant DC.
  Define ripple and identify its origins.
Notes: <number>

## Slide 5: Power Supply
A presentation of eSyst.org
All electronic circuits need a power source to work.
For electronic circuits made up of transistors and/or ICs, this power source must be a DC voltage of a specific value.
A battery is a common DC voltage source for some types of electronic equipment especially portables like cell phones and iPods.
Most non-portable equipment uses power supplies that operate from the AC power line but produce one or more DC outputs.
Notes: <number>

## Slide 6: Power Supply Characteristics
A presentation of eSyst.org
The input is the 120 volt 60 Hz AC power line. Alternately, the input may be 240 volt AC.
The power supply converts the AC into DC and provides one or more DC output voltages.
Some modern electronic circuits need two or more different voltages.
Common voltages are 48, 24, 15, 12, 9, 5, 3.3, 2.5, 1.8, 1.5, 1.2 and 1 volts.
A good example of a modern power supply is the one inside a PC that furnishes 12, 5, 3.3 and 1.2 volts.
Notes: <number>

## Slide 7: Components of a Power Supply
A presentation of eSyst.org
Main circuits in most power supplies.
Notes: <number>

## Slide 8: Power Supply
A presentation of eSyst.org
The AC line is first passed through a low pass filter of the form.
This eliminates noise on the AC line from bothering the power supply circuits and prevents unwanted signals from the power supply from being transferred back into the AC line where they might interfere with other equipment.
Notes: <number>

## Slide 9: Transformer
A presentation of eSyst.org
A transformer is commonly used to step the input AC voltage level down or up. Most electronic circuits operate from voltages lower than the AC line voltage so the transformer normally steps the voltage down by its turns ratio to a desired lower level.
For example, a transformer with a turns ratio of 10 to 1 would convert the 120 volt 60 Hz input sine wave into a 10 volt sine wave.
Notes: <number>

## Slide 10: Rectifier
A presentation of eSyst.org
The rectifier converts the AC sine wave into a pulsating DC wave.
There are several forms of rectifiers used but all are made up of diodes.
Rectifier types and operation will be covered later.
Notes: <number>

## Slide 11: Filter
A presentation of eSyst.org
The rectifier produces a DC output but it is pulsating rather than a constant steady value over time like that from a battery.
A filter is used to remove the pulsations and create a constant output.
The most common filter is a large capacitor.
Notes: <number>

## Slide 12: Regulator
A presentation of eSyst.org
The regulator is a circuit that helps maintain a fixed or constant output voltage.
Changes in the load or the AC line voltage will cause the output voltage to vary.
Most electronic circuits cannot withstand the variations since they are designed to work properly with a fixed voltage.
The regulator fixes the output voltage to the desired level then maintains that value despite any output or input variations.
Notes: <number>

## Slide 13: DC-DC Converter
A presentation of eSyst.org
Most modern power supplies also contain one or more DC-DC converters
Modern electronics often demand different voltages to function.
A DC-DC converter changes one DC voltage to another, higher or lower DC voltage.
A DC-DC converter is used with a power supply to prevent the need for a second AC-DC supply.
Notes: <number>

## Slide 14: How Rectifiers Work
A presentation of eSyst.org
The simplest form of rectifier is the half wave rectifier shown.
Only the transformer, rectifier diode, and load (RL) are shown without the filter and other components.
The half wave rectifier produces one sine pulse for each cycle of the input sine wave.
When the sine wave goes positive, the anode of the diode goes positive causing the diode to be forward biased. The diode conducts and acts like a closed switch letting the positive pulse of the sine wave to appear across the load resistor.
Notes: <number>

## Slide 15: How Rectifiers Work (continued)
A presentation of eSyst.org
When the sine wave goes negative, the diode anode will be negative so the diode will be reverse biased and no current will flow.
No negative voltage will appear across the load. The load voltage will be zero during the time of the negative half cycle.
See the waveforms that show the positive pulses across the load. These pulses need to be converted to a constant DC.
Notes: <number>

## Slide 16: Bridge Rectifier
A presentation of eSyst.org
Another widely used rectifier is the bridge rectifier. It uses four diodes.
This is called a full wave rectifier as it produces an output pulse for each half cycle of the input sine wave.
On the positive half cycle of the input sine wave, diodes D1 and D2 are forward biased so act as closed switches appearing in series with the load.
On the negative half cycle, diode D1 and D2 are reverse biased and diodes D3 and D4 are forward biased so current flows through the load in the same direction.
Notes: <number>

## Slide 17: How the Filter Works
A presentation of eSyst.org
A large capacitor is connected across the load resistor. This capacitor filters the pulses into a more constant DC.
When the diode conducts, the capacitor charges up to the peak of the sine wave.
Then when the sine voltage drops, the charge on the capacitor remains. Since the capacitor is large it forms a long time constant with the load resistor. The capacitor slowly discharges into the load maintaining a more constant output.
The next positive pulse comes along recharging the capacitor and the process continues.
Notes: <number>

## Slide 18: Ripple
A presentation of eSyst.org
The capacitor does a good job of smoothing the pulses from the rectifier into a more constant DC.
A small variation occurs in the DC because the capacitor discharges a small amount between the positive and negative pulses. Then it recharges. This variation is called ripple.
The ripple can be reduced further by making the capacitor larger.
The ripple appears to be a sawtooth shaped AC variation riding on the DC output.
A small amount of ripple can be tolerated in some circuits but the lower the better overall.
Notes: <number>

## Slide 19: The Regulator
A presentation of eSyst.org
Most regulators are ICs .
These are feedback control circuits that actually monitor the output voltage to detect variations.
If the output varies, for whatever reason, the regulator circuit automatically adjusts the output back to the set value.
Regulators hold the output to the desired value.
Since ripple represents changes in the output, the regulator also compensates for these variations producing a near constant DC output.
Notes: <number>

## Slide 20: In Summary
A presentation of eSyst.org
All electronic circuits and equipment need a power supply, usually one that supplies are very specific DC voltage.
A battery is a near perfect DC supply but it is used mainly in portable applications.
Most equipment uses an AC to DC power supply.
In most AC to DC supplies, the 120 volt AC line is first filtered then stepped up or down to the desired voltage level then rectified into pulsating DC, then filtered to a constant DC. A regulator holds the output to a desired level. A DC-DC converter may also be used to generate another DC voltage.
The two most common rectifiers are the single diode half wave rectifier and the four diode full wave bridge rectifier.
Notes: <number>