## Slide 1: Introduction to Bluetooth Wireless Louis Frenzel
Notes: <number>

## Slide 2: Introduction to the Demonstration
This presentation is an overview of Bluetooth, a short-range wireless technology.
Bluetooth is one of the most widely used wireless systems in use today.
Bluetooth was developed by the Ericsson company in the late 1990s.
Bluetooth is a good example of the many ways that wireless can be used.
Bluetooth is sometimes categorized as a cable replacement.
A presentation of eSyst.org
Notes: <number>

## Slide 3: Introduction to Bluetooth
Bluetooth (BT) is a short-range wireless technology designed for low speed data applications.
The main application of BT today is as a wireless link between a cell phone and a headset.
Bluetooth is a standard maintained by the Bluetooth Special Interest Group (SIG).
Bluetooth is also an IEEE standard designated 802.15.1.
A presentation of eSyst.org
Notes: <number>

## Slide 4: Bluetooth Specifications
BT operates in the unlicensed 2.4 to 2.4835 GHz band.
The basic BT version 1.2 has a maximum data rate of 1 Mbps with a total throughput of 723 kbps.
BT uses frequency hopping spread spectrum where the transmit and receive frequency changes in a random pattern 1600 time per second over 79 defined channels.
A presentation of eSyst.org
Notes: <number>

## Slide 5: Spread Spectrum Primer
Spread spectrum (SS) is a wireless technique that allows hundreds of individual signals to occupy the same bandwidth simultaneously.
There are two major forms of SS, direct sequence (DS) and frequency hopping (FH). Only FHSS will be discussed here.
Because the transmit/receive (Tx/Rx) frequency changes very quickly from one random frequency to the next, individual signals from other BT radios with different hop patterns effectively do not interfere with one another. The presence of multiple other signals simply appears as low level noise to any receiver monitoring the bandwidth.
A presentation of eSyst.org
Notes: <number>

## Slide 6: Spread Spectrum (continued)
FHSS radios can operate within a bandwidth along with other signals without interference from them or causing interference to them.
Because the FH scheme is random it cannot be easily duplicated thereby providing a method of security for the data transmitted.
A presentation of eSyst.org
Notes: <number>

## Slide 7: More Bluetooth Specifications
The BT FHSS scheme causes the Tx/Rx frequency to change 1600 times per second over 79 different frequencies spaced 1 MHz apart between 2.4 and 2.4835 GHz.
During the interval between hops (625 µs), data is transmitted at a 1 Mbps rate. With each bit interval being 1 µs, a total of 625 bits of data are transmitted.
The data to transmitted is assembled into packets with the format shown in Fig. 1 (see next slide).
The modulation is GFSK or Gaussian frequency shift keying. The binary pulses are shaped by a Gaussian response low pass filter to minimize sidebands and the transmission bandwidth.
A presentation of eSyst.org
Notes: <number>

## Slide 8: Figure 1 Bluetooth Packet

## Slide 9: Bluetooth Power Levels
Bluetooth signals can be transmitted at one of three power levels.
  Class 1 power is 20 dBm or 100 mW.
  Class 2 power is 4 dBm or 25 mW.
  Class 3 power is 0 dBm or 1 mW.
Most BT radios operate at the 4 dBm level.
Class 1 BT radios usually require an external power amplifier (PA) chip.
A presentation of eSyst.org
Notes: <number>

## Slide 10: Transmission Range
Class 3 BT radios with 0 dBm power have a typical maximum range of 1 meter or about 3.2 feet.
Class 2 BT radios extend this range up to about 10 meters or roughly 33 feet.
Class 1 BT radios have a maximum range of about 100 meters or 300 feet.
All ranges are assumed to be a clear line of sight path. Any obstacles (walls, trees, etc) will shorten the range.
A presentation of eSyst.org
Notes: <number>

## Slide 11: Bluetooth Version 2.1
A later version of the BT standard boosts the data rate to 3 Mbps with a throughput of 2.1 Mbps.
This version of the BT standard is called enhanced data rate (EDR).
It uses a form of phase shift keying (PSK) modulation so that more bits are transmitted per transmit symbol period (baud).
For a data rate to 2 Mbps the modulation is /4-DQPSK for 2 bits per baud. For 3 Mbps the modulation is 8DPSK for 3 bits per baud.
A presentation of eSyst.org
Notes: <number>

## Slide 12: Relationship Between Data Rate and Bandwidth
The binary data rate of a system is determined by the bandwidth (BW) of the channel and the amount of noise present.
Assuming minimal noise, the data rate is roughly proportional to BW.
The goal in communications is to achieve maximum data rate for a given channel BW. This is known as spectral efficiency.
The measure of spectral efficiency is bits per Hertz or bits/Hz.
The number of bits/Hz is a function the type of modulation.
A presentation of eSyst.org
Notes: <number>

## Slide 13: Spectral Efficiency
As a general rule, for basic modulation types like FSK or BPSK or their derivatives, you can transmit roughly 1 bit/ 1 Hz.
For a 1 MHz Bluetooth channel BW, the data rate is 1 Mb/s using GFSK.
To achieve higher data rates in the same 1 MHz BW Bluetooth channel more efficient modulation methods must be used.
Bluetooth switches from GFSK to variations of phase shift keying (PSK) to double or triple the data rate.
A presentation of eSyst.org
Notes: <number>

## Slide 14: Symbol Rate
Symbol rate is also known as baud rate.
In GFSK, two frequencies are used to represent 0 and 1. Each frequency is a “symbol”.
With two symbols, two bits can be represented.
In basic binary PSK different phase shifts are used to represent the bits, 0º represents binary 0 and 180º represents binary 1.
We usually show this in the form of a constellation diagram. See Fig. 2 (see next slide).
BPSK produces a spectral efficiency of 1 bit/ Hz like GFSK.
In both GFSK and BPSK, the bit rate is the same as the symbol rate. In Bluetooth the symbols are changing at a 1 MHz rate.
A presentation of eSyst.org
Notes: <number>

## Slide 15: Figure 2 BPSK

## Slide 16: Quardature Phase Shift Keying (QPSK)
QPSK is a technique for doubling the data rate but keeping the symbol rate the same.
QPSK generates two sine waves at the carrier frequency but shifted by 90º. These are added together to form the final signal. The result is a scheme that generates 2 bits/Hz. The symbol rate stays at 1 MHz but the data rate doubles to 2 Mb/s. 2-bit per baud.
One way of showing QPSK is with a constellation diagram like that in Fig. 3 (see next slide).
Each phasor represents a carrier sine wave. The length of the phasor is its amplitude in power and the angle represents the phase shift from some reference.
With four different phase shifts means that you can represent 2 bits for each phase.
The symbol rate remains at 1 MHz but with 2 bits represented with each of four phase shifts, the data rate is 2 Mb/s.
A presentation of eSyst.org
Notes: <number>

## Slide 17: Figure 3 /4 - DQPSK

## Slide 18: /4-DQPSK
The /4 designation means a 45º phase shift from zero reference.
This produces phasors at +45, +135, -45 and -135 degrees.
The D means differential which refers to how the signal is demodulated. It compares the phase of the currently received symbol with the previous symbol to resolve which bit pair is being transmitted.
A presentation of eSyst.org
Notes: <number>

## Slide 19: 8DPSK
To achieve the 3 Mb/s data rate in a 1 MHz Bluetooth channel, 8-DPSK modulation is used.
The 8 refers to the use of eight different phase shift values.
Each phase shift represents a 3-bit code.
The constellation diagram is shown in Fig. 4 (see next slide).
Each phasor is shifted 45º from the next.
The symbol rate is still1 MHz but with 8 different phase shifts, the data rate triples to 3 Mb/s.
The spectral efficiency is 3 bits/Hz or 3-bits per baud.
A presentation of eSyst.org
Notes: <number>

## Slide 20: Figure 4 8 - DPSK

## Slide 21: Other Bluetooth Versions
An even higher speed version of BT is Version 3.0 + HS. It uses an IEEE 802.11 standard (Wi-Fi) radio carrying the BT protocol to achieve 24 Mbps data rate.
An ultra lower energy version 4.0 of BT reduces power consumption to a very low level meaning that it is ideal for battery powered devices and can provide a long battery life.
A presentation of eSyst.org
Notes: <number>

## Slide 22: Bluetooth Networks
Two BT radios can find one another if they are within range and will “pair” with one another. This is called a peer-to-peer connection.
BT radios can also form small networks called piconets.
A piconet allows 7 BT radios to talk to one another in a master-slave relationship. Fig. 5 (see next slide). One BT radio serves as a master controller that manages all connections between other radios.
A piconet can connect to another piconet to form a larger scatter net between master transceivers.
A presentation of eSyst.org
Notes: <number>

## Slide 23: Figure 5 Bluetooth Piconet

## Slide 24: Bluetooth Hardware
Bluetooth radios come as a single IC chip.
All radio functions are fully integrated.
Most chips are only a few millimeters in width and depth. See Figure 6 (see next slide).
Many BT chips also incorporate an FM radio and a GPS receiver for navigation.
The only external components usually needed are an antenna, a battery, a power bypass capacitor, and a PA for Class 1.
Most BT chips cost less than $3 each but less in high volume.
A presentation of eSyst.org
Notes: <number>

## Slide 25: Figure 6 New Features for Bluetooth Chip
A presentation of eSyst.org
Notes: <number>

## Slide 26: Bluetooth Profiles
BT can be used to build an almost infinite number of specific applications.
Some of the more common applications are defined by software. This software is known as profiles that describe the behavior of the BT radios.
The most popular profiles are:
  Audio distribution in audio/stereo/hi-fi music systems.
  Cell phone headsets
  Wireless printer connections
  Human interface devices (HIDs) like mouse and keyboard.
  Hands-free profile for in-vehicle use.
A presentation of eSyst.org
Notes: <number>