## Slide 1
NanoScience and Nanotechnology

## Slide 2: NanoScience and Nanotechnology: How the Smallest Building Blocks are Impacting Life Today and Tomorrow
Dr. Allen Kimel, Assistant Professor
Materials Science and Engineering
Pennsylvania State University

## Slide 3: Overview
What is Materials Science and Engineering
  What is a material
  Engineering versus Science
  Example – Turkey Timer
Impact now and in the Future
  Interest in Nanotechnology
  Making materials small generates big changes
  Products
  Research
Questions

## Slide 4: Ceramics in General
Bond metal to a non-metal
Ionic and covalent bonding
High stiffness with no toughness
Insulators
High temperature and chemical resistivity

## Slide 5: Metals in General
Metallic bonding – sharing of electrons
Alloyed with addition of other elements
High strength, tough/ductile
Can engineer stiffness and toughness through both atomistic and microstructural manipulations
Conductors

## Slide 6: Polymers in General
Long carbon chains (does not have to be carbon)
Covalent bonds within chains with covalent and van der Waals bonds between chains
Low stiffness and high ductility/toughness
Low temperature
Performance highly dependent on molecular weight and degree of crystallinity

## Slide 7: THE MATERIALS’ SCIENCE TETRAHEDRON
chemistry, thermodynamics,
kinetics, transport phenomena
crystallography, electron and x-ray diffraction, analytical methods
solid state physics, optics, electromagnetics, mechanical properties, chemical stability, etc.
Application

## Slide 8: Engineering versus Science
Engineering answers the question how
Science answers the question why
Example: creation of a hard surface to use to hit an object (hammer, golf club, tennis racket, etc.)
Engineering chooses a metal and develops a setup to generate power
Science asks what can we change within the components of the engineered system to exact improved properties for better performance

## Slide 9: Turkey Day Materials Science
Element | Field’s Metal Weight % | Turkey Timer Weight %
Bismuth (Bi) | 32.5 | 32.5
Indium (In) | 51 | 18.7
Tin (Sn) | 16.5 | 48.5
Melting Point Celsius (F) | 62 (144) | 85 (185)

## Slide 10: Nanoscience and Nanotechnology
Nano: 10-9 meters or 0.000000001 meters
Essentially any material with a defining property determined by a structure at the nanometer scale
Working definition for materials science and engineering is 0.1 – 100 nanometers

## Slide 11
What Makes Nanotechnology Development and Education Challenging and Exciting?
It’s cross disciplinary!
Physics
Chemistry
Biology
Engineering
Agriculture
Medicine
Nanotechnology
New products and services
Education
Business
Psychology
Sociology
Philosophy

## Slide 12: Large Effects of Smallness
Nanoparticles: as you DECREASE the diameter of the particles you INCREASE the surface area. (you can get a lot more particles into the same fixed volume of space
Left jar contains 3000 marbles 5/8”in diameter
Right jar contains 5000 marbles ½” in diameter
A reduction of 20% created a gain of 2000 marbles

## Slide 13: Large Effects of Smallness
Sometimes we are just interested in making really small particles
Here quantum dots of cadmium selenide (CdSe) are used to create an array of colors

## Slide 14: Large Effects of Smallness
Surface area: amount of surface available for chemical reaction
“traditional” ceramic powders are typically around 1 to 10 micrometers in size
Surface area of <1 m2/g
These ceramic particles are around 8 nanometers in size
A reduction of ~1000 times in size
Surface area of ~130 m2/g
What does that mean physically?
A one centimeter cube full of this 8nm particle size powder would have an equivalent surface area of ~1400 sq ft.!
1cm = 0.40 inches

## Slide 15: A Little History
Nanotechnology has been around for a long time – 2000 years ago nano-gold particles were used in coloring of glass
The left picture shows the array of colors possible with gold nanoparticles

## Slide 16: Career Pathways
Business
Communications
Human Services
Engineering and Industrial
Science

## Slide 17: Making Things Smaller and Cheaper
Portable music player
Pocket calculator
Portable camera
Portable video camera
Portable GPS
Portable
telecommunication
Portable gaming device

## Slide 18: System Integration
Portable music player
Pocket calculator
Portable camera
Portable video camera
Portable GPS
Portable
telecommunication
Portable gaming device

## Slide 19: System Integration
Portable music player
Pocket calculator
Portable camera
Portable video camera
Portable GPS
Portable
telecommunication
Portable gaming device

## Slide 20: System Integration
Portable music player
Pocket calculator
Portable camera
Portable video camera
Portable GPS
Portable
telecommunication
Portable gaming device

## Slide 21: System Integration
Portable music player
Pocket calculator
Portable camera
Portable video camera
Portable GPS
Portable
telecommunication
Portable gaming device

## Slide 22: System Integration
Portable music player
Pocket calculator
Portable camera
Portable video camera
Portable GPS
Portable
telecommunication
Portable gaming device

## Slide 23: System Integration
Portable music player
Pocket calculator
Portable camera
Portable video camera
Portable GPS
Portable
telecommunication
Portable gaming device

## Slide 24
Nanotechnology on our Desktops
Hard Disk
Sensor Medium
Transistor
Gate
Source
Drain
Switching layer
5 nm
Magnetic grain
10 nm
Gate oxide
4 nm
Well
6 nm
Notes: Here are examples of nanotechnology at work in our computers. A quantum well laser reads a CD or DVD, the standard MOSFET transistor that runs all our computers has a gate oxide only 2-4 nanometers thick, and a hard disk has actually two components at the single-digit nanometer scale, the magnetic layer in the reading head that senses a stored bit, and the magnetic grains that store the data.
In the following two lectures, we will go through these examples in more detail.

## Slide 25
Gate oxide has shrunk to < 2nm, < 10 atom layers.
Electrons can tunnel through when applying a gate voltage.
Uses up to 1/3 of the power.
Power consumption by a leaky gate oxide: A show-stopper for Moore’s Law ?
Notes: The shrinking thickness of the gate oxide is currently the biggest threat to silicon technology and to its continued improvement via Moore’s law. These oxide layers have become so thin that the electrons can tunnel through it. That creates a leakage current, which has grown to about the third of the power consumption (i.e. heat load) of a microprocessor. This led to a major change in silicon technology. After 40 years of using silicon dioxide as gate insulator the most recent generation of silicon chips uses new oxides with higher dielectric constants. These can be made thicker than SiO2 while maintaining the same electrical performance (same capacitance).

## Slide 26

AlO2
LaO
TiO2
SrO

Ohtomo and H. Hwang Nature 427 (2004) 423-426
J. Mannhart1,* and D. G. Schlom2,*
Science 327, 1607 (2010)
Surprising phenomena at oxide-oxide interfaces: formation of a 2dimensional electron gas between two bulk insulators

## Slide 27: How Do We Arrange Them?
atomic spray painting approach
J. Am. Cer. Soc. 91, 2429 (2008).

## Slide 28: How Do We Arrange Them?
atomic spray painting approach
D. Muller group, Cornell
InGaAsP superlattice for high-efficicency solar cells, Sugiyama Lab, U of Tokyo
nm
AlAs/GaAs superlattices, atomically sharp interfaces, perfect atomic registry across interfaces, nanoscale arrangement of two structurally similar materials with entirely different electronic properties

## Slide 29: Ingredients for Atomic Scale Control
  surface
Keep the growth environment clean!
  adatom
  Ultrahigh vaccum is the choice!
  enough time to build up the crystal layer by layer without incorporating gas molecules

## Slide 30: Grow Slowly to Maintain Control
We want to grow atomic layer by atomic layer
  How many atoms will form a monolayer?
  How do I generate this this much flux?
  Knudsen
  Effusion cell

## Slide 31: Is This Feasible?
What are the vapor pressures of elements?

## Slide 32: Put Everything Together into a System: MBE

## Slide 33: Can We Do Nanoscience with this Last Century Technology?
Pioneering work in the U.S.: Al Cho and Art Gossard
Pioneering work in Germany: Klaus Ploog

## Slide 34: How Good is Good?

## Slide 35
3 mph
How Good is Good?

## Slide 36: Separate Scatters from Transport
65 mph

## Slide 37: Materials Perfection: Impurity Control
10000 mph
hypersonic scram jet

## Slide 38: Semiconductor Nanowires
Less than 5nm in diameter
Increase speed of electrons in nanowires – faster computing, improve efficiency of solar cells
Large surface area attractive for chemical sensing – homeland security

## Slide 39: The Many Uses of Gold Nanoparticles
First Response home pregnancy test
Gold nanoparticles with complementary DNA base pair sequence for HcG
The gold nanoparticles allow for more base pair detectors to be present on the applicator – thus heighten sensitivity to elevated levels of HcG

## Slide 40: Nano-Sun block
Keys incorporates nanosized ZnO particles into a cream
ZnO nanoparticles adsorb UVA and UVB
radiation wavelengths
However, because of the small size of
the ZnO particles (around 25 nm)
the particles do not scatter visible light
No white appearance

## Slide 41: Easton Sports Stealth CNT Bat
Combines carbon fiber technology with carbon
nanotube (CNT) technology
In between the carbon fibers is a polymer
resin containing CNT
Optimizes stiffness of bat for maximum
energy transfer to the ball

## Slide 42
Electrodeposition is performed using an electrochemical cell. A negatively charged metal is dissolved and metal atoms redeposit on the positively charged club head.
Dense layer of a nano-grained metal on the surface of the club head. This leads to a lighter and stronger club face with a bigger “sweet spot”
Nanotechnology in Golf

## Slide 43: The Result of Materials Improvements
Distances are average drive lengths (in yards) for PGA Tour players over the last 25 years
Note the substantial increase in the last decade (over 25 yards)
not to scale

## Slide 44: ARC Outdoors - ArcticShield Socks
Silver is known for its antimicrobial properties
Attempts have been made to incorporate
silver into linen socks via metal threads
Through the use of silver nanoparticles
ARC has incorporated the silver into
the polymer fibers
ARC claims permanent resistance
to odor or fungus

## Slide 45: Block Copolymer Assemblies to Form Ionic Channels
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
+
-
Hydrophobic part of the polymer provides mechanical strength.
Transmission electron micrograph of a block copolymer with hydrophobic and ionic phases. The ionic phases for channels for transport of ions and water.
Schematic of the self-assembly of like parts of the block copolymer.
Ionic part of the polymer is hydrophilic and conducts ions and water.
Elabd and Hickner, Macromolecules 2011.

## Slide 46: Block Copolymers can Form Many Different Structures
5 nm phases
High aspect ratio lines and corners
Selective patterning
Holes and isolated dots
Wormlike micelles in solution
Bates and Fredrickson, Physics Today 1999.

## Slide 47: Polymer Nanocomposites
Addition of a small amount of nanoparticles gives large change in properties of polymer
However, important polymer properties such as optical transparency, flexibility, and low weight remain
Imagine this 10’s of 1000’s of times over

## Slide 48: Wilson high performance tennis balls
inner core (barrier)
butyl-rubber + clay
http://www.wilsonsports.com.au/tennis/doublecore.html

## Slide 49
Application of Nanocomposite
Polymer Materials
A
B
C
Pump for artificial heart
Decrease sneaker weight, increase response
Running boards and body panels for cars

## Slide 50: Non-halogen, low flammability cables
Addition
of organo-clay
Improvements
on fire performance
and smoke density
Char formation of a cable with nanocomposite
J.W. Gilman, 2002

## Slide 51
SEM of nylon-6/5wt% clay nanocomposite after exposure to simulated solid-rocket motor exhaust &
& R.A. Vaia et al ,
Air Force Research Lab, 2001
Improvement of Thermal Properties
Thermal Conductivity
PC with 5wt% clay nanocomposite

## Slide 52: O'Lala Foods - Choco'la Chewing Gum
Incorporating chocolate into chewing gum has actually been challenging because the cocoa
butter fats in chocolate cause the
gum to lose its elastic nature
O’Lala has incorporated nano-
crystals that change the surface
characteristics of the gum allowing
for the incorporation of chocolate
flavoring

## Slide 53
Biological
Research
NANOMEDICINE
Raw
Nanomaterials
Nanostructured
Materials
Artificial Binding
Sites
Control of Surfaces
Nanopores
Cell Simulations
& Diagnostics
DNA Manipulation,
Sequencing, Diagnostics
Tools and Diagnostics
Intracellular
Devices
Drug Delivery
Molecular
Medicine
Artificial Enzymes
& Enzyme Control
Nanodevices
Biotechnology &
Biorobotics
Nanorobotics

## Slide 54: Surgical Tools
50 mm
Bend bars made using 400 micron thick molds
Bend bars made using 25 micron thick molds

## Slide 55: Nanocomposite Particles
20 nm
Particles on the order of 1 – 100 nm in diameter
Shell and core of particle are two different materials
Can be tailored to absorb specific radiation frequencies – military application
Can be designed to emit specific wavelengths of light – flat panel displays
Can be designed with any desired surface – biomedical imaging and drug delivery
Silica shell with rhodamine WT core

## Slide 56: Drug Delivery Systems
Erica Marden Senior Honors Thesis, 2012