## Slide 1
Introduction to Nanotechnology
Module #10
Nanotechnology:
Impact on Microelectronics
Nanotechnology is Impacting Everything
© patton brothers illustration (www.pattonbros.com)
Copyright April 2009 The Pennsylvania State University
Last Updated: 1/6/2011
Notes: <number>
There is a glossary that comes along with this set of modules. Each term in blue print in every module is defined in this glossary.

## Slide 2
  This module is one of a series designed to be used by faculty members at post-secondary institutions in workshops, courses, and overview lectures to introduce nanotechnology and its applications. There is no particular significance to the module number system
  The series was funded in part by:
  The National Science Foundation
  Grant # DUE 0532646 and DUE 0802498
  and
  The Pennsylvania Department of Community and Economic Development
  Grant # C000029471 and C000036659
  Any opinions, findings, and conclusions or recommendations expressed in this material are those of the author and do not necessarily reflect the views of the National Science Foundation or the Pennsylvania Department of Community and Economic Development
Copyright April 2009 The Pennsylvania State University

## Slide 3: Glossary of Terms
Throughout these modules you will find words and terms printed in the color blue. These words and terms are defined in the glossary (glossary.html), which can be opened by clicking here.
Copyright April 2009 The Pennsylvania State University

## Slide 4: Outline
Why is nanotechnology so critical to microelectronics
The need but the cost problem
What’s being made now
Alternatives to current nano-scale microelectronics
Nano-electronics
Moltronics
Key Ideas
Copyright April 2009 The Pennsylvania State University
Notes: <number>
The instructor may want to break this module into two lectures. There`s a lot of material here.

## Slide 5: Outline
Why is nanotechnology so critical to microelectronics
The need but the cost problem
What’s being made now
Alternatives to current nano-scale microelectronics
Nano-electronics
Moltronics
Key Ideas
Copyright April 2009 The Pennsylvania State University
Notes: <number>
The instructor may want to break this module into two lectures. There`s a lot of material here.

## Slide 6: Why is Nanotechnology so critical to Microelectronics?
The “push” in microelectronics is constantly toward smaller transistors. This allows faster devices (shorter distances for the electrons to travel) and more devices on a chip giving more memory and more functionality; i.e., giving new products to sell.
The microelectronics industry has reached 1 billion transistors on a chip! Transistors in production starting in 2008 are as small as 45nm!
Today’s advanced devices require that the microelectronics industry uses nanotechnology everyday to make these transistors.
Copyright April 2009 The Pennsylvania State University

## Slide 7: Why is Nanotechnology so critical to Microelectronics (continued)
Dr. Gordon E. Moore, a co-founder of Intel, has noticed over the course of almost 40 years that the number of transistors on a chip doubles about every 18 months. This observation is known as Moore’s Law. It captures the frenzy with which microelectronics companies have been pushing each other to make smaller and smaller transistors---it is a business observation, not a law of nature.
Copyright April 2009 The Pennsylvania State University

## Slide 8
Courtesy: R.J. Trew, NCSU
Copyright April 2009 The Pennsylvania State University
Notes: <number>
Vertical axis is number of transistors on a chip.

## Slide 9: Outline
Why is nanotechnology so critical to microelectronics
The need but the cost problem
What’s being made now
Alternatives to current nano-scale microelectronics
Nano-electronics
Moltronics
Key Ideas
Copyright April 2009 The Pennsylvania State University
Notes: <number>
The instructor may want to break this module into two lectures. There`s a lot of material here.

## Slide 10
The microelectronics industry is using top-down nanofabrication to make its nano-scale production transistors.
All the deposition, lithography, material modification, and etching steps required by top-down fabrication mean cleanrooms and very expensive equipment are required. These equipment requirements get more stringent as the transistors get smaller.
Copyright April 2009 The Pennsylvania State University

## Slide 11
The fabrication facilities (called “fabs”) needed to make these transistors get more expensive as the transistors get smaller.
Dr. Moore also noticed a trend in this cost. His observation was that the cost of building a new fab doubled every three years. This observation is called Moore’s Second law. It gives business people some idea of what future costs will be to stay in the microelectronics business.
Copyright April 2009 The Pennsylvania State University

## Slide 12
Moore’s Second Law
Doubling time ~ 3 years
Copyright April 2009 The Pennsylvania State University
Courtesy : R.J. Trew, NCSU

## Slide 13: The Need and the Cost
Microelectronics relies on nanotechnology—it needs nano-scale devices-- but the costs of the fabrication facilities (lithography equipment, etc) are getting prohibitively high
The nanofabrication used in microelectronics today is top-down fabrication so it relies on lithography
Optical lithography is hard-pressed to make the nano-scale devices now required
E-beam lithography requires rastering a beam so it is too slow for manufacturing
Copyright April 2009 The Pennsylvania State University

## Slide 14: Outline
Why is nanotechnology so critical to microelectronics
The need but the cost problem
What’s being made now
Alternatives to current nano-scale microelectronics
Nano-electronics
Moltronics
Key Ideas
Copyright April 2009 The Pennsylvania State University
Notes: <number>
The instructor may want to break this module into two lectures. There`s a lot of material here.

## Slide 15
Gate
Source
Drain
n+
n+
P-type
Channel
Oxide
Metal Electrode
Courtesy of CNEU
Schematic of what’s being made: The metal-oxide field effect transistor (MOSFET)
Copyright April 2009 The Pennsylvania State University

## Slide 16
Courtesy : Bob Trew, NCSU
Copyright April 2009 The Pennsylvania State University
Notes: <number>
These a cross-sections of MOSFET transistors. They are made by cutting a chip and looking in edge-wise at the cross-sections of the transistors using FESEM. These are lab transistors. The smallest in production today is 45nm.

## Slide 17
Yasuo Wada, Prospects for Single Molecule Information Processing Devices, IEEEXplore, Vol. 89 Issue. 8, August 2001. p 1150. (© 2001 IEEE)
The Interconnects
Schematic cross-section showing the many levels involved in a modern Microelectronics Circuit. The actual MOSFET transistors are seen (see 3 and 4) down in the “basement”. They are “wired” together by the many layers of complicated interconnects above (seen in black).
Copyright April 2009 The Pennsylvania State University
Notes: <number>
Schematic cross-section. Note that the transistor look as they really do in the earlier FESEM micrograph.

## Slide 18
The Problems:
  The prohibitive cost of factories that make ever smaller devices using lithography
  How to avoid devices that are lithographically determined
  How to more easily form the interconnects that connect transistors into circuits
Moore’s Second Law
Doubling time ~ 3 years
The fundamental problems of this technology
Courtesy : R.J. Trew, NCSU
Copyright April 2009 The Pennsylvania State University
Notes: <number>
Moore’s Second Law is that the cost of the factories (or fabs) for fabricating electronic devices has also been increasing exponentially with time. This is because the requirements on the size and positioning of features of features on a chip have been getting much more stringent, as has the complexity of the chips and the necessity to maintain a clean environment. In the past, the cost of the fabrication facility was small compared to all other costs, which have been increasing essentially linearly. However, now the cost of the fab is becoming a dominant cost, and the rate of its increase is significantly larger than the rate at with the market is growing. Thus, many experts believe that the economic issues illustrated by Moore’s Second Law will bring an end to the First.

## Slide 19: Nano-scale devices are needed but the costs are getting higher and higher
Alternatives to producing nano-scale devices that are different from what we are doing now are needed
Perhaps bottom-up nanofabrication should be explored
Copyright April 2009 The Pennsylvania State University

## Slide 20: Outline
Why is nanotechnology so critical to microelectronics
The need but the cost problem
What’s being made now
Alternatives to current nano-scale microelectronics
Nano-electronics
Moltronics
Key Ideas
Copyright April 2009 The Pennsylvania State University
Notes: <number>
The instructor may want to break this module into two lectures. There`s a lot of material here.

## Slide 21: Alternatives
Many people have suggested that the microelectronics industry has to stop using top-down nanofabrication and must move to bottom-up or hybrid nanofabrication
If this worked, it would stop the spiraling costs of producing nano-scale transistors
Copyright April 2009 The Pennsylvania State University

## Slide 22: Alternatives (continued)
Two approaches have been proposed:
(1) Microelectronics based on nanoparticles. This has been termed nano-electronics.
(2) Microelectronics based on the ultimate nanoparticle-- molecules. This has been termed moltronics.
Copyright April 2009 The Pennsylvania State University

## Slide 23: Nano-electronics
Devices start small
  Nanoparticles are “born” small
  No need for etching
  Position with self-assembly; then no need for lithography
Possible new device physics
  Very small structures possible—this gives rise to quantum mechanical effects
  New types of devices possible
Copyright April 2009 The Pennsylvania State University

## Slide 24: Moltronics
Devices start very small
  Molecules are inherently small
  No need for etching
  Position with self-assembly; then no need for lithography
Possible new device physics and chemistry
  New types of devices possible
Copyright April 2009 The Pennsylvania State University

## Slide 25: Where are we with these alternatives?
Generic solution that is proposed:
  Use bottom-up nanofabrication (lots of self-assembly of nanoparticles or molecules) and avoid lithography
Present state-of-the-art:
  Nano-electronics--Nanowire and nanotube demonstrations
  Moletronics--Molecular device demonstrations
Challenge:
  Make complex self-assembled circuits
  Prove reliable
  Prove high-yield manufacturability
Copyright April 2009 The Pennsylvania State University

## Slide 26: Outline
Why is nanotechnology so critical to microelectronics
The need but the cost problem
What’s being made now
Alternatives to current nano-scale microelectronics
Nano-electronics
Moltronics
Key Ideas
Copyright April 2009 The Pennsylvania State University
Notes: <number>
The instructor may want to break this module into two lectures. There`s a lot of material here.

## Slide 27: Nano-electronics
Copyright April 2009 The Pennsylvania State University

## Slide 28: Building Blocks for Nano-electronics
Nanowires
Nanotubes
Quantum dots
Copyright April 2009 The Pennsylvania State University

## Slide 29: Nano-electronics Device Fabrication
Bottom Up Fabrication--usually based on nanoparticles produced by
  Vapor-Liquid-Solid (VLS) mechanism
  Colloidal (solution) chemistry
Device Fabrication done by
  Grow-and-place approach
        Grow particles
        Harvest them
        Position them
        Make devices
  Grow-in-place approach
        Make particles where devices will be
        Make devices
Copyright April 2009 The Pennsylvania State University

## Slide 30: Grow-and-Place Approach An Example
Growth  Harvest  Place  Make device
Duan, X., et. al., Nature, 2003, 425, 274
You start with something like this and assemble them into devices like this
Copyright April 2009 The Pennsylvania State University
Notes: <number>
The term “TFT” used here means thin film transistor.

## Slide 31
SEM image of a carbon nanotube field-effect transistor with silicon back gate. The source/drain separation is approximately L=300nm.
J. Appenzeller, J. Knoch, R. Martel, V. Derycke, S. Wind, Ph. Avouris, Short-channel like effects in Schottky barrier carbon nanotube field-effect transistors, IEEE Technical Digest 2002. p.285. (© 2002 IEEE)
Carbon Nanotube FET-type Transistor Made by Grow-and-Place
Copyright April 2009 The Pennsylvania State University

## Slide 32
Assembly of p-type silicon (p-Si) and n-type gallium nitride (n-GaN) NWs to form crossed nanoscale p-n junctions.
Yu Huang, Xiangfeng Duan, Yi Cui, Lincoln J. Lauhon, Kyoung-Ha Kim, Charles M. Leiber, Logic Gates and Computation from Assembled Nanowire Building Blocks, SCIENCE Vol. 294, Nov. 9, 2001. p1314.
Nanowire p/n Junction Diodes Made by Grow-and-Place
Copyright April 2009 The Pennsylvania State University
Notes: <number>
Diode behavior is seen from these nanowires in the picture. Vertically oriented nanowires are p-type; horizontally oriented nanowires are n-type. Where they cross forms a p/n junction.

## Slide 33: Grow-in-Place Approach: An Example
(a)
(b)
(c)
(d)
An overview of the process flow for the fabrication of “grow-in-place” Si nanowire using “nursing” nanochannel templates: (a) Sacrificial/catalyst metal (Au) line defined by e-beam lithography, deposition, and etching. (b) Patterning and deposition of a capping layer. (c) Partial etching of the sacrificial metal to form the nanochannels with catalyst in the middle. (d) Si nanowire growth and extrusion out of channel by the VLS mechanism.
Copyright April 2009 The Pennsylvania State University
By Yinghui Shan and Stephen J. Fonash. “Self-Assembling Silicon Nanowires for Device Applications Using the Nanochannel-Guided “Grow-in-Place” Approach.” Nano Letters. 2008
Notes: <number>
The term SiNW means silicon nanowire.

## Slide 34
Small size, High density, and High performance
Si Nanowire FET-type Transistor (Current flow between source/drain controlled by gate) Made by Grow-in-Place
Actual transistor Nanowire seen between source and drain
By Yinghui Shan and Stephen J. Fonash. “Self-Assembling Silicon Nanowires for Device Applications Using the Nanochannel-Guided “Grow-in-Place” Approach.” Nano Letters. 2008
Copyright April 2009 The Pennsylvania State University
Notes: <number>
Many SiNW MOSFET transistors on a chip.

## Slide 35: Outline
Why is nanotechnology so critical to microelectronics
The need but the cost problem
What’s being made now
Alternatives to current nano-scale microelectronics
Nano-electronics
Moltronics
Key Ideas
Copyright April 2009 The Pennsylvania State University
Notes: <number>
The instructor may want to break this module into two lectures. There`s a lot of material here.

## Slide 36: Moltronics
Copyright April 2009 The Pennsylvania State University

## Slide 37
The idea of using molecules as components in electronic circuits dates back at least to a 1974 article by Aviram and Ratner entitled, “Molecular Rectifiers” [Chem. Phys. Lett., 29, 277, (1974)]. Although this seminal paper introduced the concept of exploiting electron transfer in molecules to perform useful electronic functions, the idea was not realized in practice until the mid-1990s.
Copyright April 2009 The Pennsylvania State University

## Slide 38
Since then most microelectronic functions have been experimentally observed in single molecules or molecular assemblies, including memory, rectification, and switching.
Copyright April 2009 The Pennsylvania State University

## Slide 39
Ideally a functioning molecular circuit component may be as small as a single molecule or approximately 100 or more times smaller than the current state of the art transistor (45nm) which is based on silicon top-down fabrication.
Copyright April 2009 The Pennsylvania State University

## Slide 40
This radical idea of using just molecules as electronic devices (moltronics) has been accompanied by some “teething difficulties” due to previously unexplored concepts and phenomena. It is not yet clear how molecules “should” behave in electronic circuits and how robust they can be. The “rules” are only beginning to be worked out.
Copyright April 2009 The Pennsylvania State University

## Slide 41
Moltronics is a really new approach and there are problems. For some results reported to date, it was not clear which observations were “molecular” and which were artifacts of the measurement or the fabrication technique. Inevitably, these false starts have resulted in reinterpretation of initial observations, but many of the basic questions about molecular conductivity and electronic function are now beginning to be answered reliably.
Copyright April 2009 The Pennsylvania State University

## Slide 42
An Example of a Metal-Molecule-Metal Structure
S. M. Lindsay, “Single Molecule Electronics”, The Electrochemical Society Interface, Spring 2004, Page 26
Copyright April 2009 The Pennsylvania State University

## Slide 43
Molecule Diode (Current flows easily in only one direction)
Robert M. Metzger, “Four Examples of Unimolecular Electrical Rectifiers”, The Electrochemical Society Interface, Spring 2004, Page 41
Copyright April 2009 The Pennsylvania State University

## Slide 44: Outline
Why is nanotechnology so critical to microelectronics
The need but the cost problem
What’s being made now
Alternatives to current nano-scale microelectronics
Nano-electronics
Moltronics
Key Ideas
Copyright April 2009 The Pennsylvania State University
Notes: <number>
The instructor may want to break this module into two lectures. There`s a lot of material here.

## Slide 45
Key Ideas
Consumer pressure for more and better electronics keeps pushing microelectronics to smaller and smaller devices
Production transistors are currently well into the nano-scale in size—and getting smaller
These transistors are made using top-down nanofabrication
Copyright April 2009 The Pennsylvania State University

## Slide 46
Key Ideas (continued)
Top-down transistor fabrication is requiring more and more expensive fabs (microelectronics factories)
Nanoelectronics and/or Moltronics may provide an alternative to top-down transistor fabrication
Nanoelectronics, based on nanoparticles, and Moltronics, based on molecules, start with things that are small and use self-assembly to construct devices
Copyright April 2009 The Pennsylvania State University

## Slide 47
Key Ideas (continued)
Nanoelectronics works. Viable manufacturing approaches need to be developed
Moltronics needs to prove its robustness, reliability, and manufacturability
Copyright April 2009 The Pennsylvania State University

## Slide 48
This module, produced by the Center for Nanotechnology Education and Utilization at
The Pennsylvania State University,
is one of a series developed to introduce nanotechnology and its applications to a broad audience. Each module, its component viewgraphs, and the companion glossary are copyrighted 2009 by
The Pennsylvania State University.
All rights reserved.
Copyright April 2009 The Pennsylvania State University