## Slide 1
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 2
Outline
A. Introduction to concept of commercial building energy auditing
  1. Why energy efficiency (EE) is important
  2. Energy use and waste in commercial building operations
  3. Prioritizing energy efficiency over renewable energy generation
B. Ordinances, policies and standards governing commercial building audits
  1. San Francisco Existing Commercial Buildings Performance Ordinance
  2. State of California energy goals
  3. ASHRAE standards, including Building Energy Assessment Professional (BEAP)
  4. Other audit standards
C. Three ASHRAE audit levels
  1. Preliminary energy use analysis
  2. Level 1, Walk-through analysis
  3. Level 2, Intermediate, energy survey and energy analysis
  4. Level 3, Detailed analysis of capital-intensive modifications
D. Developing the scope of work in a commercial building audit
  1. Objectives of the audit, including needed data and resources
  2. Assessment management
  3. Responsibilities of audit team members
E. Elements in preliminary analysis of building performance data
  1. Engineering and architectural document review
  2. Geographical and climatic review
  3. Review and analysis of current energy use and costs
  4. Benchmarking procedures
F. Factors in on-site building assessment
  1. Common safety hazards and field safety techniques
  2. Occupant interviews and assessment of building operations
  3. Building envelope
  4. Electrical systems
  5. HVAC&R systems
  6. Lighting systems and use
  7. Miscellaneous other energy use systems
  8. Domestic water systems and use
  9. Indoor environmental quality
G. Analysis of data collected
  1. Identify opportunities for efficiency improvement
  2. Calculate value of efficiency improvements and return on investment
  3. Prioritize options based on client criteria
H. Audit completion activities
  1. Prepare and present written report
  2. Assist with development of implementation plan
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 3
B. Ordinances, policies and standards governing commercial building audits
  1. San Francisco Existing Commercial Buildings Performance Ordinance
  2. State of California energy goals
  3. ASHRAE standards, including Building Energy Assessment Professional (BEAP)
  4. Other audit standards
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 4
B. Ordinances, policies and standards governing commercial building audits
  1. San Francisco Existing Commercial Buildings Performance Ordinance
  2. State of California energy goals
  3. ASHRAE standards, including Building Energy Assessment Professional (BEAP)
  4. Other audit standards
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 5
Course No. ENRG 50
SF Existing Commercial Buildings Performance Ordinance
1. SF Existing Commercial Buildings Performance Ordinance
    Requirements:
    Benchmark energy use each year, so one can compare with others and track progress
    Get an energy audit every five years, which identifies cost-effective opportunities to improve
© honestbuildings.com

## Slide 6
Course No. ENRG 50
SF Existing Commercial Buildings Performance Ordinance
1. SF Existing Commercial Buildings Performance Ordinance
    Who shall participate?
    - Owners of commercial buildings over 10,000 sf
    - Buildings >50,000 sf required to report benchmarking by Oct. 2011
    Why participate?
    - Saving energy saves money.
    - Benchmarking to ensure owners/users don’t use more energy than competitors.
    - Get recognized for leadership in energy management.
    - The policy was written with extensive input from commercial stakeholders
    - The ordinance gives SF environment the authority to impose fines of up to $100 per day.

## Slide 7
Course No. ENRG 50
Benchmarking
1. San Francisco Existing Commercial Buildings Performance Ordinance
    Why benchmark?
    - Assess energy performance baselines and set goals for improvement.
    - Track and report on energy performance, costs, and environmental impact over time, for individual buildings and entire portfolios
    - Comply with California Assembly Bill 1103, which requires disclosure of benchmarking data for real estate transactions
    - Comply with the new San Francisco Ordinance that requires benchmarking of buildings >=10,000 sf in 2011
    - Receive a prestigious ENERGY STAR label with scores above 75.
    - Earn points toward LEED ® certification.
    PG&E’s free Automated Benchmark Service:
    http://www.pge.com/benchmarking/

## Slide 8
Course No. ENRG 50
Benchmarking
1. San Francisco Existing Commercial Buildings Performance Ordinance
    Required data for benchmarking?
    - Portfolio Manager username and password.
    - The building street address, year built, and contact information.
    - The building gross floor area and key operating characteristics for each major space type.
    - 12 consecutive months of utility bills for all fuel types used in the building.
Data Collection Worksheet:
    http://www.energystar.gov/ia/business/downloads/PM_Data_Collection_Worksheet.doc
    Portfolio Manager Quick Reference Guide:
    http://www.energystar.gov/ia/business/downloads/PM_QuickRefGuide.pdf?cff0-e2dd
    We will talk about the benchmarking procedures in Chapter E
© Corporator.com

## Slide 9
Course No. ENRG 50
Energy Auditing
1. San Francisco Existing Commercial Buildings Performance Ordinance
    Requirements:
    Except buildings:
    - Having had a qualifying audit or retrocommissioning since 2008
    - Earning LEED for Existing Buildings certification
    - Getting the ENERGY STAR label regularly (score>=75)
    - Residential, less than five years old, smaller than 10,000sf, or under financial distress are also exempt
Building size | Minimum Level of Effort
50,000 sf and larger | ASHRAE Level II – An “intermediate” survey and energy analysis
10,000 to 49,999 sf | ASHRAE Level I – A basic energy analysis

## Slide 10
Course No. ENRG 50
SF Ordinance Energy Efficiency Auditor Qualifications
1. San Francisco Existing Commercial Buildings Performance Ordinance
Licensed Professional Engineer and one of the following:
- At least 2 years experience performing energy efficiency audits or commissioning of existing buildings; or
- ASHRAE Commissioning Process Management Professional Certification; or
- Similar qualifications in energy efficiency analysis or commissioning.
Association of Energy Engineers Certified Energy Manager (CEM);
At least 10 years experience as a building operating engineer, or at least 5 years experience as a chief operating engineer and one of the following:
- BOC International Building Operator Certification; or
- International Union of Operating Engineers Certified Energy Specialist; or
Equivalent professional qualifications to manage, maintain, or evaluate systems, as well as specialized training in energy efficiency audits and maintenance of systems, as determined by the Director.

## Slide 11
Course No. ENRG 50
Energy Efficiency audit report shall include:
1. San Francisco Existing Commercial Buildings Performance Ordinance
(1) The date(s) that the audit was performed;
(2) A list of all retro-commissioning and retrofit measures available to the owner;
(3) An estimate of the approximate energy savings, avoided energy cost, and costs to implement each measure; and
(4) One of the following:
- A list of all retro-commissioning and retrofit measures available to the owner with a simple payback of not more than 5 years; or
- A list of all retro-commissioning and retrofit measures available to the owner with a positive net present value; or
- An integrated package of retro-commissioning and retrofit measures that in combination will equal or exceed the total combined reduction in energy consumption of implementing all retrofit and retro-commissioning measures with a simple payback of not more than 5 years.

## Slide 12
B. Ordinances, policies and standards governing commercial building audits
  1. San Francisco Existing Commercial Buildings Performance Ordinance
  2. State of California energy goals
  3. ASHRAE standards, including Building Energy Assessment Professional (BEAP)
  4. Other audit standards
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 13
Course No. ENRG 50
CA Strategic Plan by CPUC
2. State of California energy goals
    ZNE – Zero Net Energy
    All NEW residential construction will be ZNE by 2020
    All NEW commercial construction will be ZNE by 2030.
    information source: http://www.cpuc.ca.gov/NR/rdonlyres/6C2310FE-AFE0-48E4-AF03-530A99D28FCE/0/ZNEActionPlanFINAL83110.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 14
Course No. ENRG 50
CA Strategic Plan by CPUC
2. State of California energy goals
Information source:
    http://www.cpuc.ca.gov/NR/rdonlyres/6C2310FE-AFE0-48E4-AF03-530A99D28FCE/0/ZNEActionPlanFINAL83110.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 15
Course No. ENRG 50
CA Strategic Plan by CPUC
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/6C2310FE-AFE0-48E4-AF03-530A99D28FCE/0/ZNEActionPlanFINAL83110.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 16
Course No. ENRG 50
CA Strategic Plan by CPUC
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/6C2310FE-AFE0-48E4-AF03-530A99D28FCE/0/ZNEActionPlanFINAL83110.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 17
Course No. ENRG 50
History of CPUC Utility Goals for EE
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/E1E38C4A-5E56-4ACB-B0C9-AFD69656BFA0/0/goalsdecisionssummary.pdf
Yr of decision | Desicions | Goals | File sources
Sep. 2004 | Original Goals Decision | D. 04-09-060 | http://docs.cpuc.ca.gov/word_pdf/FINAL_DECISION/40212.pdf
Sep. 2007 | Incentive Mechanism | D. 07-09-043 | http://docs.cpuc.ca.gov/WORD_PDF/FINAL_DECISION/73172.PDF
Oct. 2007 | Interim Opinion on Issues Relating the Future Savings Goals | D. 07-10-032 | http://docs.cpuc.ca.gov/WORD_PDF/FINAL_DECISION/74107.PDF
Jul. 2008 | 2008 Goals Decision | D. 08-07-047 | http://docs.cpuc.ca.gov/WORD_PDF/FINAL_DECISION/85995.PDF
May 2009 | May 2009 Decision | D. 09-05-037 | http://docs.cpuc.ca.gov/WORD_PDF/FINAL_DECISION/101543.PDF
Sep. 2009 | Sep. 2009 Decision | D. 09-09-047 | http://docs.cpuc.ca.gov/PUBLISHED/GRAPHICS/107829.PDF
Oct. 2010 | Oct. 2010 Decision | D. 10-10-033 | http://docs.cpuc.ca.gov/word_pdf/FINAL_DECISION/125983.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 18
Course No. ENRG 50
History of CPUC Utility Goals for EE
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/E1E38C4A-5E56-4ACB-B0C9-AFD69656BFA0/0/goalsdecisionssummary.pdf
The affect on the CPUC adopted goals as a result of decision since D.04-09-060
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 19
Course No. ENRG 50
History of CPUC Utility Goals for EE
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/E1E38C4A-5E56-4ACB-B0C9-AFD69656BFA0/0/goalsdecisionssummary.pdf
GWh saving goals
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 20
Course No. ENRG 50
History of CPUC Utility Goals for EE
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/E1E38C4A-5E56-4ACB-B0C9-AFD69656BFA0/0/goalsdecisionssummary.pdf
MW saving goals
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 21
Course No. ENRG 50
History of CPUC Utility Goals for EE
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/E1E38C4A-5E56-4ACB-B0C9-AFD69656BFA0/0/goalsdecisionssummary.pdf
Therm saving goals
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 22
Course No. ENRG 50
Energy Efficiency Evaluation Report 2010-2011
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/89718A1B-C3D5-4E30-9A82-74ED155D0485/0/EnergyEfficiencyEvaluationReport.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 23
Course No. ENRG 50
Energy Efficiency Evaluation Report 2010-2011
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/89718A1B-C3D5-4E30-9A82-74ED155D0485/0/EnergyEfficiencyEvaluationReport.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 24
Course No. ENRG 50
Estimated Savings and Performance Towards Goals
2. State of California energy goals
    Information source: http://www.cpuc.ca.gov/NR/rdonlyres/89718A1B-C3D5-4E30-9A82-74ED155D0485/0/EnergyEfficiencyEvaluationReport.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 25
Course No. ENRG 50
Energy Efficiency Evaluation
2. State of California energy goals
    Information source: http://www.cacleanenergyfuture.org/documents/EnergyEfficiency.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 26
Course No. ENRG 50
Energy Efficiency Evaluation
2. State of California energy goals
    Information source: http://www.cacleanenergyfuture.org/documents/EnergyEfficiency.pdf
Notes: CPUC-California Public Utilities Commission
IOU- Investor-owned utility

## Slide 27
B. Ordinances, policies and standards governing commercial building audits
  1. San Francisco Existing Commercial Buildings Performance Ordinance
  2. State of California energy goals
  3. ASHRAE standards, including Building Energy Assessment Professional (BEAP)
  4. Other audit standards
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 28
Course No. ENRG 50
35 Years of Standard ASHRAE 90.1
3. ASHRAE standards
http://ali.ashrae.biz/2012winterconferencecourses/std90-1envelope/Complying_90-1-2010_Env_Ltg_Chicago_2012_Final_Slides.pdf

## Slide 29
Course No. ENRG 50
Standard ASHRAE 90.1 savings- Estimates for 4 Generations
3. ASHRAE standards
http://ali.ashrae.biz/2012winterconferencecourses/std90-1envelope/Complying_90-1-2010_Env_Ltg_Chicago_2012_Final_Slides.pdf

## Slide 30
Course No. ENRG 50
Standard ASHRAE 90.1 – 2004 vs. 1999
3. ASHRAE standards
http://ali.ashrae.biz/2012winterconferencecourses/std90-1envelope/Complying_90-1-2010_Env_Ltg_Chicago_2012_Final_Slides.pdf

## Slide 31
Course No. ENRG 50
Future goals for ASHRAE codes
3. ASHRAE standards
http://ali.ashrae.biz/2012winterconferencecourses/std90-1envelope/Complying_90-1-2010_Env_Ltg_Chicago_2012_Final_Slides.pdf

## Slide 32
Course No. ENRG 50
ASHRAE currently offers 6 certification programs
3. ASHRAE standards
    Building Energy Assessment Professional (BEAP)
    Building Energy Modeling Professional (BEMP)
    Commissioning Process Management Professional (CPMP)
    Healthcare Facility Design Professional (HFDP)
    High-Performance Building Design Professional (HBDP)
    Operations & Performance Management Professional (OPMP)

## Slide 33
Course No. ENRG 50
Building Energy Assessment Professional Certification (BEAP)
3. ASHRAE standards, including BEAP
    Was developed in close collaboration with representatives from:
    - ASHRAE’s Building Energy Quotient (bEQ) program
    - Illuminating Engineering Society (IES)
    - National Institute of Building Sciences (NIBS)
    - Sheet Metal and Air-Conditioning Contractors’ National Association (SMACNA)
    - Testing, Adjusting and Balancing Bureau (TABB)

## Slide 34
Course No. ENRG 50
BEAP Eligibility Requirements
3. ASHRAE standards, including BEAP
    Meet ONE of the following criteria and > 2 yrs’ building energy assessment experience, will be eligible to take exam:
    - Government-issued/recognized license as a professional engineer, architect, or building contractor; or
    - Minimum of Bachelor’s degree in engineering or related field, and > 3 yrs’ energy-related HVAC, architecture, lighting, envelope, or renewable energy experience; or
    - Associate’s degree or Technical degree, > 5 yrs related experience; or
    - High School diploma, and >8 yrs related experience

## Slide 35
B. Ordinances, policies and standards governing commercial building audits
  1. San Francisco Existing Commercial Buildings Performance Ordinance
  2. State of California energy goals
  3. ASHRAE standards, including Building Energy Assessment Professional (BEAP)
  4. Other audit standards
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 36
Course No. ENRG 50
Other audit standards
4. Other audit standards
    NREL procedure
    http://www.nrel.gov/docs/fy06osti/38601.pdf

## Slide 37
Course No. ENRG 50
NREL procedure
4. Other audit standards

## Slide 38
Course No. ENRG 50
NREL procedure outline
4. Other audit standards
Project Definition
Identify project goals
Questionnaires
Determine boundaries of facility
Select tier 1 or 2 analysis
Specify accuracy of results
Identify period of analysis
Assemble basic building data
Estimate budget for project
Obtain pre-existing perf. data

## Slide 39
Course No. ENRG 50
NREL procedure outline
4. Other audit standards
Measurement System Design
Select performance metrics to be measured
Identify data required for each metric
Specify physical location of each measurement
Specify frequency of each measurement
Specify measurement equipment
Determine practicality of measurements
Estimate cost of DAS equipment and operation
Resolve cost and uncertainty with expectations

## Slide 40
Course No. ENRG 50
NREL procedure outline
4. Other audit standards
Reporting Results
Monitor data for quality control
Reporting
Data Collection and Analysis
Assemble data for the period of analysis
Calculate monthly metrics
Calculate annual metrics

## Slide 41
Course No. ENRG 50
Other audit standards
4. Other audit standards
    LBNL Industrial Energy Audit Guidebook
    http://minotaur.lbl.gov/china.lbl.gov/sites/china.lbl.gov/files/LBNL-3991E.Industrial%20Energy%20Audit%20Guidebook_0.pdf

## Slide 42
Course No. ENRG 50
LBNL Industrial Energy Audit Guidebook
4. Other audit standards
    Typical steps:
    - preparation and planning
    - data collection and review
    - plant surveys and system measurements
    - observation and review of operating practices
    - data documentation and analysis
    - reporting of the results and recommendations

## Slide 43
Course No. ENRG 50
LBNL Industrial Energy Audit Guidebook
4. Other audit standards
    Types of energy audits:
    - preliminary audit (walk-through audit)
    - detailed audit (diagnostic audit)
    Procedures:
    - energy audit preparation
    - energy audit execution
    - energy audit reporting
    - post-audit activities

## Slide 44
Course No. ENRG 50
LBNL Industrial Energy Audit Guidebook
4. Other audit standards
Energy audit preparation
Audit criteria
Audit scope
Selection of audit team
Audit plan
Checklists preparation
collecting bills and data
Preliminary analysis
Initial walk-through

## Slide 45
Course No. ENRG 50
LBNL Industrial Energy Audit Guidebook
4. Other audit standards
Energy audit execution
Data inventory and measurements
Analyzing energy use patterns
Benchmarking and comparative analysis
Identifying energy efficiency potentials
Cost-benefit analysis

## Slide 46
Course No. ENRG 50
LBNL Industrial Energy Audit Guidebook
4. Other audit standards
Post-audit activities
Writing audit report with recommendation
Preparing action plan for implementation
Implementing the action plan
Energy audit reporting