## Slide 1
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 2
Outline
A. Introduction to concept of commercial building energy auditing
  1. Why energy efficiency (EE) is important
  2. Energy use and waste in commercial building operations
  3. Prioritizing energy efficiency over renewable energy generation
B. Ordinances, policies and standards governing commercial building audits
  1. San Francisco Existing Commercial Buildings Performance Ordinance
  2. State of California energy goals
  3. ASHRAE standards, including Building Energy Assessment Professional (BEAP)
  4. Other audit standards
C. Three ASHRAE audit levels
  1. Preliminary energy use analysis
  2. Level 1, Walk-through analysis
  3. Level 2, Intermediate, energy survey and energy analysis
  4. Level 3, Detailed analysis of capital-intensive modifications
D. Developing the scope of work in a commercial building audit
  1. Objectives of the audit, including needed data and resources
  2. Assessment management
  3. Responsibilities of audit team members
E. Elements in preliminary analysis of building performance data
  1. Engineering and architectural document review
  2. Geographical and climatic review
  3. Review and analysis of current energy use and costs
  4. Benchmarking procedures
F. Factors in on-site building assessment
  1. Common safety hazards and field safety techniques
  2. Occupant interviews and assessment of building operations
  3. Building envelope
  4. Electrical systems
  5. HVAC&R systems
  6. Lighting systems and use
  7. Miscellaneous other energy use systems
  8. Domestic water systems and use
  9. Indoor environmental quality
G. Analysis of data collected
  1. Identify opportunities for efficiency improvement
  2. Calculate value of efficiency improvements and return on investment
  3. Prioritize options based on client criteria
H. Audit completion activities
  1. Prepare and present written report
  2. Assist with development of implementation plan
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 3
E. Elements in preliminary analysis of building performance data
  1. Engineering and architectural document review
  2. Geographical and climatic review
  3. Review and analysis of current energy use and costs
  4. Benchmarking procedures
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 4
Course No. ENRG 50
Building Documentation
1. Engineering and architectural document review
Types of documentation:
- As built drawings
- Equipment inventory
- Submittals/test and balance reports
- Controls schedule
- Maintenance logs/service requests
What are you looking for:
    - The major building loads
    - Control strategies
    - Efficiencies of equipment

## Slide 5
Course No. ENRG 50
Engineering and architectural document review
1. Engineering and architectural document review
Typical design work products
A_._ (e.g. A1.0) : Architectural
S_._ : Structural
M_._ : Mechanical (HVAC)
E_._ : Electrical (including lighting)
P_._ : Plumbing (domestic water, hot water, waste water)
C_._ : Civil (site work, stormwater)
L_._ : Landscape

## Slide 6
Course No. ENRG 50
Building floor plan
1. Engineering and architectural document review
    Info:
    - Name and location
    - Year of construction
    - Size: floors, sf
    - North arrow
    - Locations of mechanical, electrical and other rooms with specialized equipment
    If drawings not available
    - photograph egress plans
    - Building outline from Google maps
http://www.veritasschool.net/plans.html

## Slide 7
Course No. ENRG 50
Equipment inventory demo
1. Engineering and architectural document review
http://www.irs.gov/pub/irs-procure/techexhibit_5_equipment_pm_inventory.pdf

## Slide 8
Course No. ENRG 50
Catalog existing equipment
1. Engineering and architectural document review
    System configuration
    - Equipment:
      Type
      Quantity
      Efficiency
    Controls
    - Identify schedules (Building automation system)
    - Locate other sensors and controls
    - Locate zone controls

## Slide 9
E. Elements in preliminary analysis of building performance data
  1. Engineering and architectural document review
  2. Geographical and climatic review
  3. Review and analysis of current energy use and costs
  4. Benchmarking procedures
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 10
Course No. ENRG 50
Geographical and climate review
2. Geographical and climate review
http://www.commercialwindows.org/codesstandards_ashrae90_1_more.php#2010

## Slide 11
Course No. ENRG 50
Geographical and climate review
2. Geographical and climate review
http://www.commercialwindows.org/codesstandards_ashrae90_1_more.php#2010

## Slide 12
Course No. ENRG 50
Climate data for simulation
2. Geographical and climate review
http://apps1.eere.energy.gov/buildings/energyplus/weatherdata_simulation.cfm
Weather Bank - maintains hourly and daily historical data records from every National Weather Service reporting station in US, as well as other locations around the world. They archive weather data on a real-time basis and certain updates are made hourly. This hourly archiving began in late Nov., 1994.
National Climatic Data Center - NCDC is the world's largest active archive of weather data. NCDC produces numerous climate publications and responds to data requests from all over the world. NCDC operates the World Data Center for Meteorology which is co-located at NCDC in Asheville, North Carolina, and the World Data Center for Paleoclimatology which is located in Boulder, Colorado.
Weather Source - Weather Source provides historical and real-time digital weather information for more than 10,000 locations across the United States and around the world.
Weather Analytics - Site specific weather files in EnergyPlus format based on the latest 30 years of hourly data are now available from the private sector company Weather Analytics for any official weather station on more than 600,000 35-km grid tiles across the globe. These files are built by integrating hourly weather station observations and the new NOAA reanalysis data sets. Both Typical Meteorological Year (TMY) files and individual, Actual Meteorological Year (AMY) files are available, as are files constructed from the previous 12 months.
Meteonorm - Meteonorm extrapolates hourly data from statistical data for a location. Where statistical data aren't available, Meteonorm interpolates from other nearby sites. Generally, a statistical approach is a last resort ‐ weather files generated from statistics will not demonstrate the normal hour-to-hour and day-to-day variability seen in measured data.

## Slide 13
E. Elements in preliminary analysis of building performance data
  1. Engineering and architectural document review
  2. Geographical and climatic review
  3. Review and analysis of current energy use and costs
  4. Benchmarking procedures
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 14
Course No. ENRG 50
Utility analysis
3. Review and analysis of current energy use and costs
    Utility rate schedules
    - used to calculate the savings and paybacks
    http://www.uos.harvard.edu/fmo/building_maintenance/quincy_house_energy_audit.pdf

## Slide 15
Course No. ENRG 50
Energy performance summary by fiscal year
3. Review and analysis of current energy use and costs
    http://www.uos.harvard.edu/fmo/building_maintenance/quincy_house_energy_audit.pdf

## Slide 16
Course No. ENRG 50
Utility spending breakdown
3. Review and analysis of current energy use and costs
    http://www.uos.harvard.edu/fmo/building_maintenance/quincy_house_energy_audit.pdf
FY 10 FY09 FY08
Steam was the most expensive utility followed by electricity.

## Slide 17
Course No. ENRG 50
End use component energy usage breakdown
3. Review and analysis of current energy use and costs
    http://www.uos.harvard.edu/fmo/building_maintenance/quincy_house_energy_audit.pdf

## Slide 18
Course No. ENRG 50
Energy use and cost indices by fiscal year
3. Review and analysis of current energy use and costs

## Slide 19
Course No. ENRG 50
Electrical demand by fiscal year
3. Review and analysis of current energy use and costs
Because the demand has been stable for the past three fiscal years, the audit team recognizes equipment and operations have been consistent and will look for opportunities to reduce the building’s peak load.

## Slide 20
E. Elements in preliminary analysis of building performance data
  1. Engineering and architectural document review
  2. Geographical and climatic review
  3. Review and analysis of current energy use and costs
  4. Benchmarking procedures
Introduction to Commercial Building Audits
Course No. ENRG 50

## Slide 21
Course No. ENRG 50
Benchmarking
    Required data for benchmarking?
    - Portfolio Manager username and password.
    - The building street address, year built, and contact information.
    - The building gross floor area and key operating characteristics for each major space type.
    - 12 consecutive months of utility bills for all fuel types used in the building.
Data Collection Worksheet:
    http://www.energystar.gov/ia/business/downloads/PM_Data_Collection_Worksheet.doc
    Portfolio Manager Quick Reference Guide:
    http://www.energystar.gov/ia/business/downloads/PM_QuickRefGuide.pdf?cff0-e2dd
© Corporator.com
4. Benchmarking procedure

## Slide 22
Course No. ENRG 50
Partial Data Collection Worksheet
4. Benchmarking procedure

## Slide 23
Course No. ENRG 50
Benchmarking – Identify Energy Efficiency Projects
4. Benchmarking procedure

## Slide 24
Course No. ENRG 50
Benchmarking – Identify Energy Efficiency Projects
4. Benchmarking procedure

## Slide 25
Course No. ENRG 50
Benchmarking – Track Progress over Time
4. Benchmarking procedure

## Slide 26
Course No. ENRG 50
Benchmarking – Verify and Document Results
4. Benchmarking procedure