## Slide 1: Introduction to Energy and Building Science Fundamentals Course No. ENRG 52

## Slide 2
Outline
A. Introduction to fundamentals of lighting
  Lighting terminology
  Physics and principles of lighting
  Units of measurement
  Vision and colors
  Ambient, directional and task lighting
  Over- and under-illuminance
B. Lighting systems
  Components
  Types of lamps
  Ballasts
  Lamp comparison matrix
  Types of lighting luminaires and intensities
  Energy efficiency measures (EEMs)
C. Lighting controls
  Basic concepts of effectiveness of lighting control
  Types and appropriate applications of lighting controls
  Lighting control equations
  Energy efficiency measures (EEMs)
D. Additional EEMs
  De-lamping
  Scotopic lighting
  Task and ambient light levels
  Circadian rhythms
E. Lighting measurements
  Tools
  Data loggers and applications
F. Lighting calculations
  Equation and method of calculating lumens (zonal cavity formula)
  Equation and method of calculating energy savings
  Method of calculating skylight energy savings
G. Lighting standards, codes and regulations
  Underwriters' Laboratory (UL)
  Uniform Building Code (UBC)
  Americans with Disabilities Act (ADA)
  Title 24 applications
H. O&M measures to assure optimal performance
Introduction to Energy and Building Science Fundamentals
Course No. ENRG 54

## Slide 3
Balance Point and Emissivity

## Slide 4: Balance Point and Emissivity
The emissivity of material is the relative ability of its surface to emit (throw off) energy by radiation
In a thermal equilibrium, there should be a balance point between absorbed radiation and emitted radiation

## Slide 5
Solar Geometry
  Sun angles
  Azimuth
  Plot of sun path

## Slide 6: Earth-Sun Geometry
Driving variable of environmental processes on Earth
Geometry determines the amount and intensity of incoming solar radiation (insolation) reaching particular earth
Geometry (and how it changes) determines:
  Seasonality (1 yr)
  Glacial (cold) and interglacial (warm) periods (1000’s of years)
Notes: 6

## Slide 7
The earth moves about the sun in an elliptical orbit, completing one revolution per year. In addition, the earth rotates once per day about its polar axis. The polar axis is inclined at an angle of 23.45o from the normal to the plane of the earth’s orbit (ecliptic)

## Slide 8: SOLAR ANGLES
ψ = Zenith Angle = Angle between sun's ray and a line perpendicular to the horizontal plane at P.
β = Altitude Angle = Angle in vertical plane between the sun's rays and projection of the sun's ray on a horizontal plane.
It follows β + ψ =π/2
= Azimuth angle = Angle measured from north to the horizontal projection of the sun's ray.
= Azimuth Angle = angle measured from south to the horizontal projection of the Sun’s ray.
Sun

## Slide 9: Solar Angle
The amount of heat energy received at any location on the globe is a direct effect of sun angle on climate
The angle at which sunlight strikes the Earth varies by location, time of day, and season due to the Earth’s orbit around the sun and the Earth’s rotation around its tilted axis.
Seasonal change in the angle of sunlight, caused by the tilt of the Earth's axis, is the basic mechanism that results in warmer weather in summer than in winter.
Change in day lenght is another factor.

## Slide 10
As the Earth revolves around the Sun, tilt creates variation in day and night lengths over the duration of a calendar year
What day of the year is this?
Circle of illumination

## Slide 11: Effects of Sun Angle
Diagram illustrates how sunlight is spread over a greater area in the polar regions. In addition to the density of incident light, the dissipation of light in the atmosphere is greater when it falls at a shallow angle.
One sunbeam one mile wide shines on the ground at a 90° angle, and another at a 30° angle. The one at a shallower angle covers twice as much area with the same amount of light energy
Notes: http://en.wikipedia.org/wiki/Effect_of_sun_angle_on_climate

## Slide 12: How you experience the changing of the seasons in terms of Earth-Sun geometry
Sun’s altitude: angle between horizon and sun is different throughout the year. Sun is not always directly overhead at a 90° angle at noon. Max sun angles in summer, lower in winter
Day/night length: Maximum contrast at solstices to uniformity (12 hrs day/12 hours night) across the globe on the equinoxes.
Notes: Declinations are used for other things as well—magnetic declination, for example.

## Slide 13: Long-term variations in Earth-Sun geometry
Contribute to alternating climates:
  Interglacial (warm)
  Glacial (cold)
Have profound effects on sea-level
Pleistocene: approximately 2 million year period of glacials and interglacials

## Slide 14
Solar Geometry
  Sun angles
  Azimuth
  Plot of sun path

## Slide 15: Azimuth
Is an angular measurement in a spherical system.
The azimuth is the angle formed between a reference direction (North) and a line from the observer to a point of interest projected on the same plane as the reference direction.
Azimuth is usually measured in degrees (°). The concept is used in many practical applications including navigation, astronomy, and engineering.

## Slide 16: Azimuth

## Slide 17
Solar Geometry
  Sun angles
  Azimuth
  Plot of sun path

## Slide 18: Sun Path
Sun path refers to the apparent significant seasonal-and-hourly positional changes of the sun (and length of daylight) as the Earth rotates, and orbits around the sun.
The relative position of the sun is a major factor in the heat gain of buildings and in the performance of solar energy systems.
Accurate location-specific knowledge of sun path and climatic conditions is essential for economic decisions about solar collector area, orientation, landscaping, summer shading, and the cost-effective use of solar equipment
Notes: http://en.wikipedia.org/wiki/Sun_path

## Slide 19: Sun Path