## Slide 1: Measurement Tools & Verification of Savings Calculations H. Developing the M&V Plan
Notes: <number>

## Slide 2: H. Develop M&V Plan
When to develop and M&V Plan?
M&V Plan contents

## Slide 3: When to do an M&V Plan?
M&V Planning <number>
The M&V Plan should be developed while the EEMs are being designed in order to:
  include the cost of M&V when deciding project economics, and
  record baseline data and methodology for savings calculations while baseline conditions are still measurable before any savings happen.
The design of the data collection plan and procurement of any new metering equipment is done concurrently with the audit or while the EEM designs are being completed.
Notes: © Efficiency Valuation Organization
M&V Planning <number>
The energy user may have pre-decided to measure total facility performance (using Option C or D) or just to measure the retrofit (using Option A, B or D). This is the first part of the M&V design.
Section 2, Basic Steps of M&V, Step 1b), stressed the inability to go backwards in time to get some baseline data after retrofit. So you need to get baseline data while it is available.
There will always be a perception of bias in any baseline chosen after savings have actually happened.
Meter design can proceed in parallel with the retrofit design – to ensure optimum placement of meters and selection that suits the budget

## Slide 4: M&V Plan Contents
M&V Planning <number>
Document:
  The purpose of each EEM and its impact on operating conditions
  The measurement boundaries for each EEM (note there can be one or multiple measurement boundaries in a project)
  Interactive effects, if any, beyond the boundary
  Baseline energy/demand
  Identification of independent variables and their values during the baseline
  Conditions within the boundary during the baseline period
    Used as a basis for determining non-routine adjustments
  Reporting responsibilities in the reporting period
Notes: © Efficiency Valuation Organization
M&V Planning <number>
See IPMVP Chapter 5.

## Slide 5: M&V Plan Contents, cont.
M&V Planning <number>
Document
  The reporting period
  The adjustments to baseline and how they will be made
  Identify which Options will be used and describe the analysis methods
  Define the energy price or rates to be used
  Identify the measurement and metering points and procedures
  Define the quality assurance procedures (i.e. how will bad data be addressed, etc.)
  Estimate the expected costs and accuracy
  Define the report formats and frequency
Notes: © Efficiency Valuation Organization
M&V Planning <number>

## Slide 6: M&V Plan Contents, conclusion
M&V Planning <number>
Specifically for Option A:
Document the justification of the non-key parameters used
Define the periodic inspections that will be made after installation of equipment
For Option D:
Document the name and software version used for simulation
Provide the input data files and describe the method of measuring any parameters used to support input values
Provide the output from software
Describe how the simulation was calibrated (reference calibration criteria)
Notes: © Efficiency Valuation Organization
M&V Planning <number>