## Slide 1
Introduction to Energy and Building Science Fundamentals

## Slide 2: Measurement Tools & Verification of Savings Calculations A. Role of Measurement & Verification in energy efficiency, renewable energy, or demand response process
Notes: <number>

## Slide 3: A. Role of Measurement & Verification
What is M&V?
M&V within an energy efficiency, renewable, or demand response project
Why M&V is important
Uses of M&V
Other benefits

## Slide 4: What is Measurement & Verification?
Formal definition is found in Chapter 2 of the International Performance Measurement & Verification Protocol, Volume I: www.evo-world.com.
  “Measurement & Verification (M&V) is the process of using measurements to reliably determine actual savings created within an individual facility by an energy management program.”

## Slide 5: Measurement & Verification
Energy savings cannot be measured, because it represents the absence of energy use.
Savings are determined by making a fair comparison of energy use before and after a project is implemented.
The comparison is fair if the baseline and post-installation energy use is made under the same set of conditions (i.e. weather, occupancy, etc.)

## Slide 6: Conceptually ‘Measuring Savings’
Notes: The pink line shows the measured energy use in a building over many years.
During the baseline period (entire period not shown) an audit was conducted, EEMs were recommended and approved, and implemented in the time between the baseline and post-installation periods. Note that the energy use starts going down.
A mathematical model is developed using baseline period data, and projected into the post-installation period – represented by the blue line.
The savings is represented by the difference between the lines in the post-installation period.
<number>

## Slide 7: M&V Within a Project Process
Based on an energy audit, a building owner decides to invest in an energy efficiency project because it will lower utility bills and has a high return on investment
The owner is relying on the accuracy of the audit’s savings calculations, and that the project will be installed correctly, and will generate savings
The M&V process verifies whether or not the project yields the expected savings

## Slide 8: Audit and M&V Process Comparison
Project Phase
Audit
Implementation
Verification
Audit Activity
- Prepare, conduct site visit
- Collect data and information
- Identify EEMs, quantify savings and costs
- Evaluate cost-effectiveness
- Deliver audit report
- Owner installs EEMs
- EEMS commissioned
M&V Activity
- Assess EEM impact
- Define measurement boundary
- Collect baseline data
- Develop M&V Plan
- Collect post-install data
- Verify savings
- Repeat
Notes: This side-by-side process comparison shows important steps in both the audit and the M&V process.
Note that the audit process stops when the report is delivered. An owner must then ‘take over’ and select EEMs for installation, and manage that process.
The implementation process may be simple or complicated, such as hiring contractors and overseeing their work. To make sure the EEMs are installed correctly, owner’s may require a commissioning process be completed. This does not always take place however.
Many things can go wrong, and there is no way to know whether the EEMs actually saving energy until the M&V process is complete. Note the only post-installation phase activities are in the M&V process.
<number>

## Slide 9: Why is M&V Important?
Savings estimates from audits are of unknown quality – may be good or bad
EEMs may not be correctly installed and result in no savings
EEMs may be installed correctly but staff insufficiently trained on proper operation – savings quickly degrade
Notes: Distinguish between ex-ante and ex-post.
Ex-ante: activity prior to an event
Ex-post: activity after an event
The event is installation of energy efficiency measures (EEMs), which cause a change in energy performance.
<number>

## Slide 10: Why M&V Important?
Provides rigorous 2nd check on savings
To assure savings actually achieved
To assure utility costs have gone down
To assure a return on investment
As a basis of payments to an ESCO
Notes: ESCO means energy services company. Such companies offer pay for performance services directly to customers under energy performance contracts. The general process is:
ESCO performs a detailed audit of customers facilities. Report identifies savings and costs for ESCO to manage and install the EEMs.
ESCO guarantees the savings if customer hires ESCO to install and commission EEMs. If customer does not hire ESCO, customer pays for audit. There are different types of guarantees:
Shared savings (requires detailed M&V)
Guaranteed minimum savings (preferred by ESCOs)
M&V is used to determine actual savings after EEMs are installed.
<number>

## Slide 11: Uses of M&V
As a Quality Assurance Process
  Like ‘savings insurance’
  Rigorous – not a ‘2nd opinion’
  Relies on measurements
  Able to estimate savings uncertainty
Payment basis for ESCO projects
  ESCO guarantees savings, gets paid from owner’s operations budget

## Slide 12: Other Benefits of M&V
Persistence of Savings
  Provides periodic or continuous update on facility/equipment/EEM energy performance
Facilitates ‘Energy Awareness’ for Owner & Occupants
  Energy dashboards
Basis for continuous energy improvement programs