## Slide 1: Measurement Tools & Verification of Savings Calculations C. Savings Calculation Fundamentals
Notes: <number>

## Slide 2: C. Savings Calculation Fundamentals
Fundamental concept of savings calculations
Adjustments
  Routine
  Non-routine

## Slide 3: Quantifying Savings
IPMVP Chapter 3:
Energy Savings = Baseline Energy Use – Post-Retrofit Energy Use ± Adjustments
Adjustments are:
  Routine
  Non-Routine

## Slide 4: Routine Adjustments
Normal and expected variations in energy use due to operating conditions, weather, normal production rates, etc.
Equation becomes:
  Energy Savings = Adjusted Baseline Energy
  – Post-Installation Period Energy
  ± Non-Routine Adjustments

## Slide 5: Energy Models
Energy models describe how baseline energy use is affected by routine parameters of interest
Energy models can be:
  Mathematical equations: kWhsave = kW (HRSbase – HRSpost)
  Statistical relationships: kWhsave = f (Toutside, time-of-week)
  Complex computer simulations of buildings: DOE-2, EnergyPlus, eQUEST
The model enables one to determine what baseline use would have been under post-installation or any other conditions

## Slide 6: Savings
Measured post-install use is subtracted from adjusted baseline to calculate Avoided Energy Use
Normalized Savings are calculated from baseline and post-install energy use under different conditions
  e.g. typical meteorological year (TMY)
  requires post-install model as well
Avoided Energy Use

## Slide 7: Non-Routine Adjustments
Unexpected changes in energy use due to:
  Tenants moving in or out
  Chiller failure and replacement
  New building loads (office eqp., servers, etc.)
  Major renovations
Accounting for impact:
  Measure or estimate non-routine energy impact
    Quantity and duration
  Remove from adjusted baseline

## Slide 8: Non-Routine Adjustments
<number>

## Slide 9: Non-Routine Adjustment
<number>