## Slide 1: Chapter Six
Understanding and Using Ladder Diagrams
Notes: <number>

## Slide 2: Objectives
Identify a wiring diagram
Identify the parts of a wiring diagram
Convert a wiring diagram to a ladder diagram
List the rules that govern a ladder diagram

## Slide 3: Wiring Diagrams
Show circuit wiring and associated devices
  In relative physical location
Figure 6-1 Wiring diagram

## Slide 4: Ladder Diagrams
Show electrical relationship of components
Also called schematics
Figure 6-1 Ladder diagram

## Slide 5: Ladder Diagram Rules
Read like a book
  Left to right, top to bottom
Vertical power lines represent voltage potential
Devices shown in order of importance
Electrical devices shown in their normal condition

## Slide 6: Ladder Diagram Rules (cont’d.)
Contacts have same number or letter designation as controlling device
Contacts change position when the device is energized
STOP function devices normally wired in series
  START function devices normally wired in parallel

## Slide 7: Basic STOP/START Circuit
Figure 6-9 Ladder diagram for basic STOP/START circuit

## Slide 8: Sequenced Motor Starting
Figure 6-11 Three-motor start circuit

## Slide 9: Digital Logic Gates
Programming alternative to ladder logic
AND
  Both inputs must be true before output is true
OR
  At least one input must be true before output is true
NOT
  Inverts the input

## Slide 10
Figure 6-13 Two-input AND gate with truth table
Figure 6-15 Two-input OR gate with truth table

## Slide 11
Figure 6-14 Two input devices wired in series with truth table

## Slide 12
Figure 6-16 Two input devices wired in parallel with truth table

## Slide 13
Figure 6-17 NOT gate with truth table
Figure 6-19 NAND gate with truth table

## Slide 14
Figure 6-21 NOR gate with truth table
Figure 6-23 XOR gate with truth table

## Slide 15: Summary
Two types of electrical diagrams
  Wiring diagrams show physical location and wiring
  Ladder diagrams show electrical relationships
    Vertical sides of the diagram called rails
    Horizontal lines called rungs
Two or more devices wired in series:
  Perform an AND function

## Slide 16: Summary (cont’d.)
Two or more devices wired in parallel:
  Perform an OR function
Logic gates represent motor control device logic in a circuit
Common logic gates: AND, OR, NOT, NOR, NAND, XOR
Gates combine to create complex control circuits