## Slide 1: Chapter Two
Understanding the
Input/Output (I/O) Section
Notes: <number>

## Slide 2: Objectives
Describe the I/O section of a programmable controller
Identify DIP switches
Describe how basic AC and DC input and output modules work
Define optical isolation and describe why it is used
Notes: <number>

## Slide 3: Objectives (cont’d.)
Describe the proper wiring connections for input and output devices and their corresponding modules
Explain why a hard-wired emergency-stop function is desirable
Define the term interposing
Notes: <number>

## Slide 4: Objectives (cont’d.)
Describe what I/O shielding does
List environmental concerns when installing PLCs
Notes: <number>

## Slide 5: I/O Section
Changes voltage or current signal into a logic-level signal:
  Compatible with the processor
Input modules provide ON/OFF status of buttons, switches to the processor
Signal sent to output device based on program logic
Notes: <number>

## Slide 6: Fixed I/O
Complete unit containing processor, I/O section, and power supply
Add expansion units with various I/O configurations:
  To provide more capability or different voltages
Notes: <number>

## Slide 7
Figure 2-2 SLC 500 fixed I/O chassis with optional two-slot expansion
Notes: <number>

## Slide 8: Modular I/O
More flexible than fixed I/O units
Various types of input and output modules
  Housed in a rack or chassis
Local I/O
  I/O modules mounted with the processor
Remote I/O
  Processor is mounted remotely from I/O
Notes: <number>

## Slide 9: Modular I/O (cont’d.)
Jumpers or switches used to configure racks
  DIP switches commonly used
Device connections must have a distinct address
  Used to communicate with the processor
Notes: <number>

## Slide 10: Discrete I/O Modules
Only accept digital or ON/OFF signals
Discrete input module
  Communicates status of real-world input device to the processor
  Available in a wide range of voltages
  Contains multiple input terminals
Notes: <number>

## Slide 11: Discrete I/O Modules (cont’d.)
AC discrete input module
Figure 2-7 Simplified AC input module circuit with indicator light
Notes: <number>

## Slide 12: Discrete I/O Modules (cont’d.)
DC discrete input module
Figure 2-13 Simplified circuit for DC input module with indicator light
Notes: <number>

## Slide 13: Discrete I/O Modules (cont’d.)
Fast-responding DC input modules
  Used with high-speed or high volume applications
  Examples: encoders, proximity switches to count product from high-speed machine
  Delay in filtering circuit less than 1 millisecond
Notes: <number>

## Slide 14: Discrete I/O Modules (cont’d.)
Discrete output modules
  Control current flow to real-world devices
  Signals are digital
  Classified as AC or DC
  Sized by number of devices that can be connected
Notes: <number>

## Slide 15: Discrete I/O Modules (cont’d.)
AC output module
Figure 2-15 Typical AC output module circuit
Notes: <number>

## Slide 16: Discrete I/O Modules (cont’d.)
Output fuses
  Provide protection for overcurrent, shorts, or ground faults
Status lights
  Indicate that output point has been turned ON
Notes: <number>

## Slide 17: Discrete I/O Modules (cont’d.)
Module keying
  Notches prevent wrong type of module from being installed
DC output modules
  Same operation as AC output modules
  Use a power transistor to control output current
Notes: <number>

## Slide 18: Discrete I/O Modules (cont’d.)
Sourcing and sinking
  If a device provides current, it is sourcing
  If a device receives current, it is sinking
Contact output modules
  Electromechanical relay used to open or close a set of contacts
Notes: <number>

## Slide 19: Discrete I/O Modules (cont’d.)
Interposing relay
  Used to control loads larger than the current rating of an individual output circuit
Reed relay output module
  Used when dry reed relays desirable
Transistor-transistor logic I/O modules
  Compatible with other solid-state controls
Notes: <number>

## Slide 20: Analog I/O Modules
Analog input modules
  Used to convert analog signals to binary
  For use by the PLC logic
Analog output module
  Changes binary into analog signals
  Example of use: controlling variable speed controllers
Notes: <number>

## Slide 21
Figure 2-29 Analog input module
Notes: <number>

## Slide 22: Safety Circuit
Hardwired emergency stop
  Removes power to the output devices
  Independent of the PLC program
  Required by NEMA standard when operator is exposed to machinery
Emergency stop relay (ESR) contact
  Used for safe system restart
Notes: <number>

## Slide 23: Rack Installation
Factors to consider
  Temperature
  Dust
  Vibration
  Humidity
  Wiring distances
  Accessibility for troubleshooting
Notes: <number>

## Slide 24: Electrical Noise (Surge Suppression)
Electrical noise
  Generated when inductive loads are operated by hard contacts
  High transient voltages when inductive device switched OFF
Methods to reduce or eliminate noise
  Isolation
  Suppression
Notes: <number>

## Slide 25: Grounding
Helps eliminate effects of electromagnetic induction
Equipment grounding conductor
  Attached to metal frame of PLC
Notes: <number>

## Slide 26: I/O Shielding
Shielded cable reduces effect of electrical noise
Shield should only be grounded at one end
Shield should be terminated at the I/O rack
Notes: <number>

## Slide 27: Summary
I/O rack houses input and output modules
  Modules connect to real-world devices
I/O categories
  Fixed or modular
  Digital or analog
Consider environmental conditions when installing PLC equipment
Notes: <number>