## Slide 1: Chapter One
What is a Programmable Logic Controller (PLC)?
Notes: <number>

## Slide 2: Objectives
Describe several advantages of a programmable logic controller (PLC) over hard-wired relay systems
Identify the four major components of a typical programmable logic controller and describe the function of each
Notes: <number>

## Slide 3: Objectives (cont’d.)
Define the term discrete
Define the term analog
Identify different types of programming devices
Notes: <number>

## Slide 4: Programmable Logic Controller
Solid-state system for control and operation of manufacturing equipment
  Replaces relays, switches, counters
Lack of hard wiring allows frequent changes to programming
Uses RELAY LADDER LOGIC
  High level, graphic programming language
Notes: <number>

## Slide 5: PLC Characteristics
Designed to be operated by plant engineers and maintenance personnel
Designed to operate in an industrial environment
  Variations in temperature, vibration, humidity
Not usually affected by electrical noise
Notes: <number>

## Slide 6
Figure 1-1 Comparison of a Computer System and a PLC
Notes: <number>

## Slide 7: PLC Components
Processor unit
  Microprocessor “brain”
Power supply
  Converts 120 or 240 AC volts to low voltage DC
  Can be a separate unit
Notes: <number>

## Slide 8
Figure 1-5 Block diagram of a typical power supply
Notes: <number>

## Slide 9: PLC Components (cont’d.)
Input/Output interface
  Input device examples
    Buttons, switches, sensors
  Output device examples
    Motor coils, solenoid valves, lights
Programming device
  Used to enter desired program into memory
  Computer is most common device
Notes: <number>

## Slide 10: Types of I/O Devices
Discrete
  Either ON or OFF, open or closed
  Examples: limit switches and push buttons
Analog
  Have a range of possible values
  Examples: temperature and pressure sensors
Notes: <number>

## Slide 11: Summary
PLCs are used to control process machinery
Programmable for fast, easy changes in RELAY LADDER LOGIC
PLCs are designed to be used by technicians
  Easy to program
Notes: <number>