## Slide 1: Chapter Four
Memory Organization
Notes: <number>

## Slide 2: Objectives
Identify the two broad categories of memory and describe the function of each
Identify the types of information stored in each category of memory
Define the term byte
Define the acronym bits
Define holding registers
Notes: <number>

## Slide 3: Memory Words and Word Locations
Binary signals have only two states
  ON or OFF
  1 or 0
  High or low
Bit: binary digit
Binary words can be 32, 16, or 8 bits in length
Notes: <number>

## Slide 4
Figure 4-1 16-bit word
Notes: <number>

## Slide 5: Memory Words and Word Locations (cont’d.)
Byte: group of 8 bits
Address: memory storage location
Addressing scheme also identifies hardware location
  Rack, module, terminal number
Notes: <number>

## Slide 6
Figure 4-2 Relationship of bit address to input and output devices
Notes: <number>

## Slide 7
Figure 4-4 Limit switch address I:013/12
Notes: <number>

## Slide 8: SLC 500 and MicroLogix Addressing Scheme
Letter I used for input addresses
Letter O used for output addresses
Figure 4-7 Allen-Bradley SLC 500 and MicroLogix addressing scheme
Notes: <number>

## Slide 9: Memory Organization
Storage memory
  Entire storage memory called data table or register table
  Data can be stored in a variety of numbering systems
User memory
  Holding registers store temporary data needed by the processor
Notes: <number>

## Slide 10: Allen-Bradley PLC-5 File Structure
Allen-Bradley PLC-5 processors
  Programmed with a PC and PLC-5 specific software
Files
  Areas of memory
Memory section 0: output image file
File 1: input image file
Notes: <number>

## Slide 11: Allen-Bradley PLC-5 File Structure (cont’d.)
File 2: status file
File 3: bit file
File 4: timer file
File 5: counter file
File 6: control file
File 7: integer file
  Stores whole numbers
Notes: <number>

## Slide 12
Figure 4-16 PLC-5 file structure
Notes: <number>

## Slide 13: SLC 500 and MicroLogix File Structure
Program files (user)
  Contain controller information, programs, and subroutines
Data files (storage)
  Contain various types of data for use with the program
Notes: <number>

## Slide 14: Summary
All PLC data is stored in binary form
  Allows rapid scanning and executing the user program
I/O addresses
  Identify word and bit associated with I/O
  Indicate the hardware location
Memory section names vary by PLC manufacturer, but work similarly
Notes: <number>