## Slide 1: Chapter Three
Processor Unit
Notes: <number>

## Slide 2: Objectives
Describe the function of the processor
Describe a typical program scan
Identify the two distinct types of memory
Describe the function of the watchdog timer
Identify various memory designs
Notes: <number>

## Slide 3: The Processor
Consists of microprocessor, chips, circuits
Memory and communication circuits
  May be separate from microprocessor module
Notes: <number>

## Slide 4
Figure 3-1 Basic PLC configuration
Notes: <number>

## Slide 5: The Processor (cont’d.)
Microprocessor scan
  Monitors status of input devices
  Executes logic of user program
  Controls state of output devices
  Communicates with other devices
  Manages memory and updates timers, counters, registers
Notes: <number>

## Slide 6
Figure 3-3 Typical processor scan
Notes: <number>

## Slide 7: The Processor (cont’d.)
Watchdog timer
  Sets time limit for each scan
  Puts processor into fault condition if timer exceeded
User memory
  Stores user program containing relay logic
Storage memory
  Stores status, accumulated values, etc.
Notes: <number>

## Slide 8: The Processor (cont’d.)
Volatile memory
  Loses information when power is removed
Nonvolatile memory
  Retains stored information when power is removed
Notes: <number>

## Slide 9: Memory Types
Random Access Memory (RAM)
  Common type of volatile memory
  Often called read/write memory
Read Only Memory (ROM)
  Stored information cannot be changed
Programmable Read Only Memory (PROM)
  Can be written to once only
Notes: <number>

## Slide 10: Memory Types (cont’d.)
Ultra Violet Programmable Read Only Memory (UVPROM)
  Also called Erasable Programmable Read Only Memory (EPROM)
  Semi permanent storage
  Used when security needed to prevent unauthorized changes
Notes: <number>

## Slide 11: Memory Types (cont’d.)
Electrically Erasable Programmable Read Only Memory (EEPROM)
  Chip can be programmed and erased
  Erased by sending proper signal to erase pin
  Used primarily as nonvolatile backup for user program RAM
Notes: <number>

## Slide 12: Memory Size
Expressed in K values (example: 16K)
Binary system used in PLCs
  Base 2
  Digits are 1s and 0s
PLCs may use 8-bit or 16-bit words
Required memory size depends on application
Notes: <number>

## Slide 13: Programming Devices
Needed to enter, modify, and troubleshoot the PLC program, or to check the condition of the processor
Two types
  Hand-held: see Figures 3-9 and 3-11 in the text
  Computer: see Figure 3-10 in the text
    More display, documentation, and storage options
Notes: <number>

## Slide 14: Guarding Against Electrostatic Discharge (ESD)
ESD
  Discharge of static electricity
  Major cause of failure of memory chips
Precautions
  Use nonstatic floor coverings
  Handle chips correctly
  Ground the work surface
  Wear a wrist strap
Notes: <number>

## Slide 15: Memory Structure
Two general classifications
  User memory
  Storage memory
Specific PLC memory structure information
  Review individual manufacturer literature
Notes: <number>

## Slide 16: Summary
Processor tasks
  Monitor status of the inputs
  Execute steps in the user program
  Control condition of the outputs
User program stored in memory
Memory types: volatile and nonvolatile
Notes: <number>