## Slide 1: Chapter Eight
Programming a PLC
Notes: <number>

## Slide 2: Objectives
Explain the term On-line programming
Describe basic programming techniques
Describe the Force On and Force Off features, and the hazards that could be associated with both
Notes: <number>

## Slide 3: Introduction
On-line programming
  Changing the program while the processor is running
Off-line programming
  Program is developed while not connected to the process or equipment
Most PLCs have override capability
  Force On and Force Off
Notes: <number>

## Slide 4: Programming with a Computer
Rockwell RSLogix software
  Used for programming examples in the text
  Windows-based
  User friendly
Start RSLogix software by double-clicking the RSLogix icon
Notes: <number>

## Slide 5
Figure 8-1 SLC 5/03 processor mounted in a 4-slot chassis
Notes: <number>

## Slide 6
Figure 8-2 Basic STOP/START circuit
Notes: <number>

## Slide 7
Figure 8-3 RSLogix opening screen
Notes: <number>

## Slide 8: Programming with a Computer (cont’d.)
Click on File, New
  Select Processor Type window appears
  Scroll to find processor you are using
Assign a name, and click OK
Left side of screen: project tree
Right side of screen: programming area
Notes: <number>

## Slide 9
Figure 8-4 Select Processor Type screen
Notes: <number>

## Slide 10
Figure 8-7 Controller screen
Notes: <number>

## Slide 11: Programming with a Computer (cont’d.)
Double-click Controller folder
Double-click Controller Properties
  Shows memory used and memory left
Close Controller Properties
Double-click IO Configuration
  Select appropriate configuration from pull-down list
Notes: <number>

## Slide 12
Figure 8-9 IO Configuration screen
Notes: <number>

## Slide 13: Programming with a Computer (cont’d.)
To determine the correct power supply to use:
  Single-click on the Power Supply button
  Power Supply Loading window opens
  Displays minimum recommended power supply
Notes: <number>

## Slide 14: Programming with a Computer (cont’d.)
Data Files folder displays file status
  I/O files
  Binary file
  Timer file
  Counter file
  Control file
  Integer file
  Floating point file
Notes: <number>

## Slide 15
Figure 8-14 Data File window
Notes: <number>

## Slide 16: Programming with a Computer (cont’d.)
Data File window
  Shows status of first three words of input file
Symbol tells what the device is
  Example: PB 1 (pushbutton 1)
Description explains what the input device does
  Example: Stop
Notes: <number>

## Slide 17
Figure 8-19 Program area with rung added
Notes: <number>

## Slide 18
Figure 8-20 Simple STOP/START circuit without overloads
Notes: <number>

## Slide 19: Programming with a Computer (cont’d.)
Steps to program circuit in Figure 8-20
  Program STOP button by clicking Normally Open contact symbol
  Enter STOP button address
  Program START button by clicking BRANCH START symbol button
  Move dark vertical line to upper left corner
Notes: <number>

## Slide 20: Programming with a Computer (cont’d.)
Steps to program circuit in Figure 8-20 (cont’d.)
  Click on N.O. symbol to add the next contact
  Click question mark to enter the address
  Enter symbol and description for address I:1/1
  Add the holding contact for the motor starter
  Program the output device: motor starter 1
Notes: <number>

## Slide 21
Figure 8-34 Completed STOP/START circuit
Notes: <number>

## Slide 22: Programming with a Computer (cont’d.)
To check finished program for correctness:
  Click Verify Project button
Verify result shown in lower left corner of screen
  Verify has completed; no errors found
  Or error will be identified by rung number
Notes: <number>

## Slide 23: Programming with the Logix5000 Software
Programming example:
  Use RSLogix 5000 to program a ControlLogix 1756-L62 processor mounted in a 4-slot chassis: see Figure 8-37 in text
  Will be the same simple STOP/START circuit that was used in prior example
Notes: <number>

## Slide 24
Figure 8-49 Input Module 1756-IA16 Data Points
Notes: <number>

## Slide 25
Figure 8-63 Completed STOP/START circuit
Notes: <number>

## Slide 26: Summary
PLC is programmed using specific PLC software
  Operational codes and addresses used
Programs usually developed and tested in Off-Line mode
Contacts or coils can be forced ON or OFF while circuit is operational
Notes: <number>