## Slide 1: Chapter 24
Photoelectric Semiconductors, Fiber Optics, and Light-Based Applications
Section 24-1 Photoelectric Devices
Section 24-2 Photoelectric Sensors
Section 24-3 Fiber Optics
Section 24-4 Photoelectric Sensor Applications
Section 24-5 Photoelectric Control Applications
Notes: Chapter 24-<number>

## Slide 2: Objectives Section 24-1 Photoelectric Devices
Describe photoelectric devices.
Define and describe PIN photodiodes.
Define and describe phototransistors.
Define and describe light-activated silicon-controlled rectifiers (LASCRs).
Define and describe phototriacs.
Define and describe light-emitting diodes (LEDs).
Define and describe optocouplers.
Notes: Chapter 24-<number>

## Slide 3
A solid-state switch uses a triac, SCR, NPN (current sink) transistor, or PNP (current source) transistor output to perform the switching function.
Notes: Photoelectric devices typically contain solid-state output switches. A solid-state switch has no moving parts (contacts). A solid-state switch uses a triac, SCR, NPN (current sink) transistor, or PNP (current source) transistor output to perform the switching function. See Figure 24-1. The triac output is used for switching AC loads. The SCR output is used for switching high-power DC loads. The current sink and current source transistor outputs are used for switching low-power DC loads. Solid-state switches include normally open (NO), normally closed (NC), or combination switching outputs.
Chapter 24-<number>

## Slide 4
A PIN photodiode is a diode with a large intrinsic region sandwiched between P-type and N-type regions.
Notes: A PIN photodiode is a diode with a large intrinsic region sandwiched between P‑type and N‑type regions. PIN stands for P‑type material, insulator, and N‑type material. See Figure 24-2. The operation of a PIN photodiode is based on the principle that light radiation, when exposed to a PN junction, momentarily disturbs the structure of the PN junction. The disturbance is due to a hole created when a high‑energy photon strikes the PN junction and causes an electron to be ejected from the junction. Thus, light creates electron‑hole pairs that act as current carriers. PIN photodiodes are used in gas detectors, spectrometers, and gas analyzers.
Chapter 24-<number>

## Slide 5
A phototransistor is a device that combines the effect of a photodiode and the switching capability of a transistor.
Notes: A phototransistor is a device that combines the effect of a photodiode and the switching capability of a transistor. The symbol for a phototransistor is similar to the symbol for a standard transistor except with the addition of two arrows that represent a light source pointing into the transistor. See Figure 24-3. A phototransistor, when connected in a circuit, is placed in series with the bias voltage so that it is forward biased.
Chapter 24-<number>

## Slide 6
A light-activated SCR (LASCR) is an SCR that is activated by light.
Notes: A light‑activated SCR (LASCR) is an SCR that is activated by light. The symbol of an LASCR is identical to the symbol of a regular SCR with one difference. The only difference is that arrows are added in the LASCR symbol to indicate a light‑sensitive device. See Figure 24-4.
Chapter 24-<number>

## Slide 7
A phototriac is a triac that is activated by light.
Notes: A phototriac is a triac that is activated by light. See Figure 24-5. The gate of a phototriac is light sensitive. It triggers the triac at a specified light intensity. In darkness, the triac is not triggered. The remaining leakage current is referred to as peak blocking current. A phototriac is bilateral and designed to switch AC signals.
Chapter 24-<number>

## Slide 8
A light-emitting diode (LED) is a semiconductor diode that produces light when current flows through it.
Notes: A light-emitting diode (LED) is a semiconductor diode that produces light when current flows through it. As electrons move across the depletion region, they give up extra kinetic energy. The extra energy is converted to light. An electron must acquire additional energy to get through the depletion region. This additional energy comes from the positive field of the anode. If the positive field is not strong, the electron will not get through the depletion region and no light will be emitted. See Figure 24-6.
Chapter 24-<number>

## Slide 9
A laser diode is similar to an LED but with an optical cavity that is required for lasing production (emitting coherent light).
Notes: A laser diode is a diode similar to an LED but with an optical cavity that is required for lasing production (emitting coherent light). The optical cavity is formed by coating opposite sides of a chip to create two highly reflective surfaces. See Figure 24-7.
Chapter 24-<number>

## Slide 10
An optocoupler consists of an IRED as the input stage and an NPN phototransistor as the output stage.
Notes: An optocoupler is an electrically isolated device that consists of an IRED as the input stage and an NPN phototransistor as the output stage. An optocoupler is normally constructed as a dual inline package. See Figure 24-8.
Chapter 24-<number>

## Slide 11: 24-1 Checkpoint
What solid-state device is used to switch high-power DC loads?
What distinguishes the symbol for a phototransistor from the symbol for a standard transistor?
If an LASCR is required to switch a higher power load, how is the LASCR used?
What is the difference between the symbol for a photodiode and the symbol for an LED?
Notes: Chapter 24-<number>

## Slide 12: Objectives Section 24-2 Photoelectric Sensors
Define photoelectric sensor.
Describe AC photoelectric sensors.
Describe DC photoelectric sensors.
Notes: Chapter 24-<number>

## Slide 13
AC photoelectric sensors are connected in series with the loads they control.
Notes: AC photoelectric sensors switch AC circuits. An AC photoelectric sensor is connected in series with the load that it controls. The sensor is connected between line 1 (L1) and the load to be controlled. See Figure 24-9. Because AC photoelectric sensors are connected in series with the load, special precautions must be taken. The three main factors considered when connecting AC photoelectric sensors include load current, operating (residual) current, and minimum holding current.
Chapter 24-<number>

## Slide 14
Load current is the amount of current drawn by a load when energized and flows through AC photoelectric sensors.
Notes: Load current is the amount of current drawn by a load when energized. Because a solid-state sensor is wired in series with the load, the current drawn by the load must pass through the solid-state sensor. For example, if a load draws 5 A, the sensor must be able to safely switch 5 A. Five amperes burns out most solid-state proximity sensors because they are normally rated for a maximum of less than 0.5 A. An electromechanical or solid-state relay must be used as an interface to control the load if a solid-state sensor must switch a load above its rated maximum current. A solid-state relay is the preferred choice for an interface with a sensor. See Figure 24-10.
Chapter 24-<number>

## Slide 15
Operating current is the amount of current a sensor draws from the power lines to develop a field that can detect a target.
Notes: Operating current (residual or leakage current) is the amount of current a sensor draws from the power lines to develop a field that can detect a target. When a sensor is in the OFF condition (target not detected), a small amount of current passes through both the sensor and the load. This operating current is required for the solid-state detection circuitry housed within the sensor. Operating currents are normally in the range of 1.5 mA to 7 mA for most sensors. See Figure 24-11.
Chapter 24-<number>

## Slide 16
Minimum holding current is the minimum amount of current required to keep a sensor operating.
Notes: Minimum holding current is the minimum amount of current required to keep a sensor operating. When the sensor has been triggered and is in the ON condition (target detected), the current drawn by the load must be sufficient to keep the sensor operating. Minimum holding currents range from 3 mA to 20 mA for most solid-state sensors. The amount of current a load draws must be correct for the proper operation of a sensor. Excessive current (operating current) burns up the sensor. Low current (minimum holding current) prevents proper operation of the sensor. See Figure 24-12.
Chapter 24-<number>

## Slide 17
AC photoelectric sensors may be connected in series or parallel.
Notes: All AC two-wire photoelectric sensors may be connected in series or parallel to provide both AND and OR control logic. When connected in series (AND logic), all sensors must be activated to energize the load. When connected in parallel (OR logic), any one sensor that is activated energizes the load. See Figure 24-13.
Chapter 24-<number>

## Slide 18
When an NPN (current sink) transistor is used, the load is connected between the positive terminal of the supply voltage and the output terminal of the sensor.
Notes: When using an NPN transistor, the load is connected between the positive terminal of the supply voltage and the output terminal (collector) of the sensor. When the sensor detects a target, current flows through the transistor and the load is energized. See Figure 24-14.
Chapter 24-<number>

## Slide 19
When a PNP (current source) transistor is used, the load is connected between the negative terminal of the supply voltage and the output terminal of the sensor.
Notes: When using a PNP transistor, the load is connected between the negative terminal of the supply voltage and the output terminal (collector) of the sensor. When the sensor (current source) detects a target, current flows through the transistor and the load is energized. See Figure 24-15.
Chapter 24-<number>

## Slide 20: 24-2 Checkpoint
Can a transistor output be used in a photoelectric switch to switch an AC load?
Can a triac output be used in a photoelectric switch to switch a DC load?
Does the operating current of a two-wire photoelectric switch affect low impedance or high impedance loads more?
As a general rule, how many two-wire photoelectric sensors can be connected in series or parallel?
Notes: Chapter 24-<number>

## Slide 21: Objective Section 24-3 Fiber Optics
Define and describe fiber optics.
Notes: Chapter 24-<number>

## Slide 22
Fiber optics connect two electronic circuits consisting of a transmitter and a receiver.
Notes: Fiber optics is a technology that uses a thin, flexible glass or plastic optical fiber to transmit light. Fiber optics is most commonly used as a transmission link. As a transmission link, it connects two electronic circuits consisting of a transmitter and a receiver. See Figure 24-16.
Chapter 24-<number>

## Slide 23
Optical fibers consist of a core, cladding, and protective jacket.
Notes: Optical fibers consist of a core, cladding, and protective jacket. See Figure 24-17. The core is the actual path for light in an optical fiber cable. The core is normally made of glass but may occasionally be constructed of plastic. Cladding is the first layer of protection for the glass or plastic core of an optical fiber cable. A glass or plastic cladding layer is bonded to the core. The cladding is enclosed in a jacket for additional protection.
Chapter 24-<number>

## Slide 24
Improper connection of optical fiber cables can result in poor or no transmission.
Notes: Splices and fiber interconnections are often more of a negative factor than poor quality materials because of alignment problems that can arise, such as fiber gap, lateral offset, and angular misalignment. The elimination of alignment problems can be accomplished through proper installation of fiber splices, connectors, and couplers. See Figure 24-18.
Chapter 24-<number>

## Slide 25: 24-3 Checkpoint
What two materials can be used for core of optical fiber?
Why are signals sent over an optical fiber cable not affected by electrical noise such as external magnetic fields produced by motors and other coils?
What are three poor splice problems that can occur and cause reduced data transfer in fiber optics?
Notes: Chapter 24-<number>

## Slide 26: Objectives Section 24-4 Photoelectric Sensor Applications
Describe how photoelectric sensors are used.
Define photoelectric scanning and list the most common scanning techniques.
Explain the difference between modulated and unmodulated light.
Explain response time and sensitivity adjustment.
Explain the difference between dark-operated and light-operated photoelectric controls.
Notes: Chapter 24-<number>

## Slide 27
Photoelectric sensors are used to detect objects without touching the objects.
Notes: Photoelectric sensors can detect most materials and have a longer sensing distance than ultrasonic and proximity sensors. Depending on the model, photoelectric sensors can detect objects from several millimeters to over 100′ away. The maximum sensing distance of any sensor is determined by the size, shape, color, and character of the surface of the object to be detected. Many sensors include an adjustable sensing distance, making it possible to exclude detection of the background of the object. Photoelectric sensors are used in applications in which the object to be detected may be excessively light, heavy, hot, or untouchable. See Figure 24-19.
Chapter 24-<number>

## Slide 28
The scanning method used for an application depends on the environment of the scanning area.
Notes: The phototransmitter and photoreceiver may be set up for several different scanning techniques. The best technique depends on the particular application. The scanning method used for an application depends on the environment of the scanning area. In many applications, several methods of scanning work, but normally one method is the best. See Figure 24-20.
Chapter 24-<number>

## Slide 29
Direct scan is a method of scanning in which the target is detected as it passes between the transmitter and receiver.
Notes: Direct scan (transmitted beam, thru-beam, opposed scan) is a method of scanning in which the transmitter and receiver are placed opposite each other so that the light beam from the transmitter shines directly at the receiver. The target must pass directly between the transmitter and receiver. The target size should be at least 50% of the diameter of the receiver lens to block enough light for detection. See Figure 24-21. For very small targets, a special converging lens or aperture may be used.
Chapter 24-<number>

## Slide 30
Retroreflective scan is a method of scanning in which the target is detected as it passes between the photoelectric sensor and reflector.
Notes: Retroreflective scan (retro scan) is a method of scanning in which the transmitter and receiver are housed in the same enclosure and the transmitted light beam is reflected back to the receiver from a reflector. The light beam is directed at a reflector that returns the light beam to the receiver when no target is present. When a target blocks the light beam, the output switch is activated. See Figure 24-22.
Chapter 24-<number>

## Slide 31
Polarized scan uses a special lens that filters the beam of light from the emitter so it is projected in one plane only.
Notes: Polarized scan is a method of scanning in which the receiver responds only to the depolarized reflected light from corner cube reflectors or polarized sensitive reflective tape. The light source (emitter) and photoreceiver in a polarized scanner are located on the same side of the object to be detected. A special lens filters the beam of light from the emitter so that it is projected in one plane only. See Figure 24-23. The receiver ignores the light reflected from most varieties of shrink-wrap materials, shiny luggage, aluminum cans, or common reflective objects. Thus, the receiver picks up the reflection from the reflector but cannot pick up the reflection from most shiny targets.
Chapter 24-<number>

## Slide 32
Specular scan is a method of scanning in which the transmitter and receiver are placed at equal angles from a highly reflective surface.
Notes: Specular scan is a method of scanning in which the transmitter and receiver are placed at equal angles from a highly reflective surface. The angle at which light strikes the reflective surface equals the angle at which it reflects from the surface. This is similar to billiards in which a ball leaves the cushion at an angle equal to the angle at which it struck the cushion. See Figure 24-24.
Chapter 24-<number>

## Slide 33
Diffuse scan is a method of scanning in which the target is detected when some of the emitted light is reflected and received.
Notes: Diffuse scan (proximity scan) is a method of scanning in which the transmitter and receiver are housed in the same enclosure and a small percentage of the transmitted light beam is reflected back to the receiver from the target. In diffuse scan, the transmitter and the receiver are placed in the same enclosure so the receiver picks up some of the diffused (scattered) light. The target detected may be large or small. See Figure 24-25.
Chapter 24-<number>

## Slide 34
Convergent beam scan is a method of scanning that simultaneously focuses and converges a light beam to a fixed focal point in front of a photoreceiver.
Notes: Convergent beam scan is a method of scanning that simultaneously focuses and converges a light beam to a fixed focal point in front of a photoreceiver. See Figure 24-26. Glass optical fiber cables are used with photoelectric sensors to conduct the transmitted light into and out of the sensing area. The optical fiber cables are used as light pipes.
Chapter 24-<number>

## Slide 35
Fiber optics use transparent fibers of glass or plastic to conduct and guide light energy.
Notes: A control beam is transmitted through an optical fiber cable and returned to the receiver through a separate cable either combined in the same cable assembly (known as a bifurcated fiber bundle) or within a separate cable assembly. Retroreflective scan and diffuse scan use a bifurcated cable and direct scan uses two separate cables (emitter and receiver). See Figure 24-27. Scan distances commonly vary from 0.4″ to 54″, depending on the scanning technique. An optical lens accessory that attaches to certain cable ends significantly increases scan distances.
Chapter 24-<number>

## Slide 36
Fiber-optic controllers are available in different sizes and configurations.
Notes: Fiber-optic controllers are available in different sizes and configurations. See Figure 24-28. Combining the optical fiber cables with photoelectric sensors enables their use in limited mounting spaces and for small parts detection and detection in applications having high temperature, high vibration, or high electrical noise levels.
Chapter 24-<number>

## Slide 37
Modern photoelectric sensors use modulated or unmodulated light.
Notes: Although some older photoelectric transmitters used white light (unmodulated), modern photoelectric light sources produce infrared light, which can be either modulated or unmodulated. Most photoelectric sensors today use modulated infrared light. See Figure 24-29.
Chapter 24-<number>

## Slide 38
The response time of a photoelectric control is the number of pulses per second the sensor can detect.
Notes: Response time is the number of pulses (objects) per second a controller can detect. The response time of a photoelectric control must be considered when the object to be detected moves past the beam at a very high speed or when the object to be detected is not much bigger than the effective beam of the controller. This information is listed in the specification sheet of the photoelectric control. For example, a photoelectric control may have an activating frequency of 10 pulses per second. This means the photoelectric control, on average, can detect an object passing by it every 1/10 (0.1) sec. See Figure 24-30.
Chapter 24-<number>

## Slide 39
Many photoelectric sensors have adjustment screws for setting sensitivity of operation and may also have a screw to adjust time delay.
Notes: Many photoelectric and proximity sensors have a sensitivity adjustment screw that determines the operating point or the intensity of light that triggers the output. See Figure 24-31. This adjustment allows the sensitivity to be set between a minimum and maximum range. The adjustment is made after the unit has been installed and the minimum and maximum settings for the application are experimentally determined. The sensitivity adjustment is normally set halfway between the minimum and maximum points.
Chapter 24-<number>

## Slide 40
A photoelectric control can have a dark-operated or light-operated mode.
Notes: Basic photoelectric controls are designed to be dark-operated. A dark-operated photoelectric control is a photoelectric control that energizes the output switch when a target is present (breaking the beam). Some photoelectric controls include an optional feature that allows the control to be set in a light-operated mode. A light-operated photoelectric control is a photoelectric control that energizes the output switch when the target is missing (removed from the beam). See Figure 24-32.
Chapter 24-<number>

## Slide 41: 24-4 Checkpoint
What type of scanning method works best when other reflective surfaces are in the same area but must not affect the sensor detecting the actual target reflector?
What type of scanning method provides the longest detection distance because the light travels in only one direction and is considered the best first choice when selecting a detection method?
What type of scanning method works best when detecting a color mark used to register the location of a product or point on a product?
Does a modulated or unmodulated light source work best in a high ambient light area, such as when a machine is used under a skylight?
When detecting an object, when is the known response time of a photoelectric sensor important?
When an attempt is made to detect an object once it breaks the light beam, should a dark-operated or light-operated mode be used?
Notes: Chapter 24-<number>

## Slide 42: Objective Section 24-5 Photoelectric Control Applications
Explain how to properly mount photoelectric sensors.
Notes: Chapter 24-<number>

## Slide 43
Photoelectric sensors may be used to monitor a truck loading bay for clearance and distance.
Notes: Photoelectric sensors may be used to monitor a truck loading bay for clearance and distance. See Figure 24-33. In this application, any truck 14′-0″ or larger must be unloaded at another bay. (The dimensions vary depending on particular needs.) In the control circuit, photoelectric sensor 1 (PHOTO 1) turns on an alarm in line 2 if the truck is too high. Photoelectric sensor 2 (PHOTO 2) starts a recycle timer (TR) that flashes a yellow light on and off at a distance of 2′ from the dock. Photoelectric sensor 3 (PHOTO 3) starts a recycle timer that turns on a red light at a distance of 6″ from the dock.
Chapter 24-<number>

## Slide 44
Photoelectric sensors may be used to detect a backup of a product on a conveyor line.
Notes: Photoelectric sensors may be used to detect a backup of a product on a conveyor line. See Figure 24-34. In this application, three photoelectric sensors are used to turn on a warning light and turn off the conveyor motor if required.
Chapter 24-<number>

## Slide 45
A transmitter is mounted on the clean side of the detection zone because light scattered by dirt on the transmitter lens affects the system more than light scattered by dirt on the receiver lens.
Notes: A receiver is positioned to receive as much light as possible from the transmitter when photoelectric sensors are mounted. When more light is available at the receiver, greater operating distances are allowed and more power is available for the system to see through dirt and debris in the air and on the transmitter and receiver lenses. The transmitter is mounted on the clean side of the detection zone because light scattered by debris on the transmitter lens affects the system more than light scattered by debris on the receiver lens. See Figure 24-35.
Chapter 24-<number>

## Slide 46: 24-5 Checkpoint
In the truck loading bay application shown in Figure 24-33, is it best to use a modulated or unmodulated light source?
In the conveyor line application shown in Figure 24-34, what type of scanning method is used to detect the product?
Notes: Chapter 24-<number>