## Slide 1: What is Demand Response
Demand response (DR) is a load management tool which provides a cost-effective alternative to traditional supply-side solutions to address the growing demand during times of peak electrical load.
The California Energy Commission (CEC) defines DR as “a reduction in customers’ electricity consumption over a given time interval relative to what would otherwise occur in response to a price signal, other financial incentives, or a reliability signal.”
This definition is most reflective of how DR is understood and implemented today in countries such as the US, Canada, and Australia.
  DR is primarily a “dispatch-able” resource responding to signals from utilities, grid operators, and/or load aggregators (or DR providers).
Notes: Addressing Energy Demand through Demand Response: International Experiences and Practices , Authors: Bo Shen, Girish Ghatikar, Chun Chun Ni, and Junqiao Dudley. Environmental Energy Technologies Division
Lawrence Berkeley National Laboratory. Phil Martin and Greg Wikler
ENERNOC, INC. June 2012
LBNL-5580E
<number>

## Slide 2: Understanding the Benefits
Summarize some of the benefits of demand response programs:
  Demand response is less expensive than using natural gas-fired peaking power plant. The capital cost required to build out 1MW of demand response capacity is of the order of $240,000 versus $400,000 for a gas-fired plant, a 40% cost savings.
  Demand response capacity managed by a large, technology-enabled demand response provider, can be dispatched in a very short time (less than 5 minutes), whereas a peaking power plant can take up to 30 minutes to ramp up to full capacity.
  By reducing the stress on the grid and keeping wholesale electricity prices down during peak demand, demand response also facilitates the sale of power in the wholesale markets from a region with surplus capacity to another in need of the extra capacity, thus ensuring nationwide grid reliability.
  Demand response is a clean source of capacity since it does not generate greenhouse and other toxic emissions unlike a power plant.
  Demand response capacity is more reliable than peaking power plant capacity, as it can be sourced from a large and diversified geographic region.
Notes: http://downloads.lightreading.com/internetevolution/Thomas_Weisel_Demand_Response.pdf
White Paper on Demand Response. The Power Grid: Evolving from a “Dumb” Network to a “Smart” Grid. Jeff Osborne and Dilip Warrier, 10/16/2007.
<number>

## Slide 3: Types of DR Programs
Demand response programs are established to motivate changes in electricity use by end-use customers in response to changes in the price of electricity over time, or to give incentive payments designed to induce lower electricity use at times of high-market prices or when grid reliability is jeopardized:
  Price-based demand response programs such as real-time pricing (RTP), critical peak pricing (CPP) and time-of-use (TOU) tariffs, charge customers time-varying rates that reflect the value and cost of electricity in different time periods. Customers who have access to the electricity rates they are paying, tend to use less electricity when electricity prices are high
  Incentive-based demand response programs pay participating customers to reduce their loads at times requested by the program sponsor, triggered either by a grid reliability problem or high electricity rates

## Slide 4: Utility DR Programs for Business
Business Programs
  Peak Day Pricing: Price discount to conserve energy during times of peak demand
  Base Interruptible Program: Incentives to reduce your businesses’ consumption to a level that you preselect.
  Demand Bidding Program: Incentives to reduce consumption when we notify you of a Demand Response event day.
  Scheduled Load Reduction Program: Get paid to reduce consumption to a previously agreed level; customer specifies the time period and the days in advance.
  Opt-In Binding Mandatory Curtailment Plan: Reduce the overall load of your facility and avoid rotating outages during high demand periods
Notes: http://www.pge.com/en/mybusiness/save/energymanagement/index.page
<number>

## Slide 5: DR Programs for Aggregators
Aggregator Managed Portfolio:
  A non-tariff program of bilateral contracts with aggregators to provide utility with price-responsive Demand Response
Capacity Bidding Program
  A monthly incentive to reduce energy by a previously agreed amount once an electric-resource generation facility reaches a pre-determined level
Notes: http://www.pge.com/en/mybusiness/save/energymanagement/index.page
DR Aggregators: are demand response providers
<number>

## Slide 6: DR Enablement Incentives
Technology Incentives
  Financial incentive to help businesses invest in energy management technologies that will enable them to take part in Demand Response.
Automated Demand Response Incentive
  Provides funds to help businesses pre-program energy management and control systems. These allow us to automatically initiate previously agreed load reduction strategies during times of high demand.
  ADR Program incentives, as defined by category of technology selected:
    Semi-Automated Demand Response $125
    Automated Demand Response $200
    Emerging & Advanced Technology HVAC/R $350
    Emerging & Advanced Technology Lighting $400