## Slide 1
ACADs (08-006) Covered
Keywords cosmic terrestrial internal radiation, uranium, thorium, radium, curie, becquerel, roentgen, dose, RAD, REM, x-rays, gamma, beta, alpha, fission fragments, mrad, tissue, organ, affect on cells, blood, whole body exposure, acute, chronic, genetic, body burden, time distance shielding, gonads
Description This module examines the affects of short and long term exposure to all types of radiation.
Supporting Material
1.1.4.5 | 1.1.8.2 | 1.1.8.3 | 1.1.8.3.1 | 1.1.8.3.2 | 1.1.8.3.3
3.3.2.1 | 3.3.2.2 | 3.3.4.4.1 | 3.3.4.4.2 | 3.3.4.4.5 | 3.3.4.4.6
4.10.1.1 | 4.10.1.2 | 4.10.1.3 | 4.10.1.4 | 4.10.2 | 4.12.1.1
4.12.1.2 | 4.12.1.3 | 4.12.1.4 | 4.12.2 |  | 
Notes: If you edit other slides, use Arial (Headings) 36 flush left for titles and Arial (Body) 24 for body text.
<number>

## Slide 2: Sources of Radiation Exposure in the US
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 3: Natural Sources of Radiation
Natural background radiation comes from three sources:
  Cosmic Radiation
  Terrestrial Radiation
  Internal Radiation
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 4
Cosmic Radiation
  Sun and stars send constant stream of cosmic radiation to Earth
    Like steady drizzle of rain
  Differences in certain variables can change the amount (or dose) of cosmic radiation that we receive.
    Elevation
    Atmospheric conditions
    Earth's magnetic field
NET 130
Module 3: Biological Effects of Radiation
<number>
Natural Sources of Radiation

## Slide 5
Terrestrial Radiation
  The Earth itself is a source of terrestrial radiation
  Radioactive materials exist naturally in soil and rock
    Uranium
    Thorium
    Radium
  Water contains small amounts of dissolved uranium and thorium
  All organic matter (both plant and animal) contains radioactive carbon and potassium.
NET 130
Module 3: Biological Effects of Radiation
<number>
Natural Sources of Radiation

## Slide 6
Internal Radiation
  All animals (including people) have internal radiation
  Comes from radioactive potassium-40 and carbon-14 inside their bodies
    Present from birth
    Very minor sources of exposure to others
NET 130
Module 3: Biological Effects of Radiation
<number>
Natural Sources of Radiation

## Slide 7: Man-Made Sources of Radiation
All living things are exposed to natural background radiation
Exposure to man-made radiation sources differs by group:
  Members of the Public
  Occupationally Exposed Individuals (Workers)
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 8
NET 130
Module 3: Biological Effects of Radiation
<number>
Members of the Public
  Medical Sources (by far, the most significant man-made source)
    Diagnostic x-rays
    Nuclear medicine procedures (iodine-131, cesium-137, and others)
Man-Made Sources of Radiation

## Slide 9
NET 130
Module 3: Biological Effects of Radiation
<number>
Consumer Products
  Building and road construction materials
  Combustible fuels, including gas and coal
  X-ray security systems
  Televisions
  Fluorescent lamp starters
  Smoke detectors (americium)
Man-Made Sources of Radiation

## Slide 10
NET 130
Module 3: Biological Effects of Radiation
<number>
Consumer Products
  Luminous watches (tritium)
  Lantern mantles (thorium)
  Tobacco (polonium-210)
  Ophthalmic glass used in eyeglasses
  Some ceramics
Man-Made Sources of Radiation

## Slide 11
NET 130
Module 3: Biological Effects of Radiation
<number>
Occupationally Exposed Individuals (Workers)
  Industrial radiography (X-ray imaging)
  Nuclear medicine departments
    Radiology (medical imaging, X-rays, etc)
    Radiation oncology (cancer treatment)
  Nuclear power plants
  Nuclear fuel cycle facilities
    Production
    Disposal
  Government and university research laboratories
Man-Made Sources of Radiation

## Slide 12: Radiation Measurement Units
Radioactive Material Quantity
  Curie :: the amount of radioactive material decaying at 2.22 X 10 12 atoms per minute or 3.7 X 10 10 atoms per second
    1 ci = 3.7 X10 10 decays per second (dps)
  Becquerel :: the amount of radioactive material decaying at 1 decay per second
    1 ci = 3.7 × 1010 Bq
    1Bq = 1 dps
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 13
NET 130
Module 3: Biological Effects of Radiation
<number>
Biological Effects
  Not fully described by decay rate of radioactive material
  Additional factors must considered
    Radiation type
    Radiation energy
Radiation Measurement Units

## Slide 14: Radiation Measurement Units: Roentgen (R)
Relates to gamma or x-ray interactions in air
Relates to energy deposition in air
Qty of x-ray or gamma radiation producing 1 esu of charge (positive or negative) in 1 cc (cm3) of dry air
  esu = electrostatic unit of charge
  1 ionizing event = addition or removal of 1 electron = ±4.8 X10 -10 esu
  1 R = 2.08 X10 9 ion pairs
  1 R = 88 erg/gram energy deposition in air
    erg = unit of work or energy
Problem: Doesn’t relate to biological damage.
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 15: Radiation Measurement Units: Radiation Absorbed Dose (RAD)
Dose = Total amount of energy delivered to a specific area or organ by radiation.
Dose rate = dose units per unit of time
1 RAD is an amount of any type of ionizing radiation that deposits 100 ergs/gram in tissue.
1 RAD = 100 ergs/gram energy deposition (tissue)
Problem: Different types of ionizing radiation might have the same energy, but have totally different effects on tissue.
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 16: Radiation Measurement Units: Roentgen Equivalent Man (REM)
The amount of ionizing radiation required to produce the same biological effect as one rad of high-penetration x-rays.
Radiation dose in rem is referred to as the dose equivalent (DE)
DE (rem) = Dose (rad) x QF
Quality Factor (QF)
  Accounts for differences in biological effect for different types of radiation
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 17: Quality Factor
Gamma, X-Rays, and High-Energy Beta
  1 rad = 1 rem
Alpha, Proton, Neutron, and Low-Energy Beta
  1 rad  1 rem
  1 rem = 1 rad * QF
NET 130
Module 3: Biological Effects of Radiation
<number>
RADIATION | QUALITY FACTOR
GAMMA | 1
X | 1
BETA, ELECTRON>0.03 MeV | 1
BETA, ELECTRON < 0.03 MeV | 1.7
THERMAL NEUTRONS | 3
FAST NEUTRONS | 10
PROTONS | 10
ALPHA | 10
HEAVY IONS | 20

## Slide 18: Different Radiation Types
Biological effect of any radiation is related to rate at which radiation transfers energy to tissue
Linear Energy Transfer (LET)
  Measure of the interaction density along radiation travel path
  Equivalent to ionization potential or stopping power of body tissue
  Inversely proportional to radiation range
    Short range particles like alphas have a high LET
Most damaging types of radiation to a biological system are those with a high LET.
High LET radiation deposits all of its energy in a short distance of travel.
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 19
LET increases with:
  Increasing mass of incident radiation
  Increasing charge of incident radiation
  Decreasing energy of incident radiation
In order of decreasing LET:
  Fission fragments
  Low mass number nuclei
  Alpha particles
  Protons
  Neutrons
  Low energy Beta, x-ray and gamma
  High energy beta, x-ray and gamma
NET 130
Module 3: Biological Effects of Radiation
<number>
Different Radiation Types
Notes: <number>

## Slide 20: Relationship between LET and QF
NET 130
Module 3: Biological Effects of Radiation
<number>
LINEAR ENERGY TRANSFER (LET) (KeV/micron in water) | QUALITY FACTOR (QF)
3.5 or less | 1
3.5 – 7.0 | 1 – 2
7.0 – 23 | 2 – 5
23 - 53 | 5 – 10
53 – 175 | 10 - 20

## Slide 21: Example 1
The total dose of alpha particles to an individual is three rad. Calculate the dose equivalent in rem using the appropriate Quality Factor (QF).
NET 130
Module 3: Biological Effects of Radiation
<number>
RADIATION | QUALITY FACTOR
GAMMA | 1
X | 1
BETA, ELECTRON>0.03 MeV | 1
BETA, ELECTRON < 0.03 MeV | 1.7
THERMAL NEUTRONS | 3
FAST NEUTRONS | 10
PROTONS | 10
ALPHA | 10
HEAVY IONS | 20

## Slide 22: Example 2
As measured by instruments, an individual was exposed to radiation field consisting of 5 mrad gamma, 2 mrad beta, and 5 mrad fast neutrons. Calculate the dose equivalent in rem.
NET 130
Module 3: Biological Effects of Radiation
<number>
RADIATION | QF
GAMMA | 1
X | 1
BETA, ELECTRON>0.03 MeV | 1
BETA, ELECTRON < 0.03 MeV | 1.7
THERMAL NEUTRONS | 3
FAST NEUTRONS | 10
PROTONS | 10
ALPHA | 10
HEAVY IONS | 20

## Slide 23: Biological Organization
Cell – basic unit of the human body
Tissue - cells with similar structure performing same function
Organ – cells with different structure (different tissues) performing similar overall function
System – group of organs performing common function
Organism
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 24
NET 130
Module 3: Biological Effects of Radiation
<number>
Biological Organization: Cell
Cell membrane
  protects cell from external influences, such as toxins
  “gatekeeper”
Cytoplasm
  80% water
  Helps convert nutrients into energy
  Location of biochemical reactions for bodily functions
nucleolus
nucleus
ribosome
vesicle
rough endoplasmic reticulum (ER)
Golgi apparatus
cytoskeleton
smooth endoplasmic reticulum
mitochondria
vacuole
cytoplasm
lysosome
centrioles within centrosome
Image source: Wikimedia.org
(public domain)

## Slide 25
NET 130
Module 3: Biological Effects of Radiation
<number>
Biological Organization: Cell
Nucleus
  Contains instructions for:
    Cellular reproduction
    Cellular function
      Contained within chromosomes
Chromosomes
  Strands of amino acids (deoxyribonucleic acids – DNA)
  Abnormal bodily function if damaged or malformed
Image source:
Wikimedia.org
(public domain)

## Slide 26
NET 130
Module 3: Biological Effects of Radiation
<number>
Segment of DNA Strand
Image source:
Wikimedia.org
(public domain)

## Slide 27: Cellular Effects of Radiation
Free radical formation
Direct radiation damage
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 28
Radical
  An atom (either neutral or charged) with unpaired electrons that wants to join with another atom to stabilize itself
Free radicals
  Radicals that have not yet bonded with other atoms
  Highly reactive atoms or chemical compounds that can alter existing state of cells
Changes in cellular chemistry are the root causes of all the harmful effects of radiation.
NET 130
Module 3: Biological Effects of Radiation
<number>
Cellular Effects of Radiation: Free Radical Formation

## Slide 29
Direct Effect of Radiation on Cells
  Ionization and excitation of intracellular water molecules produces free radicals
Indirect Effect of Radiation on Cells
  Subsequent interference of free radicals with cells not direct affected by radiation
NET 130
Module 3: Biological Effects of Radiation
<number>
Cellular Effects of Radiation: Free Radical Formation

## Slide 30
NET 130
Module 3: Biological Effects of Radiation
<number>
Radiolysis: production of free radicals in water
Radiolysis by Ionization: Hydrogen Radical (H. )
  Electron absorbed
  Hydrogen radical and hydroxyl ion formed
. = radical
Cellular Effects of Radiation: Free Radical Formation

## Slide 31
NET 130
Module 3: Biological Effects of Radiation
<number>
Radiolysis by Ionization:
Hydroxyl Radical (OH. )
  Electron removed from water molecule
  Positively ionized water removes hydrogen from neutral water to form hydroxyl radical
Cellular Effects of Radiation: Free Radical Formation

## Slide 32
NET 130
Module 3: Biological Effects of Radiation
<number>
Radiolysis by Excitation:
Hydrogen and Hydroxyl Radicals
  Incident electron excites water molecule, but is not absorbed
  Excited water molecule splits into hydrogen and hydroxyl radicals
Cellular Effects of Radiation: Free Radical Formation
* = excited

## Slide 33
NET 130
Module 3: Biological Effects of Radiation
<number>
Most of these radicals immediately react with each other to produce harmless compounds
However, they might react with other molecules in the cell, causing damage
Cellular Effects of Radiation: Free Radical Formation
Hydrogen Gas
Hydrogen Peroxide
Water

## Slide 34
Cell may die
Cell may reproduce but new cells may die
Cell may reproduce producing abnormal cells
Cell may repair itself and function normally
NET 130
Module 3: Biological Effects of Radiation
<number>
Cellular Effects of Radiation

## Slide 35
NET 130
Module 3: Biological Effects of Radiation
<number>
DNA radiation damage
Cellular Effects of Radiation
Image source:
Wikimedia.org
(public domain)

## Slide 36
NET 130
Module 3: Biological Effects of Radiation
<number>
Molecular
  Damage to enzymes, DNA etc. and interference with biological pathways
Subcellular
  Damage to cell membranes, nucleus, chromosomes etc.
Cellular Inhibition of cell division, cell death, transformation to a malignant state
Effects of Radiation by Biological Organization

## Slide 37
NET 130
Module 3: Biological Effects of Radiation
<number>
Tissue, Organ
  Disruption to central nervous system, bone marrow, intestinal tract
  Induction of cancer
Whole Animal
  Death
  Life shortening
Populations
  Changes in the genetic characteristics of individual members
Effects of Radiation by Biological Organization

## Slide 38: Radiosensitivity
Different cells within the body have different structures and functions
Vary in their radiosensitivity
  Susceptibility to radiation-induced damage
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 39
Cellular division rate
  Rapidly dividing cells are more sensitivity to radiation damage
Cellular metabolism rate
  Cells with high metabolism rate are more susceptible to radiation damage
Developmental stage
  Cells in division stage are more susceptible to radiation damage
Blood / nourishment to cell
  Normally undernourished cells reproduce less
  Faster reproduction = more mutations
NET 130
Module 3: Biological Effects of Radiation
<number>
4 Factors Affecting Radiosensitivity

## Slide 40: Organ / Tissue Radiation Effects
Organ / tissue radiosensitivity influenced by 2 factors
  Radiosensitivity of the tissue/organ cells
  Importance to overall organism
Most radiosensitive organs and tissues
  Blood (tissue)
  Blood-forming organs
  Gonads (reproductive organs)
  Lens of the eye
  Skin
Least radiosensitive organ
  Brain (cells do not reproduce)
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 41: Organ / Tissue Radiation Effects
Blood
  One of the most radiosensitive tissues in the human body
  Normal blood cells have an already short lifespan and high metabolic rate
    Take in toxins quickly
Gonads (reproductive organs)
  Mutations occurring in egg or sperm cells could result in a mutation in the offspring
  100 rads: temporary depletion of sperm count
  300 to 400 rad: function of ovaries impaired
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 42
NET 130
Module 3: Biological Effects of Radiation
<number>
Organ / Tissue Radiation Effects: Blood
BLOOD CELL TYPE | FUNCTION | PRODUCTION SITE | LIFETIME OF CELL | EFFECT OF SINGLE RADIATION EXPOSURE OF > 100 RADS
Red (Erythrocytes) | Carry oxygen and nutrients to body | Bone marrow | 100 days | Slight decrease in number
Lymphocyte (type of white blood cell) | Fight infection | Lymph nodes and spleen | 1 day | Highly radiosensitive; decrease in number increases with dose; decrease within 2 days after exposure; large decrease in number can result in infection
Euthrophils (type of white blood cells) | Fight infection | Bone marrow | 7 days | Highly radiosensitive; decrease in number proportional to dose; depletion results in infection and fever
Platelets | Blood clotting | Bone marrow | 7 – 10 days | Highly radiosensitive; decrease in number increases with dose; decrease in number can result in hemorrhaging

## Slide 43
First tissue to exhibit noticeable radiation injury
High radiosensitivity due to the high rate of cell division and degree of exposure
400 to 500 rad: Erythema (reddening)
Higher dose: blistering and ulceration may occur
Long term complications: scarring and skin cancer
NET 130
Module 3: Biological Effects of Radiation
<number>
Organ / Tissue Radiation Effects: Skin
Image source:
Wikimedia.org
(public domain)

## Slide 44
NET 130
Module 3: Biological Effects of Radiation
<number>
May result in cataract formation (cloudiness)
Single dose of 200-500 rad
Cumulative (spread over several months) dose of 1000 rad
Organ / Tissue Radiation Effects: Lens of the Eye
Image source:
Wikimedia.org
(public domain)

## Slide 45: Radiation Effects on Humans
Four factors:
  Radiation type
  Area exposed
  Total dose
  Dose rate
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 46
For radiation of same type, range in tissue increases with increasing energy
Depth of penetration is function of type of radiation
Charged particles and neutrons will not penetrate as far as electromagnetic radiation
Linear Energy Transfer (LET)
  LET depends on charge, mass, and energy
  Higher LET = higher QF = more biological damage
NET 130
Module 3: Biological Effects of Radiation
<number>
Radiation Effects on Humans: Radiation Type

## Slide 47
Whole Body Exposure
  Irradiation of all cells, organs, and tissues
  Symptoms depends on which organ is sensitive at the given dose level
Partial Body Exposure
  Damage limited to tissues and organs within exposed area
  Very high localized doses of radiation are used to treat certain cancers without significant damage to the rest of the body
NET 130
Module 3: Biological Effects of Radiation
<number>
Radiation Effects on Humans: Portion of Body Exposed

## Slide 48
Biological damage decreases with decreasing dose rate
Acute Exposure
  High dose
  Short exposure time
Chronic Exposure
  Low dose
  Long exposure time
  Occupational radiation exposure
  Exposure from natural background radiation
NET 130
Module 3: Biological Effects of Radiation
<number>
Radiation Effects on Humans: Rate of Exposure

## Slide 49: Acute Radiation Effects: Whole Body Exposure
Subclinical Range (0 to 100 rem)
  No sickness occurs which requires medical attention
  Some changes occur in the blood for doses near 100 rem
Therapeutic Range (100 to 200 rem)
  Nausea, vomiting, loss of appetite, and fatigue
  Blood damage more severe
  Redness of the skin
Lethal Range (>200 rem)
  Nausea and vomiting become more severe
  Internal hemorrhaging may occur
  Hair loss at 300 rem
  200 - 600 rem: small percentage of people will die within 30 days
  600 - 1000 rem: higher chance of death
  >1000 rem: Certain death
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 50
NET 130
Module 3: Biological Effects of Radiation
<number>
Dose (Rads*) | Effects
25-50 | First sign of physical effects (drop in white blood cell count)
100 | Threshold for vomiting (within a few hours of exposure)
320 - 360 | ~ 50% die within 30 days (with minimal supportive care)
480 - 540 | ~50 % die within 30 days (with supportive medical care)
1,000 | ~ 100% die within 30 days
Acute Radiation Effects: Whole Body Exposure

## Slide 51
NET 130
Module 3: Biological Effects of Radiation
<number>
RANGE | 0 TO 100 REMS SUBCLINICAL RANGE | 100 TO 1,000 REMS THERAPEUTIC RANGE |  |  | OVER 1,000 REMS LETHAL RANGE |  | 
 |  | 100 TO 200 REMS | 200 TO 600 REMS | 600 TO 1,000 REMS | 1,000 TO 5,000 REMS |  | OVER 5,000 REMS
 |  | CLINICAL SURVEILLANCE | THERAPY EFFECTIVE | THERAPY PROMISING | THERAPY PALLIATIVE |  | 
Incidence of vomiting | None | 100 rems: 5% 200 rems: 50% | 300 rems = 100% | 100% | 100% |  | 
Delay time | - | 3 hours | 2 hours | 1 hour |  |  | 
Leading organ | None | Hematopoietic tissue |  |  | Gastrointestinal tract |  | Central nervous system
Characteristic signs | None | Moderate Leukopenia | Severe leucopenia; purpose; hemorrhage; infection. Hair loss above 300 rems. |  | Diarrhea; fever, disturbance of electrolyte balance |  | Convulsions; tremor; ataxia; lethargy
Critical period post exposure | - | - | 4 to 6 weeks |  | 5 to 14 days |  | 1 to 48 hours
Therapy | Reassurance | Reassurance; hematological surveillance | Blood transfusion; antibiotics | Consider bone marrow transplantation | Maintenance of electrolyte balance |  | Sedatives
Prognosis | Excellent | Excellent | Good | Guarded | Hopeless |  | 
Convalescent period | None | Several weeks | 1 to 12 months | Long | 90 to 100% |  | 
Incidence of death | None | None | 0 to 100% (variable) | 80 to 100% (variable) |  |  | 
Death occurs within | - | - | 2 months |  | 2 weeks | 2 days | 
Cause of death | - | - | Hemorrhage; infection |  | Circulatory collapse | Respiratory failure | 

## Slide 52: Acute Radiation Effects: Localized Exposure
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 53
NET 130
Module 3: Biological Effects of Radiation
<number>
Acute Radiation Effects: Localized Exposure

## Slide 54
NET 130
Module 3: Biological Effects of Radiation
<number>
Acute Radiation Effects: Localized Exposure

## Slide 55
Telangiectasia
  Dilation (expansion) of the blood vessels in the skin
  Some areas receive excessive blood flow, diverting blood away from other areas
  The cells that LOSE blood flow suffer from oxygen deprivation
Erythema
  Early Transient: Slight inflammation of skin due to inflamed blood vessels
  Main: more severe inflammation
  Late: Severe inflammation of skin due to damaged blood vessels
NET 130
Module 3: Biological Effects of Radiation
<number>
Acute Radiation Effects: Localized Exposure

## Slide 56
Erythema
  Early Transient: Slight inflammation of skin due to inflamed blood vessels
  Main: more severe inflammation
  Late: Severe inflammation of skin due to damaged blood vessels
NET 130
Module 3: Biological Effects of Radiation
<number>
Acute Radiation Effects: Localized Exposure

## Slide 57
Acute Ulceration
  Early loss of outer skin cells (peeling)
Dermal Atrophy
  Thinning of the skin tissues
Epilation (hair loss)
Dry Desquamation
  Keratinization (hardening) of the skin
Moist Desquamation
  Skin loss due to inability of damaged skin cells to reproduce
Secondary Ulceration
  Skin damage due to dehydration and infection resulting from severe moist desquamation
NET 130
Module 3: Biological Effects of Radiation
<number>
Acute Radiation Effects: Localized Exposure

## Slide 58
NET 130
Module 3: Biological Effects of Radiation
<number>
Dermal Necrosis
  Cell/tissue death due to insufficient blood flow
Acute Epidermal Necrosis
  Severe tissue loss
  High-dose, low-energy beta irradiation
Acute Radiation Effects: Localized Exposure

## Slide 59: Chronic Radiation Effects: Whole Body Exposure
Human body tolerates small doses of radiation exposure better over a long period of time.
Human body –
  Repairs radiation damage
  Eliminates radiation-induced byproducts
….As long as the repair or elimination rate is larger than the production rate.
500 rem acute dose
  Severe radiation sickness
500 rem delivered at 10 rem per week
  Little noticeable effect
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 60
No permanent biological damage occurs unless total dose exceeds some value (threshold)
Limit long term chronic exposures to less than threshold values to protect against permanent damage
NET 130
Module 3: Biological Effects of Radiation
<number>
Chronic Radiation Effects: Threshold Effect

## Slide 61
Body continuously attempts to repair damage as it occurs
If damage too severe
  Repair mechanisms become strained
  Aging effects are increased
Continued exposure shortens average life span
May result in cancer
  Genetic mutation of cells
  Leukemia: Inability to produce white blood cells normally
NET 130
Module 3: Biological Effects of Radiation
<number>
Chronic Radiation Effects: Tissue Damage and Repair

## Slide 62: Genetic Effects of Radiation
Only seen in offspring of exposed workers
Changes to genetic information in reproductive cells due to damaged DNA structure
May be spontaneous changes due to background radiation
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 63
NET 130
Module 3: Biological Effects of Radiation
<number>
Occur in the exposed person
  Blood changes
  Skin reddening (erythema)
Depends on:
  Total Dose
  Dose Rate
  Region Exposed
  Body % Exposed
Somatic Effects of Radiation

## Slide 64: Internal Radiation Exposure
4 ways radionuclides can enter the body:
  Inhalation
  Swallowing
  Absorption
  Through Cuts
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 65: Critical or Target Organ Concept: Swallowing and Inhalation of Radionuclides
When swallowed, radionuclides pass through normal digestion processes.
When inhaled, radionuclides enter the lungs.
If soluble, transmitted through blood stream
In the blood stream, it travels through out the body.
Some organs have an affinity to specific elements – radioactive or not.
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 66
Example:
  Dial painters contract bone cancer after years of “pointing” the radium dipped brush with their tongues.
  Radium falls in same periodic table grouping as Calcium
    Replaces Calcium in bone.
  The target organ for Radium is bone.
NET 130
Module 3: Biological Effects of Radiation
<number>
Critical or Target Organ Concept
Image source:
Wikimedia.org
(public domain)
Image source:
Wikimedia.org
(public domain)

## Slide 67
NET 130
Module 3: Biological Effects of Radiation
<number>
Radium – Bone
Strontium – Bone
Cobalt – whole body
Cesium – large intestine
Iodine - Thyroid
Critical or Target Organ Concept

## Slide 68: Body Burden
Amount of internally-deposited radioactivity causing maximum permissible dose to any organ.
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 69: Protection from External Radioactivity
Time – minimize time exposed
Distance – Increase distance from source
Shielding – Increase shielding
NET 130
Module 3: Biological Effects of Radiation
<number>

## Slide 70
NET 130
Module 3: Biological Effects of Radiation
<number>
Administratively controlled: PREVENTION
  Respirators
  No eating / drinking in contaminated areas
  No open wounds
Protection from Internal Radioactivity