## Slide 1
ACADs (08-006) Covered
Keywords
Natural radiation, man-made radiation, exposure, terrestrial, extraterrestrial, cosmographic, radionuclide, decay chain, x-ray, medical radiation, norm.
Description
Supporting Material
1.1.4.5 | 3.2.3.9 | 3.3.2.1 | 3.3.2.2
4.10.1 | 4.10.2 | 4.12.1.1 | 
Notes: <number>

## Slide 2
The Natural Radiation Environment
The Man-Made Radiation Environment
Radiation Exposure to People
Summary
Background Radiation
Notes: <number>
Humans have been exposed to radiation since the beginning of time. The radiation levels on the planet have been pretty steady all throughout time. Up until the discovery and used of radioactive material humans were only exposed to natural radiation, but now we are exposed as well to man made radioactive materials.

## Slide 3
Radon
X-Rays
Consumer
Products
Nuclear
Power
Radioactive
Waste
Nuclear
Medicine
Solar Radiation
Cosmic Rays
Terrestrial
Radiation
Food &
Drink
Each
Other
  
Radiation in Life
Notes: <number>
Radiation has a place in almost every aspect of everyday life, from the food we eat to the products we use to the sun and medical applications. Radiation is energy traveling in the form of particles or waves in bundles of energy called photons. Some everyday examples are microwaves used to cook food, radio waves for radio and television, light, and x-rays used in medicine.

## Slide 4: Extraterrestrial Radiation
The primary source of cosmic radiation is from outside this solar system.
The atmosphere and the earth’s magnetic field act as a shield against incoming radiation, reducing the amount of radiation that actually reaches the earth’s surface.
The higher you rise in altitude, the higher your dose from cosmic radiation. The dose rate doubles every 1500 meters
Notes: <number>
Cosmic radiation can come in two forms, galactic cosmic radiation a solar particle events. GCR is from super novas and black holes , whereas the SPE are from the sun. the are some radionuclides that are produced by the interaction of the GCR and the upper atmosphere of the earth. The ionosphere and magnetosphere protect people on the surface of the Earth from all the radiation in space.

## Slide 5: Magnetic Fields
The Magnetic Field of the Earth stop some of the particles from the Solar wind and Galactic Radiation from penetrating to the surface
Notes: <number>
The magnetic field of the Earth helps shield the surface of the Earth from charged particles, the ionosphere helps protect fro the ions that are associated with solar particle events. Depending on your location Earth the cosmic radiation can be of variable strength.

## Slide 6
Relationship Between Altitude and Cosmic Radiation
      A dose of approximately 27 millirem/year at sea level doubles for every 1500 meter increase in elevation.
Notes: <number>
The amount of dose you receive from cosmic radiation is a relation of where you are on the Earth and what elevation you are. Usually people that live around the equator, even though they get most of the heat of the sun, generally receive less cosmic type radiation. The reason is that the atmosphere around the equator is thicker than it is near the poles, so the atmosphere functions as a shield for many of the radiation that comes from extraterrestrial sources. Elevation is a factor of how much radiation one receives from cosmic radiation for the same reason. The atmosphere is thinner at the poles that the equator this is why one can only see the northern an southern lights near the poles. There is an exception to the general rules of latitude and elevation and it is called the south Atlantic anomaly. This is a place in the south Atlantic ocean off the coast of south America where the radiation levels are much higher than expected

## Slide 7
Is radioactivity that is produced when the incoming cosmic radiation interacts with the upper atmosphere of the earth
The stable atoms, mostly N, in the upper atmosphere interact with cosmic radiation to produce radionuclides.
  Carbon-14, essential to the carbon dating process
  Hydrogen-3, or tritium, is formed when cosmic rays interact with nitrogen, oxygen, or lithium in the atmosphere.
Cosmogenic radioactivity
Notes: <number>
Many different types of radioactive materials are produced in our upper atmosphere from the interaction of the high energy cosmic radiation the molecules in the air. The two main ones are tritium and carbon –14. Both materials filter their way down through the atmosphere and get incorporated into the biological systems of every living thing.

## Slide 8
Radionuclide Series - There are four different decay chains (series) of primordial radionuclides.
To determine the series, divide the mass number of the parent isotope by four and there will be a constant remainder for all radionuclides in the series
These radionuclides include U-238, Pu-241, Th-232 and U-235. These are called “chain radionuclides”
Terrestrial Radiation: Chains or Series
Notes: <number>
Most of the naturally occurring radioactive material comes from one of the 4 naturally occurring decay chains of the primordial radionuclides. These decay chains of include some of the more well know radioactive materials such as Radium and Radon.

## Slide 9
  4n Series - Thorium (Th-232); half-life 1.39 x1010 years
  4n+1 Series - Neptunium (Pu-241); half-life 13.2 years
  4n+2 Series - Uranium (U-238); half-life 4.5x 109 years
  4n+3 Series - Actinium (U-235); half-life 7.13x108 years
Terrestrial Radiation: Chains or Series
Notes: <number>
Most of the naturally occurring radioactive material comes from one of the 4 naturally occurring decay chains of the primordial radionuclides. These decay chains of include some of the more well know radioactive materials such as Radium and Radon.

## Slide 10
General characteristics of radionuclide series:
    The first parent of each series has a half-life that is typically on the order of hundreds of millions of years (i.e., the age of the Earth).
    The final nuclide of each series is a stable isotope of lead.
    Each series has a different isotope of the radioactive gas radon.
Terrestrial Radiation: Chains or Series
Notes: <number>
Most of the naturally occurring radioactive material comes from one of the 4 naturally occurring decay chains of the primordial radionuclides. These decay chains of include some of the more well know radioactive materials such as Radium and Radon.

## Slide 11
Radon and the Uranium Decay Series
Uranium-238
4.5E9 y
Radium-226
1600 y
Radon-222
3.825 days
Lead-214
27 min (RaB)
Polonium-218
3.1 min (RaA)
Polonium-214
163.7 sec (RaC’)
Bismuth-214
19.9 min (RaC)
Lead-210
22.3 y (RaD)
Notes: <number>
Uranium eventually decays into Ra-226 then into Rn-222 and then to Po-218. But the interesting phase change happens in this process. Ra is a solid but Rn is a gas and Po is a solid again. So one of the properties of Rn that makes it so mobile is that it is a gas and can migrate through the soil and get released to either the atmosphere or into a enclosed structure (basement or house). The accumulation in Rn in enclosed spaces may become a problem.

## Slide 12
1. Cracks in Solid Floors
2. Construction Joints
3. Cracks in Walls
4. Gaps in Floors
5. Gaps around Pipes
6. Cavities in Walls
7. The Water Supply
3.
4.
1.
2.
7.
6.
5.
How Does Radon Get in the Home?
Notes: <number>
Rn can enter your house in many ways. But it depends on if your house is in an area that is prone to Rn and has an space in which Rn can accumulate many buildings that have a earth floor basement or other on enclosed area can accumulate Rn.

## Slide 13: NORM
Norm is the result of any action by people that accumulates and concentrates the naturally occurring material to a point of concern
Oil and gas production generate lots of NORM when they bring up oil from underground
The change in pressure and chemistry tend to have Ra plate out in tank and pipes
Old oil drilling piping and storage tanks may have much NORM in them

## Slide 14
Terrestrial Radiation and Radioactivity
Some common singly-occurring radionuclides that were created during the formation of earth are the following:
  Radioactive potassium (K-40) is found in bananas, throughout the human body, and anywhere else stable potassium exists.
  Radioactive rubidium (Rb-87) is found in brazil nuts among other things.
Notes: <number>
Terrestrial radiation comes from the Earth itself. It depends on where you are in the world on how much radiation you will receive. Many minerals contain radioactive materials and if the rocks on which you live contain these minerals you will receive a higher dose due to terrestrial radiation that someone who lives on rock that dose not have these minerals in it. the radioactive material that gives the body the most dose from an internal source is K-40. This comes from all the K-40 that is in the foods we eat, including bananas.

## Slide 15: Consumer Products and Radioactive Material
There are more sources of radiation in the consumer product category than in any other.
    Television sets accelerate electrons to make the picture on the screen and in the process produce a few low energy x-rays.
  Smoke detectors contain a small radioactive source and an ionization chamber
  Welding rods, static eliminators in manufacturing, and luminous dials
Notes: <number>
Surprisingly the category of consumer products contains the largest number of examples of the use of radioactive materials. Many products either have radioactive material in them or are irradiated some time in their manufacturing process. Old TVs have an electron gun in the back of the set whereas smoke detectors have radioactive material in it. Products that have been irradiated in their making are band-aides, contact lens solution, spices, tires, teflon pans, and most surgical equipment.
The two most common units of activity are the Curie and the Becquerel. The Curie is named after Pierre Curie for his and his wife Marie’s discovery of radium. One Curie is equal to 3.7x1010 disintegrations per second. A newer unit of activity if the Becquerel named for Henry Becquerel who is credited with the discovery of radioactivity. One Becquerel is equal to one disintegration per second.
It is obvious that the Curie is a very large amount of activity and the Becquerel is a very small amount. To make discussion of common amounts of radioactivity more convenient, we often talk in terms of milli and microcurie or kilo and Megabecquerels.

## Slide 16: Consumer Products
Coleman lantern mantles (if you can find them)
Radium-painted watch and compass dials, instruments dials and markers
Irradiation of contact solution, surgical equipment, spices, tires, make up, teflon pans
Electron tubes, electrostatic eliminators, Exit signs

## Slide 17
Safer Consumer Products: Food Irradiation
Food Irradiation is a physical means of food treatment comparable to heat pasteurization, canning, or freezing.
It does not make the product radioactive
Food must be marked with the symbol at the right
Notes: <number>
Exposing prewrapped food to a very high dose of radiation can help preserve the food for a lot longer than it would be able to stay fresh by itself.
the main reason food goes bad is that the bacteria and fungus in or on the food grow and break the food down or cause it to go bad. When exposed to high radiation exposures all of these bacteria and fungus get killed and can no longer grow and spoil food. One can extent the time of when the food can be used by many times by irradiating it. Milk and other normally refrigerated item can be stored longer and even without refrigeration after being irradiated.

## Slide 18
Safer Consumer Products: Food Irradiation
The process involves exposing food, either packaged or in bulk, to one of three types of radiation: gamma rays, machine generated electrons, or X rays.
Food Irradiation promises to improve our ability to preserve food longer with better retention of the original qualities of the food, while at the same time reducing the incidence of food-borne diseases and infestation problems in bulk foods.
Notes: <number>
Exposing prewrapped food to a very high dose of radiation can help preserve the food for a lot longer than it would be able to stay fresh by itself.
the main reason food goes bad is that the bacteria and fungus in or on the food grow and break the food down or cause it to go bad. When exposed to high radiation exposures all of these bacteria and fungus get killed and can no longer grow and spoil food. One can extent the time of when the food can be used by many times by irradiating it. Milk and other normally refrigerated item can be stored longer and even without refrigeration after being irradiated.

## Slide 19: Strawberries
Notes: <number>
Strawberries and other fruits are irradiation and this delays them from going bad for a long time.
this picture is strawberries that are several weeks old.
<number>

## Slide 20: Sprouting
Notes: <number>
Irradiation of potatoes will prevent them from sprouting as fast. Irradiation of other foods can prolong the shelf life of the item.
<number>

## Slide 21
The Nuclear Fuel Cycle
The public is exposed to a variety of sources from the nuclear fuel cycle in air and water emissions, radioactive waste, and direct irradiation. However, the total collective doses from the nuclear fuel cycle are very small.
  <0.03% of the total average annual effective dose to the general population of the U.S. is from nuclear power (<1 millirem/year)
  That is considerably less than the total average annual effective dose of approximately 620 millirem/year due to all sources of radiation
Notes: <number>
The nuclear fuel cycle is in the news the most of the potential items than can expose the public but in direct opposition of what most people think it actually exposes the population the least.

## Slide 22
Components of the Nuclear Fuel Cycle
Mining of Uranium and Thorium
Milling of Uranium and Thorium
Enrichment and Nuclear Fuel Production
Nuclear Power Reactors
Fuel Reprocessing and By-Product Radioactive Waste
High-Level Waste Storage
Plutonium Recycling and Storage
Specific components of the Nuclear Fuel Cycle:
Notes: <number>
There are several steps in getting material from the ground to where it can be used to generate power. Since the US does not reprocess nor does it have a operating disposal site the exposes from these source of radiation are zero. Because of this the spent nuclear fuel must be kept onsite at each power plant that generates it or transported to a place that can store it for them.

## Slide 23: High Grade Ores
Contain a few percent of uranium (1-4%), in unusual cases, up to 10%
Typically in the form of uraninite (largely UO2), or pitchblende.
These ores are found primarily in central Africa (Zaire) and in Canada (Big Bear Lake).
Pitchblende Sample
Notes: <number>

## Slide 24: Medium Grade Ores
Contain 0.1 to 1.0% uranium
Found on the Colorado plateau region (Colorado, Utah, New Mexico and Arizona), also found in California, Nevada, Texas, and Washington
Found in Canada, Australia, and Czechoslovakia
Typically carnotite, thorianite, phosphates, and carbonates
Notes: <number>

## Slide 25
Medical Uses of Radioactive Material
Diagnostic purposes - Radionuclides can be used to provide an image of an internal structure in the human body, or they can allow doctors to visualize various stages in the function of an organ.
Radiation from X rays also fall into the diagnostic category.
Notes: <number>
Medical applications are one of the lesser known applications of radioactive materials. Many people know about X rays but there are many procedures that use radioactive material. Along with radioactive materials being used in the research of new drugs they are used for he diagnostic and treatment of many conditions , including cancer.

## Slide 26
Medical Uses of Radioactive Material
Therapeutic purposes - Radiation and radionuclides can be used to damage or destroy abnormal or diseased cells.
Therapeutic uses include treatment of cancer and other diseases with ionizing radiation.
Notes: <number>
Medical applications are one of the lesser known applications of radioactive materials. Many people know about X rays but there are many procedures that use radioactive material. Along with radioactive materials being used in the research of new drugs they are used for he diagnostic and treatment of many conditions , including cancer.

## Slide 27
Characteristics of Diagnostic Medical Uses
Radionuclides should have certain characteristics:
    short half-life
    cannot emit alpha or beta radiation
    must emit gammas with sufficient energy
    highest possible specific activity
Technetium-99m is used in more than 80% of the cases.
Notes: <number>
In the diagnostic procedure , a small amount of radioactive material is introduced into the body. This material is them measured to see if the material is going to either the correct place in the body or is being used correctly by the body. The amount of radioactive material that is measured is directly related to the activity of the body, either good or bad, and a diagnosis may be made from these tests

## Slide 28
Medical Uses: Diagnostic Purposes
Notes: <number>
Example of Brain Imaging for Diagnostic Purposes

## Slide 29
Characteristics of Therapeutic Medical Uses
Criteria for internally deposited radionuclides:
    the half-life should not cause an extended stay in the hospital
    radionuclide should emit particulate radiation (alphas or betas)
    radionuclide should also emit gamma rays to determine that the appropriate region has been targeted
Notes: <number>
The therapeutic nature of the use of radioactive material is that they use a larger amount of radioactive material to kill some or all of the cells in an organ or tumor. The material an be either injected, use external irradiation , or use seeds , which are inserted into the body in the location of interest. Each of these procedures will irradiation the location and destroy the cells in that area.

## Slide 30
Medical Uses: Therapeutic Purposes
Notes: <number>
Example of an Uteruses Insert for the Therapeutic Treatment of Cervical Cancer, Brachytherapy, the bright spots in the wires are radioactive sources.

## Slide 31
Machine Sources of Radiation
X-ray Generators: Consists of a x-ray tube, a source of high voltage, tube filament current, and radiation shielding to shape the beam
    Principle types of diagnostic X rays - radiographic, fluoroscopic, and photo-fluorographic
    Therapeutic X rays - superficial x ray for skin cancer, orthovoltage x ray generators for deeper lying tumors
    Industrial X rays - nondestructive examination of metal parts and tires
Notes: <number>
From ¼-1/3 of all people who enter a hospital undergo some sort of nuclear procedure.

## Slide 32
Machine Sources of Radiation
Nuclear Particle Accelerators: Objective is to produce a high energy stream of ions, directed along some path
    Linear accelerator or Linacs (industrial and medical uses)
    Cyclotron (also includes betatrons and synchrotrons)
    Van de Graaff accelerator
Notes: <number>
From ¼-1/3 of all people who enter a hospital undergo some sort of nuclear procedure.

## Slide 33
Fallout from Nuclear Explosions
The dose to the living organism from a nuclear explosion is due mostly to released fission products, with some contribution from unused fuel, neutron activation products, and nuclides produced by nuclear reactions.
<0.03% of the total average annual effective dose to the general population in the U.S. is from fallout from weapons testing (<1millirem/year).
Notes: <number>
A lot of the dust that is added to the atmosphere is either activated dirt particles or fission products directly from the bomb. This dust goes up and gets trapped in the stratosphere and slowly rains back down on Earth.

## Slide 34
Ionizing Radiation: Activities and Effects
Food Irradiation: 100,000 rad
Cancer Radiation Therapy: 6,000 rad
Lethal WB Dose to 50% of Population: 350 rad
Increase risk of cancer by 1% 12.5 rem
Maximum Annual Occupational Dose: 5 rem
Average Annual U.S. Population Dose: 620 mrem
Average Dose from Radon per year: 200 mrem
Annual Dose Limit for General Population: 100 mrem
Dose from a skull x-ray: 8 mrem
Dose from round-trip flight LA to NY: 2 mrem
Notes: <number>
Various activities have different doses associated with them.

## Slide 35: Sources of Radiation Exposure to the U.S. Population – 1990
Total Average Annual Dose = 360 mrem (3.6 mSv)
Notes: <number>
<number>

## Slide 36: A New Evaluation of Radiation Exposure of the U.S. Public Has Been Released by the NCRP

## Slide 37: 2006 Population Dose
Sources of exposure include:
  Natural radiation exposure
  Medical uses of radiation and radioactivity
  Consumer products
  Industrial uses
  Occupational exposure
Average effective dose to each individual is 620 mrem/y (6.2 mSv/y) – not quite double!

## Slide 38: What is the largest contributor to the radiation exposure of the U. S. Population?
Medical uses 48%
Radon 37%
Natural background 13%
Others 2%

## Slide 39: 2006 Population Exposure
Computed tomography 24%
Nuclear medicine 12%
Interventional medicine 7%
Radiographic/Fluoroscopic 5%
Radon 37%
Terrestrial 3%
Internal (ingestion) 5%
Space radiation (external) 5%
Consumer products 2%
Industrial <0.1%
Occupational <0.1%

## Slide 40: Questions